## Slide 1: Caught-in-Between Hazards
Notes: Congested worksites, heavy equipment and multiple trades can contribute to caught in between hazards.

## Slide 2: Learning Objectives
Understand hazards associated with;
  Excavation Collapses
  Working on Heavy Equipment
  Guarding of Tools and Equipment
Identify OSHA requirements related to Caught-in-Between hazards in construction.
Discuss how to manage Caught-in-Between issues on job sites

## Slide 3: Soil Mechanics
Soil weighs about 100 – 140 lb/cu.ft.
Each foot of depth adds more pressure side pressure.
Once the pressure exceeds the ability of the soil to support itself, failure is possible.
120
120
120
120
120
Notes: Unit Weight of Soils refers to the weight of one unit of a particular soil. The weight of soil varies with type and moisture content. One cubic foot of soil can weigh from 110 pounds to 140 pounds or more, and one cubic meter (35.3 cubic feet) of soil can weigh more than 3,000 pounds.

## Slide 4: Basic Requirements CFR 1926.650-654
Work must be supervised by a “Competent Person.”
Protection is required over 5 feet deep or if there is a possibility of a cave-in.
Excavations must be inspected daily and/or with changes.
Access/Egress is required over 4 feet deep and within 25 feet.
A rescue plan must be in place.

## Slide 5: Protective Systems
Sloping
Shoring
Shielding

## Slide 6: OSHA Measuring Slope
Notes: Appendix B to Subpart P - Sloping and Benching. Under section (c)(3)(ii) of this Appendix, whenever surcharge loads from stored material or equipment, operating equipment, or traffic are to be present, the competent person's determination of the degree to which the actual slope must be reduced below the maximum allowable slope shall have been based on the requirements set forth in (c) (3) (ii). The requirement to slope back in accordance with (c) (3) (ii) shall be triggered in situations where the surcharge loads cause signs of distress.

## Slide 7: Responsibilities of the Competent Person
Pre-inspect the job site
Determine soil condition and type
Determine protection systems
Assure proper access & egress
Monitor environmental conditions
Inspect & provide employee safety

## Slide 8: Slope Protection
Soil Testing MUST be done
Slopes must be established based on soil class
Notes: Soil A is not very common.

## Slide 9: Benching
Benching is allowed in Class A & B soils
Bench steps must be cut behind the required slope line.
Benching in Class A Soil
Benching in Class B Soil
Notes: Note benches must be outside of slope line.
Benches are effective in collecting small encumbrances that could break off.

## Slide 10: Benching
Another option is to bench the soil.
Benching can be very useful in cohesive soils.

## Slide 11: Trench Shields or Boxes
Typically engineered for Type C soils
Can be used with all classes of soils
Shields can be moved horizontally with workers inside
Worker must stay inside shields
Notes: Some light weight shields may not be engineered for Type C soild to full depth.
Trench shields are commonly used for pipe installation work.
When used properly, shields can be much safer, effective and cheaper than sloping methods.
A minimum of two shields should always be available to extend the work area or to help work through intersecting utilities.
Trench boxes must be at least 18" above the ground.

## Slide 12: Trench Shields
Shield in a Type B soil protecting only the bottom of the trench.
Shields must be installed within 24 inches of the bottom and must assure no loss of soil below the shield.
Full depth shielding
Notes: The top of the box can be level with the top of the excavation as long as there no fall object hazards.
Shields should be tight to the bottom in type C soil
The Trench Shield must be approved for the type of soil and depth.

## Slide 13: Trench Shields

## Slide 14: Engineered Hydraulic Shoring
Use manufacturer’s recommendations or OSHA table D.1 for spacing.

## Slide 15: Excavation Spoil Piles
Spoil piles must be at least two feet back from the edge.
This spoil pile is not back two feet.
2 FEET BACK

## Slide 16: Foundation Excavations
Excavations must be sloped to the proper soil class or shored.

## Slide 17: Engineered Sheet Pile Systems
Sheet piling are driven in usually before excavation begins.
They either act on their own in bending or are tied back into the soil.
Notes: All systems must be engineered and the engineering must be available.

## Slide 18: Engineered Shoring Systems
Caissons & timber lagging
Soil ties & mesh
Notes: All systems must be engineered and the engineering must be available.

## Slide 19: Access and Egress
Required in excavations over 4 feet deep.
Must be able to walk out without use of hands.
Provided with less than 25 feet of travel or every 50 feet.

## Slide 20: Excavation Accidents

## Slide 21: Causes of Crushing Fatalities
Caught between crane and carriage
Caught between equipment and …..
Notes: Crane booms that are not adequately supported when the pins are removed during dismantling can fall on the worker driving out the pins.
Rotating cabs, housings counterweights, buckets, etc. can strike victims or even trap victims against other obstacles.

## Slide 22: Equipment Maintenance
Always Lock and Block Equipment before working in it.
No exposed moving parts.
Nothing held up by hydraulics

## Slide 23: Catches and Pinches
Always watch the position of hands and feet around movable objects.

## Slide 24
A truck driver was working between the frame and dump box of a dump truck.
The dump box dropped suddenly, crushing his head.
Pinned Between Equipment

## Slide 25: NOT Good!!!
BETTER

## Slide 26: Maintenance Hazards
No workers under equipment that is not sufficiently supported
Notes: NEVER work under equipment supported only by jacks or their own hydraulics.
All equipment must be properly shut down, parking brakes set and be adequately blocked before maintenance workers can work around or under equipment.

## Slide 27: Preventing / Controlling / Abating Maintenance Hazards
Lockout equipment
Tag out the equipment (when Lockout is not possible)

## Slide 28: Support!!
Stay Bracket
Is this adequate ground support?
Notes: The photo in the top right corner of the slide demonstrates inadequate use of blocking for protection.

## Slide 29: Machine Guarding
Install and maintain all guards on tools and heavy equipment
Ensure blade guarding is in place and does not get removed. Too often blade guards are removed and never returned.
Notes: This equipment is not properly guarded.
Make sure all moving parts, gears, shafts, belts, etc. are properly guarded. This includes all wood working equipment such as table saws, miter saws, etc.

## Slide 30: Pulley Guards
Machine guard “should“ be designed to allow for easy, but safe lubrication and inspection

## Slide 31: Miter Saws
Guards must cover the blade and only retract as the blade cuts through material.
This guard is bolted open

## Slide 32: Grinders & Abrasive Saws
Guards must remain in place and eye protection must be worn
Best practice is to use face shields and hearing protection
Sleeveless shift worn by this employee affords no protection from abrasive/grinding debris
Notes: These are also struck by’s

## Slide 33: Good Protection
Notes: Also good protection from silica (*note respirators need to be worn and maintained properly).

## Slide 34: Incident Free
Planning
  Assess site conditions prior to excavation
  Site planning for equipment
  Make appropriate notifications
Training
  Excavation Safety
  Working around mobile equipment
Inspection
  Proper soil testing and trench inspection
  Equipment inspection – mirrors, back up alarms, etc.
  Inspection of tools, guards, etc.

## Slide 35: Incident Free
Oversight
  Check site conditions before excavations
  Assure operators of heavy equipment communicate
  Address the potential hazards and dangers to pedestrians when the activity has not been excluded from public use or access.
Lessons learned
  Understand the consequences of cave-ins
  Know the types of injuries that can occur from lack of guarding
Re-evaluate
  Excavations plans and programs yearly
  Equipment usage