## Slide 1: Susan Harwood Work Zone Safety
Heavy Equipment Safety Module 1

## Slide 2: Learning Objectives
Understand hazards associated with working on foot around heavy equipment.
Identify OSHA requirements related to the use of heavy equipment in construction.

## Slide 3
We have all kinds of Heavy Equipment

## Slide 6: Where are Workers Killed With Equipment?
Operator
35.1 %
Passenger
7.9%
Worker on foot
57.0%

## Slide 7: Environmental Hazards
Weather
    Heat
    Cold
    Precipitation
    Visibility
    Lightning
Noise
Dust
Chemicals
Sanitation
Notes: Photos courtesy Marko Kaar or RW Productions. Used with permission.

## Slide 8: Big Always Wins!!!

## Slide 9: Big Always Wins
4x4v. Mine truck.mpg

## Slide 10: Hazards
It may be difficult for equipment operators to see Workers On Foot (WOFs)
Work takes place in confined work areas, near large equipment, adjacent to traffic

## Slide 16: Striking Workers on Foot
Notes: Discuss how shadowing can hide workers.
Discuss need for high visibility clothing.

## Slide 17
Hazards to On-Foot Workers: Working Near Equipment
Workers in close proximity to equipment
Notes: This slide illustrates situations where workers must perform their work activities in close proximity to heavy equipment, which may be moving or stationary. Workers must be aware of potential hazards when working near heavy equipment. Loose clothing/jewelry may get stuck in the equipment, workers may get caught in the equipment if not paying full attention, or a slip/fall may result in a severe injury while working near to such heavy equipment. Thus caution must be exercised to prevent such incidents from occurring.

## Slide 18: Worker Fatalities in Roadway Work Zones

## Slide 19: Worker Fatalities in Roadway Work Zones
Over half of “workers on foot” killed were backing fatalities
52% of these involved dump trucks
Victim (under sheet) who was backed over by a dump truck

## Slide 20
Well-designed TCPs minimize hazards to WOFs and Operators

## Slide 21: Trucks Entering/Exiting the Work Zone

## Slide 22: Blind Areas: Getting struck or run over

## Slide 23: Blind Spots
Many machines have small blind spots, where large machines have large blind spots, both can cause serious injury or death!
The taller and wider the machine, the bigger the blind spot area.
All Involved must give Constant Attention to what they are Doing!

## Slide 24: Blind Spots

## Slide 25: Workers Are Vulnerable in Blind Spots
Notes: As a worker on foot, if you can’t see the driver and the driver can’t see you, you’re in a dangerous situation. Companies and projects should identify a specific side of the vehicle where a worker should walk for each operation. Consistency is important for safety.

## Slide 26: Blind Areas
Not Visible to Operator
Visible in mirrors only
Source: NIOSH
Front of truck is facing North 
Example: this mapping diagram shows the blind areas around a Ford F-800 dump truck.
*
*

## Slide 27: Be Familiar with Your Vehicle's Blind Spots
Notes: Each vehicle has its own, unique blind spots. Operators should be familiar with the blind spots surrounding each piece of equipment he or she operates and should be sensitive to the fact workers and other objects cannot be seen – even when using mirrors.

## Slide 28: Be Familiar with Your Vehicle's Blind Spots
Notes: Each vehicle has its own, unique blind spots. Operators should be familiar with the blind spots surrounding each piece of equipment he or she operates and should be sensitive to the fact workers and other objects cannot be seen – even when using mirrors.

## Slide 29: Blind Spots
Notes: Best Practice - Every piece of equipment should have a blind spot drawing from the cab.

## Slide 30
Slip form paver had blind spot to the rear exposing workers to a struck-by hazard from moving heavy equipment; mirror was added in order for operator to see
Source: National Photo Archive ID #1860

## Slide 31: Workers Must Be Visible
Workers must be visible with regards to their high visibility clothing. . .
Notes: Workers must be clearly visible to drivers and operators. High visibility garments are now required by both FHWA and OSHA for all workers, not just those exposed to motorists/on-road traffic. These agencies require workers to be dressed in a minimum ANSI Class II vest. The make-up of these vests is explained in a standard known as the ANSI/ISEA 107 "American National Standard for High-Visibility Apparel.“ The standard also recommends high visibility hard hats for workers to improve worker visibility.

## Slide 32: Workers Must Be Visible

## Slide 33: Know Your Surroundings
Notes: The operator needs to be fully aware of his or her surroundings. This includes objects at ground level, other vehicles and workers on foot. An important practice is to communicate site conditions and safety practices with truck drivers before they enter the work space, and then continuously during operations. Keep them informed about the site safety plan and changing conditions.

## Slide 34: Operators Must Confirm Before Workers Approach Equipment
Wait for a clear signal from the operator before approaching equipment.
Notes: It is difficult for workers to tell if the operator is looking at them or someone or something directly behind or in front of them. The worker may think the operator is looking at him or her and it is safe to approach when in fact the operator is focused on something else. Before approaching a vehicle, wait for a clear signal from the operator that you have permission to do so.

## Slide 35: Backing Equipment
Have audible back-up alarms
Have a spotter to direct the operator if visibility is restricted
Keep adequate clearance behind the vehicle
Always pay attention to backing equipment
Notes: 35
Too many people are killed by becoming complacent and not paying attention and blind spots.

## Slide 36: Poor Worker Position
This worker is out of the driver’s mirror view
Notes: backing truck video

## Slide 37: Walk Around Vehicle Before Backing
Notes: Before moving vehicles or equipment, the operator should walk around it to ensure no person or obstacle is in the blind areas. An alternative plan is for the operator to use a spotter.

## Slide 38: Always Check Behind Before Backing Up.

## Slide 39: Vehicle Backover Fatalities
Dump Truck | 67
Semi/Tractor Trailer | 40
Truck | 30
Forklift | 21
Garbage Truck | 20
Pick-up Truck | 16
OSHA Intergrated Management Information System data

## Slide 40: Back Up Alarms

## Slide 41: Back Up Alarms

## Slide 42: Back Up Alarms

## Slide 43: Back Up Alarms

## Slide 44: Back Up Alarms

## Slide 45: Camera Systems
Notes: There are a growing number of manufacturers of camera/video systems and pricing is getting more competitive.

## Slide 46: Sonar
Sonar Sensors
Notes: Sonar devices are not so common as cameras, but their use continues to grow.

## Slide 47: Radar
Radar Antenna
Notes: Like sonar, radar waves create a field that will detect an object when it enters the area and create an alarm to warn the operator. The challenge in working with radar or sonar alone is the system will alert the driver to any object in the monitored area, including cones, piles of dirty, shovels, etc. Because radar and sonar do not discriminate, the operator will receive false alarms, which can cause him or her to become complacent.

## Slide 48: Radar and Camera Used in Combination
Notes: Radar and sonar systems function best when coupled with camera technology. The radar or sonar sensing devices send an alarm when an object enters their sensor field. The alarm alerts the operator to look into his monitor to see the person or object in his blind spot so he can take appropriate action.

## Slide 49: Lidar
Signals sent to detect other tags.
Location identified by tag location
Notes: The RFID technology has two components: (1) a reader, which is a device used to communicate with the (2) tag.

## Slide 50: Tag – Identifies Worker Near-by
Communications Link
Audible sounds or vibration warn worker and
operator. Operator warned to look in monitor.
Notes: The reader has at least one antenna that emits radio waves and receives signals back from the tag. The tag is a microchip attached to an antenna that can be incorporated into a product, animal, person, etc. It contains a unique serial number and can be either a passive or an active tag.

## Slide 51: Working Too Close!
When equipment is working closely behind or along side, workers must pay special attention.
Operators must watch out for workers on the ground.
Workers on the ground need to watch out when equipment is working close.

## Slide 52
Source: National Photo Archive ID #3466
Highway construction worker needs to wear high visibility reflective clothing to help prevent struck-by hazard from moving heavy equipment

## Slide 53: Working near rotating/moving equipment
Debris
    Thrown
    Blown by wind
    Falling off passing vehicle
Equipment contact with power lines
Notes: Photos courtesy Marko Kaar or RW Productions. Used with permission.
Approximately 22% of all construction worker fatalities involve being struck by something.
For 1992 to 2000, 91% of the 910 worker deaths in work zones involved vehicles, mostly dump trucks.
NIOSH records indicate that in 2005, 390 workers were killed in struck-by incidents, accounting for 7% of all occupational fatalities.
Injuries range from contusions and lacerations to fractures, crushing, and fatalities.
Current estimations are that approximately half the workers killed in highway work zones are killed by construction vehicles. These accidents usually involve crushing.

## Slide 54: Skid Steers
Extremely agile and quick.
Poor visibility from cabs
Prone to tip-over
Workers don’t respect working areas.
Notes: Photos courtesy Marko Kaar or RW Productions. Used with permission.
Even when we plan, events may happen unexpectedly.
For example, workers dumped scrap into a construction dumpster using a Lull. The debris struck a steel bar, which acted as a lever, propelling a 35-pound piece of metal lying on the other end out of the dumpster and 15 feet through the air, striking a worker in the right front of his head – thankfully on his hard hat.
The worker was dazed and sustained a small laceration on his forehead from the force of the blow on his hard hat. He walked away, visited a doctor to be checked out, and was home with his family that night.
Discuss similar accidents that may have occurred within your company.

## Slide 55
Notes: Bobcat185tricks video

## Slide 57: Potential struck-by equipment
Equipment too close.
Workers by moving wheels

## Slide 58: Broken Glass Creates Visibility Issues

## Slide 59: Proper Seats
Everyone must be in a proper seat with a seat belt .
No riding on steps or running boards!
Notes: Susan Harwood Training Grant Program (2006) Focus Four Hazards in the Construction Industry
59
All employees riding in or on equipment must be properly restrained, using proper seats and seatbelts.
This applies to ALL equipment, including (but not limited to) off road vehicles, grading equipment, and onsite transport such as golf carts.

## Slide 60
No Riders!!
Notes: Rider on loader steps video

## Slide 61: All Riders Must be in Proper Seats

## Slide 62: Fall Hazards
Notes: Susan Harwood Training Grant Program (2006) Focus Four Hazards in the Construction Industry
62

## Slide 63: Good Organization of Equipment Flow?

## Slide 64: Equipment Does Roll Over!

## Slide 65
A dozer slid off the side of a subgrade.
It tipped over on its side, pinning the operator underneath.
OSHA Fatal Fact 19
Equipment Rollover

## Slide 66: Maintain Roll-over Protection
Only remove the ROP’s per safety plan
Notes: Sometimes the Rop’s needs to be folded down due to low clearances. Rop’s must be reset immediately after low clearance work.

## Slide 67: Wear Your Seat Belt!
When there is a roll-over hazard, there must be ROP’s and a seat belt
Always wear the seat belt
Only ride in the seat provided
Notes: 67

## Slide 68
A dozer began to slide off a trailer.
The operator jumped from the cab.
The rollover cage fell on top of him, crushing him.
OSHA Fatal Fact 38
Equipment Loading

## Slide 69: Loading Equipment
Trailer secure and on a level surface
Inspect the deck for debris, blocking or chains
Have a spotter help properly align the equipment up the ramps
Be sure equipment is properly secured
Notes: 69
Many tip-over accidents occur during the loading or unloading of equipment.
Equipment can also slide off trailers or loading ramps.
Only people involved in the loading or unloading should be engaged.

## Slide 70: Rotating Equipment

## Slide 71: Swinging & Caught In Hazards
Protect swing radiuses of backhoes, etc.
Always stay well clear of swinging machines like backhoes.
Watch pinch points on articulated equipment such as rollers or front end loaders.

## Slide 72
An employee was caught by a piece of equipment that was swinging .
Caught By Swing Equipment

## Slide 73
Avoid struck-by hazards by not working within the swing radius of heavy equipment

## Slide 74: Operators Must Confirm Before Workers Approach Equipment
Wait for a clear signal from the operator before approaching equipment.
Notes: It is difficult for workers to tell if the operator is looking at them or someone or something directly behind or in front of them. The worker may think the operator is looking at him or her and it is safe to approach when in fact the operator is focused on something else. Before approaching a vehicle, wait for a clear signal from the operator that you have permission to do so.

## Slide 75: Dumping Trucks
Stay clear of dump trucks while they are dumping.
Trucks can become unstable with the boxes raised.
Watch for spillage out of the end gates.
If an end gate chain breaks, you could be covered in material.

## Slide 76: Truck Boss
PRIMARY ROLE: COMMUNICATE WITH DRIVERS
  Step away while dumping.
Notes: The truck boss needs to be informed about the daily plan as well as the initial planning of the site. He will provide vital information affecting operation safety that should be considered in the planning process. In the training process those involved need to recognize the primary purpose of the truck drivers: to deliver material. They want to do this as efficiently as possible so they can return with another load. Their focus is aligned with the ticket taker on site, and the dump man once the truck is in the queue.

## Slide 77: Poorly Maintained Equipment
Make sure all equipment is in proper working order.
Inspect all equipment before use.
Assure all warning signals work.
Always assure that guards are in place or have an adequate lockout procedure to assure that you cannot get caught in moving parts.

## Slide 78: Broken Glass Creates Visibility Issues

## Slide 79: Tire Pressure
Always check tire pressure.
Uneven pressure can result in a tip over

## Slide 80: Check Steps

## Slide 81
A mechanic was adjusting brakes under a backhoe.
The operator put the backhoe in gear.
The hood of the mechanic’s rain jacket wrapped around the drive shaft.
His neck was broken.
OSHA Fatal Fact 34
Caught in Equipment

## Slide 82: Catches and Pinches
This employee put his hand in a piece of equipment.
The finger had to be amputated.

## Slide 83
A truck driver was working between the frame and dump box of a dump truck.
The dump box dropped suddenly, crushing his head.
Pinned Between Equipment

## Slide 84: NOT Good!!!
BETTER

## Slide 85: Improper Blocking
The victim was replacing tires on the front-end loader. He was pinned under the loader when it fell off the supporting jacks.

## Slide 86: Support!!

## Slide 87: Maintenance Hazards
No workers under equipment that is not sufficiently supported
Notes: NEVER work under equipment supported only by jacks or their own hydraulics.
All equipment must be properly shut down, parking brakes set and be adequately blocked before maintenance workers can work around or under equipment.

## Slide 88: Support!!

## Slide 89: Tag Out Equipment

## Slide 90: Proper Equipment Securement

## Slide 91: Heavy Tie-Down
Notes: All equipment must be properly secured

## Slide 93: Check the Height!!!

## Slide 94
Watch Power Lines

## Slide 95: OPPS!

## Slide 96
This truck got into a high voltage line.
The truck driver panicked and jumped. Luckily the driver made it.
Later on, somebody tried to jump back on the truck just to lower the bed, made contact with the ground and the truck at the same time, and was killed.
Notes: This truck got into a high voltage line. The truck driver panicked and jumped. Luckily the driver made it, but later on, somebody tried to jump back on the truck just to lower the bed, made contact with the ground and the truck at the same time, and was killed.

## Slide 97: Overhead Power Lines
Always watch for overhead power lines.
Dump trucks, hoe arms, loader buckets etc. can snag lines creating an electrical contact.
We must maintain at least a 10 foot clearance from all overhead wires less than 50 kV.
Over 50 kV, we must add .4 inches of clearance for every kV.
If you don’t, they can kill you.

## Slide 98: The Ground May Be Hot!
Electricity dissipates with the resistance of the ground
As potential drops, fields develop around the electrified machine
If you step across a line of unequal potential, you could be electrocuted
Notes: Discuss the process of voltage dissipation by the resistance of the ground. Energy fields can be set up around the grounded object. If a person steps across two different levels of voltage or touches an object at a different level, electricity may pass through the body.

## Slide 99: If Contact Occurs
Stay on the machine if possible
Warn all others to stay away
Notify power company immediately
Attempt to move away but assure line is not “connected”
Notes: Power distribution systems many times have storm trip circuits on them.
These are relays that will trip out for a period of time (Usually 3-30 seconds) to allow a faulted object such as a tree branch to fall away.
These relays will than reset and the line will be re-energized.
This may occur 2-3 times before a breaker actually trips and the power remains out until it is manually reset.

## Slide 100: Bail Out Procedures
If you must get out, jump with your feet together
Do not touch the machine
Hop or shuffle out of the area

## Slide 101
I chose to look the other way…

## Slide 102
I could have saved a life that day,
But I chose to look the other way.
It wasn't that I didn't care,
I had the time, and I was there.
But I didn't want to seem a fool,
Or argue over a safety rule.

## Slide 103
I knew he'd done the job before,
If I called it wrong, he might get sore.
The chances didn't seem that bad,
I've done the same, he knew I had.
So I shook my head and walked on by,
He knew the risks as well as I.
He took a chance, I closed an eye,
And with that act I let him die.

## Slide 104
I could have saved a life that day,
But I chose to look the other way.
Now every time I see his wife,
I'll know I should have saved his life.
That guilt is something I must bear,
But it isn't something you need to share.

## Slide 105
If you see a risk that others take,
That puts their health or life at stake,
The question asked, or the thing you say,
Could help them live another day.
If you see a risk and walk away,
Then hope you never have to say,
I could have saved a life that day,
But I chose to look the other way.

## Slide 106: Author: Don Merrell

## Slide 107: Remember: ”It is better to be careful a 100 times than to get killed once.” Mark Twain

## Slide 108: Questions?