## Slide 1: Susan Harwood Work Zone Safety
Work Zones and Traffic Control
Module 2

## Slide 2: Learning Objectives
Understand hazards faced by workers in work zones.
Understand the requirements for high visibility clothing.
Understand how to properly set up a work zone.
Identify OSHA requirements related to traffic control signs and devices.

## Slide 3: What does WZ Safety mean to the public?

## Slide 5: What does WZ safety mean to the contractor?

## Slide 6: What Makes Work Zones Different?
Working Near and Affecting Public

## Slide 7: Work Zones Are Different
Worker Safety Is Impacted by Motorist Behavior
Reading a Book on the Interstate

## Slide 8: Distractions

## Slide 9
Parking Hazards
Parked car too close to heavy equipment in operation
Incident involving parked car and loader
Notes: This illustrates how problems may arise due to undesignated parking areas for workers personal vehicles. In the planning stages, areas for parking should be identified and all workers should be instructed to use only those areas to park. Undesignated parking may create unnecessary conflicts within the work areas.

## Slide 10: Work Zone Intrusions
  Limited physical barriers
  Lack of knowledge/ experience
  Working behind non- positive barriers
Notes: Photos courtesy Marko Kaar or RW Productions. Used with permission.
Approximately 22% of all construction worker fatalities involve being struck by something.
For 1992 to 2000, 91% of the 910 worker deaths in work zones involved vehicles, mostly dump trucks.
NIOSH records indicate that in 2005, 390 workers were killed in struck-by incidents, accounting for 7% of all occupational fatalities.
Injuries range from contusions and lacerations to fractures, crushing, and fatalities.
Current estimations are that approximately half the workers killed in highway work zones are killed by construction vehicles. These accidents usually involve crushing.

## Slide 16: Factors that Affect Drivers’ Ability
  The road itself
  Alcohol and drugs
  Driver’s age
  Driver’s experience
  Weather
Never assume a driver sees you!
Notes: When a flagger assumes he/she is being seeing by a driver, that is the day the flagger will get hurt. If anything, assume that the driver has not seen you!! They may be under the influence, or asleep, or preoccupied, or even suicidal. The road may be slippery. The sun may reduce visibility. All these factors will affect drivers’ ability to control a vehicle.

## Slide 17: Variation in Ability
AGE
  Young Drivers
  Elderly Drivers
EXPERIENCE
  Ability levels vary
PHYSICAL STATE
  Eyesight
  Reaction time
MENTAL STATE
Notes: Ford Motor Company conducted a survey on how people ranked
themselves as drivers and came up with a remarkable
statistics “Nine out of ten drivers are better than average”.

## Slide 18: Driver Age and Experience
Older drivers have poorer vision and reduced reaction time.
  In most cases, nighttime vision decreases with age
  Problems increase when signs are not well maintained, Channelizing devices are not properly placed, and there are abrupt changes in the levels of lighting
  Vision problems increase in poor weather conditions
  Population is growing older

## Slide 19: Eyesight and Age
Notes: A U of MI study states each 13 years after the age of 20 the average person requires 2X
the amount of light to see the same thing a 20 year old sees. 33 2X, 46 4X, 59 8X.

## Slide 20: The amount of light a motorist requires to see during nighttime doubles every 13 years

## Slide 21: Driver Age and Experience
New drivers lack experience
  Little experience recognizing work zone warnings
  May become nervous when operating their vehicle in narrower lanes or adjacent to concrete barriers, barrels or cones
  May over correct or react in an unpredictable way
  May be unappreciative of the dangers found in work zones, and fail to reduce speeds or avoid distractions

## Slide 22: Confusing Choices?

## Slide 23
Unsafe Condition
Notes: Is this road really closed or is the lane closed to traffic?
Appropriate signage is a step toward Covering Your organization’s Assets!

## Slide 24
Unsafe Condition
Notes: The Paddle is inside the hazard
No tapper area

## Slide 25: Inadequate Signing

## Slide 26
This attenuator truck was rear ended at 63 mph by an inattentive driver, despite workers’ attempts to get the driver’s attention.
Roadway Workers Are At Risk
Drunk drivers
Sleepy or impaired drivers
Impatient, reckless drivers
Drivers using cell phones; other inattentive drivers
Lost drivers looking for directions

## Slide 27
Truck may be traveling at a high speed
Worker is in traffic lane
Hazard to On-Foot Workers:
Too Close to Traffic Lane
Notes: This slide illustrates a situation where a worker is partially located in the traffic lane, in a kneeling position that does not allow him to respond quickly in an emergency situation. Additionally, the worker does not seem to be aware that a large truck is approaching most likely at a high speed, which puts him at very high risk. The truck already appears to be traveling on the shoulder to avoid hitting the worker. This example demonstrates a very high risk situation.

## Slide 28: Hazard to On-Foot Workers: Type of Barrier
No Rigid barriers to separate workers from passing traffic

## Slide 29
Hazards (Poor Visibility)
Hard to see a worker in the shadow of a truck
Lack of high visibility apparel/vest
Notes: This illustrates hazards related to visibility issues within a work zone. The top photograph demonstrates that workers may not be visible when working in the shadow of a truck, even during the day time. If workers cannot be seen by the truck drivers, they may be at risk of being struck. A high visibility vest would improve the visibility of this worker. Additionally, the worker should stay in communication with the vehicle operators to further ensure his safety.
The bottom photograph shows night work being conducted, where a group of workers are wearing reflectorized safety vests and are clearly visible to the oncoming trucks. However, one of the workers is not wearing high visibility clothing and may not be visible. Additionally, the workers at this job site are not wearing hard hats, which is not a safe practice.

## Slide 30: Common Issues
Uneven surfaces
Heavy traffic exposure
Moving equipment
Power lines
Labor intensive
Notes: Photos courtesy Marko Kaar or RW Productions. Used with permission.
Approximately 80% of construction worker fatalities involve a fall, being struck by something, being caught in or between things, or electrical shock.
In addition, soft tissue injuries (STI's), usually seen as strains or sprains, are one of the most frequent injury types in this work. STI's are rarely fatal but can, and do, have a serious impact on the injured workers’ and families' quality of life. Asphalt is heavy, so strains and sprains are frequent.
In asphalt paving work, we frequently find workers within feet, even inches, of vehicles weighing tons traveling at a high rate of speed. The responsible crew must have an emergency plan to address challenges resulting from injuries.
Burns may result from being struck by hot asphalt.

## Slide 31: Following Traffic
Remember, you may be “following traffic” where laborers are not paying close attention.

## Slide 32: Most Worker Fatal Collisions Result from Construction Equipment
State DOTs, contractors, workers, etc., are under increasing pressure to conduct work in a way that has minimal impact on traffic
This pressure results in more night work, compressed construction schedules, and smaller work areas

## Slide 33: Most Worker Fatal Collisions Result from Construction Equipment
The combination of workers on foot (WOF), operation of large pieces of equipment, and passing of supply vehicles in and out of a confined work area, creates significant hazards, especially for WOFs

## Slide 34: How are Roadway Construction Workers Killed?

## Slide 35: Equipment and Construction Vehicle Traffic Within Work Zone
Equipment/employee moves into oncoming traffic
Loading and unloading of equipment
Notes: Photos courtesy Marko Kaar or RW Productions. Used with permission.
Approximately 22% of all construction worker fatalities involve being struck by something.
For 1992 to 2000, 91% of the 910 worker deaths in work zones involved vehicles, mostly dump trucks.
NIOSH records indicate that in 2005, 390 workers were killed in struck-by incidents, accounting for 7% of all occupational fatalities.
Injuries range from contusions and lacerations to fractures, crushing, and fatalities.
Current estimations are that approximately half the workers killed in highway work zones are killed by construction vehicles. These accidents usually involve crushing.

## Slide 36: Mobile Workzones Common Issues
Traffic exposure
Limited notice
Multiple vehicles
High priority/speed of completion
Heavier manpower requirements
Notes: Photos courtesy Marko Kaar or RW Productions. Used with permission.
Approximately 80% of construction worker fatalities involve a fall, being struck by something, being caught in or between things, or electrical shock.
In addition, soft tissue injuries (STI's), usually seen as strains or sprains, are one of the most frequent injury types in this work. STI's are rarely fatal but can, and do, have a serious impact on the injured workers’ and families' quality of life. Concrete is heavy, so strains and sprains are frequent.
In mobile or short-term work, we frequently find workers within feet, even inches, of vehicles weighing tons traveling at a high rate of speed. The responsible crew must have an emergency plan to address challenges resulting from injuries.
Resurfacing includes grinding/milling the old surface, disposing of it, then placing a new surface.
Fractures, contusions, crushing, foreign objects in the eye, and strains and sprains are common.

## Slide 38: Building Sites

## Slide 40
Truck backing into site

## Slide 41: Managing Equipment On The Street

## Slide 42: Excavation Affecting Traffic
Proper barricades and signage needed

## Slide 43: Equipment Work In The Street
Traffic control needed.

## Slide 44: Loads Over Traffic
Loads should never fly over traffic.
Traffic control required.

## Slide 45: Material Deliveries
If a lane will be blocked, proper signage and traffic control is required

## Slide 46: Construction Entrances

## Slide 48: Two Federal Agencies Have Interests in Work Zone Safety

## Slide 49: 1926.200(g)
Traffic signs.
Construction areas shall be posted with legible traffic signs at points of hazard.

## Slide 50: 1926.200(g)(2)
All traffic control signs or devices used for protection of construction workers shall conform to Part VI of the Manual of Uniform Traffic Control Devices (AMUTCD"), 1988 Edition, Revision 3, September 3, 1993, FHWA-SA-94-027 or Part VI of the Manual on Uniform Traffic Control Devices, Millennium Edition, December 2000, FHWA, which are incorporated by reference.

## Slide 51: What is the MUTCD?
The Manual on Uniform Traffic Control Devices (MUTCD) was developed to create standardized control during roadway construction, maintenance, and utility (work zone) operations.

## Slide 52: Work Zones Must be Established
Any time construction activities will affect traffic on a public right-of-way, street or highway Including:
    Blocking lanes or restricting
    Working near traffic lanes
    Traffic entering/or leaving sites that affect traffic
Work or Loads occur over traffic

## Slide 54
Plan Based on MUTCD (or State/Local) Practices
Traffic Control Plan helps move motorist traffic safely through or around roadway work zones to protect the public and workers.
Traffic Control Plans

## Slide 56: Internal Traffic Control - Overview
An effective ITC protocol informs all parties operating within the work space about the location of others.
ITC creates “zones” designed to minimize interaction between workers on foot and construction vehicles.
Notes: In simple terms, ITCPs are a protocol to inform all parties operating within the work space about the location of others. ITCPs create “zones” designed to minimize interaction between workers on foot and construction vehicles by designating routes and operating procedures for large trucks delivering materials inside the “cone zone.”

## Slide 57: Collisions within the work zone involving construction trucks and/or equipment

## Slide 58: Internal Traffic Control Pans
Recommended on all sites where heavy equipment operates.

## Slide 59
TCP’s should include safe procedures for parking unused equipment and employee vehicles.

## Slide 60: Keep Material & Equipment Back
NOT GOOD!
BETTER

## Slide 61: Work Zone Set-Up
A dangerous time.
  Full awareness of traffic
Set the zone with traffic.
  Start with signage
  Then tapering
  Than separation devices
Tear the zone down against traffic
  Signage last

## Slide 62: Not Good!

## Slide 63: Work Zone Components
Notes: Illustration by Marko Kaar.
Planning is always the basis for success.
Pre-planning begins when the bid is assembled. At that point, major risk control issues should be identified. They should include the need for MOT and any special skills the workers might need that require specialized training, such as “'Work Zone Awareness” or “Confined Space Entrant.” Identify what pieces of equipment will be required and how many operators are needed for each. Do your workers have the proper certifications and authorizations for the equipment?
Like doing a material take-off, the estimate should be reviewed and identified safety issues placed on paper.
Every worker's education should include the idea that they ask themselves, "How can I do this without injury or accident?" before starting any task. Learning to trust their own answers will help them prevent accidents and injuries to themselves.

## Slide 64: Advance Warning
Lets the public know that you are there
Install BEFORE you start work
Notes: Without advance warning the drivers do not expect the driver to be there. Never flag without advance warning signs in place.

## Slide 65: Example of Typical Warning Signs
Get drivers’ attention
    “ROAD WORK AHEAD
    “UTILITY WORK AHEAD”
    FLAGGER AHEAD
Tell them the problem
    “ONE LANE ROAD AHEAD”
    Tell them what to do
    “BE PREPARED TO STOP”
Notes: Typically, warning drivers takes a three-step process to be effective. If you only say FLAGGER AHEAD, drivers may not merge since the do not know why!

## Slide 66
Traffic Control Devices
Changeable Message Boards
Note Wrong Direction of Chevrons
Concrete Barriers

## Slide 67
Not Good!

## Slide 68: Sign Maintenance
Inspect Regularly
Keep Clean,
Replace as Needed

## Slide 69: Poor Signs and Maintenance
Dirty T/C Devices
Homemade Sign
Advance Warning

## Slide 70
Traffic Control Devices
Truck Mounted Attenuators
Notes: Rated for type of road/speed
Gross Vehicle Weight
70

## Slide 71: Poor Control Device Set-up’s
Cones Down
Chevrons in Wrong Direction
Traffic

## Slide 72: Hazard - Working Close to Traffic
Roadway work space close to traffic
Worker shifting the offset drums inside.

## Slide 73: Unsafe Practices
Loader with loaded material and moving traffic together
Workers in active traffic lanes

## Slide 74
Loading Trucks too close to moving traffic
Counterweight swing into traffic
Unsafe Practices

## Slide 75
Questionable physical separation between through traffic and heavy equipment – space for swing radius of the equipment is a problem

## Slide 76
Worker should not be talking on his cell phone near the roadway.
Note: No HV
Unsafe Practices

## Slide 77
Protect Drop-off’s

## Slide 78
Pedestrian in the work zone? Pedestrian crossing locations should be provided where necessary.

## Slide 79
Continuous physical separation between traffic and equipment provided where necessary

## Slide 80: Hi-Viz Clothing
Highly visible vest with a contrasting color
Hard hat
  Required in some states
Retro-reflective for nighttime flagging
Notes: Garments should include a highly visible vest. A hard hat may be required in your State, but even if it isn’t, it is a good idea. For nighttime flagging, garments shall be retroreflectorized. Retroreflective garments return the light back to the source.

## Slide 81: Class II Clothing
  Acceptable in many states for daytime operations
Notes: Photos courtesy Marko Kaar or RW Productions. Used with permission.
“See and Be Seen” starts here. It is very important that flag person training very strongly emphasize one of the most valuable characteristics of effective flag persons: that of acquiring mutual eye contact with approaching drivers and BOLDLY commanding/communicating the desired travel path or action for drivers.
High-visibility clothing is appropriate for all work zone environments.
Recommended support materials:
http://www.workzonesafety.org/
http://www.cdc.gov/niosh/topics/highwayworkzones/
This web site offers a possible alternative to having live flag persons performing this work activity. www.noflag persons.com

## Slide 82: Class III Clothing
  Highest level of visibility
  Wide range of weather conditions
  Required for nightime work.
  Required in some states for daytime.
  Recommended for all flaggers
Notes: Photos courtesy Marko Kaar or RW Productions. Used with permission.
“See and Be Seen” starts here. It is very important that flag person training very strongly emphasize one of the most valuable characteristics of effective flag persons: that of acquiring mutual eye contact with approaching drivers and BOLDLY commanding/communicating the desired travel path or action for drivers.
High-visibility clothing is appropriate for all work zone environments.
Recommended support materials:
http://www.workzonesafety.org/
http://www.cdc.gov/niosh/topics/highwayworkzones/
This web site offers a possible alternative to having live flag persons performing this work activity. www.noflag persons.com

## Slide 84: Dangers of Shift Work
  Work related injuries increase 15.2% for swing shift
  Work related injuries increase 27.9% for night shift
  Injury numbers are compared to day- shift operations
  Employees are 36% more likely to be injured on their fourth consecutive night shift.
Notes: Picture is of a 222 crane that tipped over in Albuquerque in 2002. Loaded onto a trailer with 180’ of boom, with leads and pile hammer attached. Truck driver adjusted the load and the whole thing went over. Accident happened at 11:30 p.m. and the free way had to be open by 5 a.m.
Review statistics.

## Slide 85: Night Work
Visibility is a factor
Fatigue of workers is an issue
Notes: Photos courtesy Marko Kaar or RW Productions. Used with permission.

## Slide 86: Night Work
Poor visibility for motorists
Poor visibility for workers
Communication between shifts
Impaired or drowsy drivers
Glare issues

## Slide 87
Lighting Devices

## Slide 88: Night Work Physical Disruptions
Sleep disruption
Risk of injury from drowsiness
Social issues from altered schedule

## Slide 90: Working at Night
Wear high visibility apparel – Class III
Have good work area lighting
Be aware of your surroundings at all times

## Slide 91
It’s not about the rules. It’s about people’s lives!!

## Slide 92: DO IT RIGHT!!