## Slide 1: Susan Harwood 2016 Work Zone Safety
Traffic Flagging
Module 3

## Slide 2: Learning Objectives
Understand hazards faced by flaggers in work zones.
Understand the responsibilities of flaggers.
Understand proper flagging techniques.
Identify OSHA requirements related to flagger safety.

## Slide 3: 1926.200(i)
Signaling by flaggers and the use of flaggers, including warning garments worn by flaggers shall conform to Part VI of the Manual on Uniform Traffic Control Devices, (1988 Edition, Revision 3 or the Millennium Edition), which are incorporated by reference in §1926.200(g)(2).

## Slide 4: Traffic Flagging
Flaggers are critical to traffic safety
Consequences of improper flagging may be severe
Flaggers have important responsibilities
Notes: Flaggers and flagging operations are critical to safety. It is imperative to follow proper procedures and to use properly trained flaggers. Otherwise, crashes may occur.

## Slide 5: Controlling Drivers is Difficult
They want to make their own decisions
They like to be in control
They have expectations
Work zones are more prone to accidents
Flaggers are in their way!
Notes: However, drivers do not want to be controlled. They are in their own world. They also see work zones as inconveniences, so flagging is not easy.

## Slide 6: Responsibilities of a Flagger
His/her own safety
Safety of other workers
Safety of the driving public
Flaggers need to know how to do their job right!!
Notes: Flagging is a selfish profession since flaggers always protect themselves first. They also protect workers and the driving public. Improper flagging procedures will lead to crashes.

## Slide 7: When Are Flaggers Necessary?
Construction Vehicles & Equipment in Uncontrolled Traffic Lanes
Two-way Traffic Can Pass in Only One Direction
Pathway Through the Construction Is Too Confusing for Motorists
Mobile Work Zone

## Slide 8: Improper Flagging Techniques
In traffic with no display
Flagger is sitting while working
Unprofessional Flagger
Notes: This illustration demonstrates various improper flagging techniques including: (1) flagger not holding the sign so that the message can be read by the motorists (sign turned to the side) and is also standing unnecessarily in the travel lanes, as shown in the upper left photograph, (2) flagger is directing traffic improperly by sitting in the back of a pick-up truck, as shown in the upper right photograph, and (3) flagger has his back toward traffic, as shown in the bottom center photograph. Additionally, in all of the photographs, the flaggers are not wearing hard hats.

## Slide 9
Truck backing into site

## Slide 10: The ABCs of Flagging
“A” for Advance Warning
“B” for be visible and alert
“C” for Control
These are essential aspects of any flagging operation!!
Notes: The ABCs of flagging are critical:
-Always have advance warning signs
Flaggers should be well visible and alert at all times
They should be in control. They are a legal traffic control device! Command respect!

## Slide 11
Minimum Signs Recommended in the Manual on Uniform Traffic Control Devices (MUTCD)

## Slide 12: Advance Warning Sign Spacing
Low speeds (40 mph or less)
  100-350’ apart
Higher speeds/rural
  500’ or more
Notes: The spacing and location of signs depends on the type of road, whether urban or rural. Urban roads usually have significant pedestrian traffic, slower speeds than rural roads, and curb and gutter. Rural road speeds tend to be faster, with little pedestrian traffic and few intersections. In rural areas, the suggested spacing for warning signs is 500 feet, for example.

## Slide 13: Taper
Needed for lane closures
Typically 50-100’ (MAX.) for two-lane flagging operations
6 devices (cones) 20’ apart
Taper
Notes: A taper is a transition needed when lanes are closed. Short tapers encourage drivers to slow down. So short tapers, not to exceed 100 feet, are recommended for two-lane roads where the remaining open lane is controlled by flaggers.

## Slide 14: Buffer Space
Creates empty space between the flagger and the work space
Length is related to approach speed and road conditions
ALWAYS EMPTY
Buffer
Notes: Buffer spaces are empty areas between the taper and the actual work space. This allows drivers to recover should they drive through the taper. The faster the speed, the longer the buffer space.

## Slide 15: STOP/SLOW Paddle
Retro-reflectorized for night use
At least 24” x 24”
  Larger for added visibility
5’ – 7’ high
Rigid handle
Good condition
Notes: A 24” x 24” paddle is the smallest allowed and should be used for low-speed operations. Larger paddles are better. They are meant to be attended so they don’t have feet. Never place a paddle in a cone or leave it unattended.

## Slide 16: Follow Standard and Uniform Flagging Procedures
Increases motorists’ respect
Promotes uniform response
Minimizes drivers’ confusion
Flagger ahead??
Notes: The key to effective flagging is to follow proper procedures in order to gain the motorists’ respect and promote uniform responses. Improper procedures lead to crashes.

## Slide 17: Flaggers Must Basics
Stay alert at all times
Face oncoming traffic
Be highly visible
  Stand alone
Stay on the shoulder
  Out of the path of vehicles
Notes: The preferred flagger position is out of the path of moving vehicles. Typically that is the shoulder, on a visible location and facing oncoming traffic.

## Slide 18: Flagger Hazards
Paddle Placed in Cone; Flagger in Shadow
Flagger Not Facing Oncoming Traffic
Confusing Signal

## Slide 19: Is Flagger training needed?
Notes: Flagging training is obviously needed! How many things are wrong with this picture? Can a flagger be seated? Can he listen to the radio? Of have his car nearby? Or use an orange flag? This flagger is not trained!

## Slide 20: Problem?
Notes: This flagger needs better high visibility and also should have at least a flag for this incidental flagging. A STOP/SLOW paddle would be better. The flagger should not stand in the traffic lane.

## Slide 21: Problem?
Notes: The flagger should not stand in the traffic lane. The flagger should ALWAYS face traffic. A STOP/SLOW paddle should be used.

## Slide 22: Problem?
Notes: The flagger should not stand in the traffic lane. The flagger should be on the shoulder.

## Slide 23: Problem?
Notes: Even a Police Officer must have a Flag or STOP/SLOW paddle when working as a construction flagger.

## Slide 24
Position?
On Shoulder WITH an escape route.
Never have car next to flagger station.
Notes: The flagger must have a clear escaper route. Vehicles can block that escape.

## Slide 25: Escape?
Notes: The flagger must have a clear escaper route. Guardrails block that escape.

## Slide 26: Watch for Glare

## Slide 27: Flaggers Must Be Visible
Workers must be visible in a variety of conditions, especially during night work.
Notes: During night time hours, inclement weather and other low-light conditions, ANSI/ISEA Class III garments are highly recommended.

## Slide 28: Night Flagging
Flagger must be well lit.

## Slide 29: Flagger
Never in a Curve!

## Slide 30: No Good!!
Notes: The Stop/Slow paddle is not squarely facing the oncoming traffic. Additionally, the flagger appears to be distracted by a hand-held device.

## Slide 31: Typical Two-Flagger Operation
Notice:
  No arrow boards
  Flagger at the beginning of a taper
  Short taper
    50’ to 100’ MAX
  Extended buffer
Notes: Notice that the buffer has been extended so the flagger is visible from the straight away. Also notice the short taper and the location of both flaggers (on the shoulder!).

## Slide 32: Flagging by a Hill

## Slide 33: Good Position

## Slide 34: Stopping Traffic
Stand on the shoulder
Display “STOP” with palm out
Face traffic
Make eye contact
NEVER stand in front of oncoming, moving traffic!!
Notes: Remember never to stop in the path of moving vehicles. Stand on the shoulder and display the STOP side of the paddle with the right hand Use the left hand to also indicate stop by displaying the palm.

## Slide 35
Single Flagger
Notes: Single flagger operations are suitable only for locations with very good approach visibility for drivers in both directions.
Traffic should be very light, nd there should be very little probability of opposing traffic arriving at the work zone at the same time.
This flagging method is not appropriate for locations where it is reasonable to expect lines of traffic to develop.

## Slide 36: DO IT RIGHT!!