## Slide 1: Susan Harwood Work Zone Safety
Crane Management
Module 4

## Slide 2: Learning Objectives
Understand the most common hazards associated with cranes and derricks in construction.
Identify OSHA requirements for cranes and derricks in construction.

## Slide 4: Causes of Crane-Related Deaths in Construction
90 deaths
132 deaths
Source: U.S. Bureau of Labor Statistics Census of Fatal Occupational Injuries Research File
Notes: IN/PRO: Q: What does a crane collapse mean?
Q: How many deaths were due to crane collapse? 89

## Slide 5: Causes of Fatalities Electrocutions 25%
  Contact with overhead power lines account for
Source: U.S. Bureau of Labor Statistics Census of Fatal Occupational Injuries Research File

## Slide 6: Causes of Fatalities Struck by the Load
21%
Failure of hooks, slings, etc.
Loads falling out of rigging
Swinging loads
Source: U.S. Bureau of Labor Statistics Census of Fatal Occupational Injuries Research File

## Slide 7: Causes of Fatalities Struck-By the Cranes Includes failures and tip-overs
Struck by Crane Parts
Struck by Crane Booms
7%
12%
Source: U.S. Bureau of Labor Statistics Census of Fatal Occupational Injuries Research File

## Slide 8: Causes of Tip-Overs
Not accounting for poor ground conditions.
Failure to properly use outriggers or additional support.
Failure to level the crane.
Exceeding the load chart.

## Slide 9: Causes of Fatalities Falls
9%
Falls from cranes, crane loads and crane baskets
Source: U.S. Bureau of Labor Statistics Census of Fatal Occupational Injuries Research File

## Slide 10: Causes of Fatalities Caught-in-Between
Caught between crane and carriage or object
Caught under the boom during dismantling
5%
Source: U.S. Bureau of Labor Statistics Census of Fatal Occupational Injuries Research File

## Slide 11: Operator Responsibilities
The operator must understand the crane’s functions and limitations and operating characteristics.
Be familiar with the operating manual & load chart.
Inspect and maintain the crane regularly.
Inform the Owner of any problems, needed maintenance or necessary repairs to the machine.

## Slide 12: Operator Responsibilities
Supervise and train the oiler if applicable.
Being aware of any site conditions, ground, the presence of power lines, etc.
Check that the site is adequately prepared for the crane.
Review the planned operation with the supervision.
Find out the load and rigging weight and determine where the load is to be placed.

## Slide 13: Operator Responsibilities
Maintain communication with signal persons.
Shut down and securing the machine properly when it is unattended.
Insure that the accessible areas within the swing radius of the rear of the rotating superstructure of the crane are sufficiently barricaded.

## Slide 14: 1926.1400 Scope
Applies to power-operated
equipment used in construction
that can hoist, lower and horizontally
move a suspended load over 2,000lbs.
Such equipment includes, but is not limited to:
  articulating cranes (such as knuckle-boom cranes);
  crawler cranes;
  floating cranes;
  cranes on barges;
  locomotive cranes;
  mobile cranes

## Slide 15: 1926.1401 Controlling Entity
The “controlling entity” is defined as the entity who has overall responsibility for safety of the jobsite in relation to the crane and derricks in construction proposal.
Controlling entity is defined as the prime contractor, general contractor, construction manager or any other legal entity which has the overall responsibility for the construction of the project—its planning, quality and completion.

## Slide 16: 1926.1402 Ground Conditions
The “controlling entity” will
  Provide a firm, drained and graded area sufficient to support the crane (in conjunction with blocking, mats, etc.)
  Inform the user and the operator of the location of hazards beneath the equipment set-up area (such as voids, tanks, utilities) if those hazards are identified in documents that are in the possession of the controlling entity or the hazards are otherwise known to that controlling entity.

## Slide 18: Uncompacted Fills
Backfilled areas may have lower bearing capacities.
Do not set up on backfilled areas unless backfill is properly compacted and larger mats or floats are used

## Slide 19: Ground Support
Crane topple waikato

## Slide 20: Outrigger Pads and Floats
Outrigger pads are designed for good ground conditions.
Poor ground conditions reduce the amount of load a crane can safely place on the outrigger pad.

## Slide 21: Proper Outrigger Setup
Responsibility of User
Use additional support cribbing or "floats."
Floats must be level to assure the outrigger pad will not slide off causing the crane to tip.
NO!!!!

## Slide 22: Poor Outrigger Support
Soft ground, no cribbing

## Slide 23: Ground Pressure Under Outriggers
3 ft. diameter pad is 7 sq. ft.
Pressure is 7150 lb./sq. ft.
5 ft. square float is 25 sq. ft.
Pressure is 2000 lb./sq. ft.
5 feet
3 feet
Assuming 50,000 lb Outrigger Load

## Slide 24: Good Outrigger Support

## Slide 25: Ground Support Mats

## Slide 26: 1926.1404 Assembly/Disassembly
Assembly/disassembly must be supervised by a person who meets the criteria for both a competent person and a qualified person, or by a competent person who is assisted by one or more qualified persons

## Slide 27: Leveling
Cranes should be within 1 degree of level.
Past this point, the crane can lose 20% or more of its rated capacity.
Tipping and boom failures are possible.
Side load to boom

## Slide 28: Crane Set-Up
Proper Leveling
  Target level has low accuracy
  Accurate methods to level
      Carpenter’s level
      Ball as plumb bob
Not
level
Notes: Image: Rob Dahl & Ken Lindberg, Travelers employees
The small target levels provided by manufacturers are usually not accurate enough to level the crane to meet the requirements of the load chart.
There are two accurate methods available to level the crane.
  Use a carpenters level on a substantial component on the upper works of the crane such as the turn table bearing. The longer the level the more accurate. Gluing a equal thickness washer to each end of the level can also improve accuracy.
  Boom up to the highest boom angle possible. Look straight at the boom and notice if the ball hangs parallel to the boom. This does not work well in windy conditions.

## Slide 29
29
Use large jobsite
plumb-bob to check
if crane is level
If crane is level, load
line should be in center
of boom at all rotation
positions

## Slide 30: Weather And Environment
Manufacturer specs
  Some cranes require a reduction in capacity at 20 mph
  Others consider 0 mph in the load chart
Ways to measure
  Anemometer on the crane boom
  Flag on the end of the boom
  Weather channels, internet, etc.
Notes: Wind is a very important factor in crane operations. Some cranes require a reduction in capacity at 20 mph, while others consider 0 mph in the load chart. The operator must know what the machine’s wind limitations are and take appropriate action based on the instructions for that particular machine.
Most manufacturers do NOT account for wind on lifted load or boom. Use the Grove TLL chart found in the student handouts to illustrate. Operation note #5 states “ Rated loads do not account for wind on the lifted load or boom. It is recommended when wind velocity is above 20mph, rated loads and boom lengths shall be appropriately reduced.” As stated in the first sentence of this note, the manufacturer does not account for wind. The second part of this note states that it is up to the operator to appropriately reduce lifting capacities.
Discuss ways that wind speed can be measured:
  Anemometer on the crane boom is the best, provided the anemometer is properly calibrated.
  Watch weather channels, internet, 1-800- weather, etc. – When using data from these sources, you have to know where their data comes from. Most students will say the airport. This is not always true. Even if it does come from the airport, how far is the contractor’s job from the airport? Where on the airport does the data come from. Most students will say the tower. This is not totally accurate, since the actual reading normally comes from a NOA weather station at the end of a runway. These are not usually very tall (around 50 feet).
  Flag on the end of the boom – This does indicate wind direction which is important. Wind taken from the side can caused side-loading of the crane boom. Wind taken from the back of the boom, can cause the radius to increase which could result in an unstable condition if operating too close to the crane’s rated capacity.
  Wind speed and direction can change based upon terrain. In city environments, the “tunnel” effect is common.

## Slide 31: Weather And Environment
Wind on Side of Boom
  Wind acting on the side of the boom reduces the strength of the boom just like an out-of-level condition. It is also the direction that makes operation the most difficult.
Notes: Wind acting on the side of the boom reduces the strength of the boom just like an out of level condition. It is also the direction that makes operation the most difficult.
Photo-CSAO, ROF

## Slide 32: Weather and Environment - Ice and/or Snow-Covered Boom
  Do not operate the crane when the boom is covered with snow or ice.
  The weight of snow and ice can be substantial.
Notes: Do not operate the crane when the boom is covered with snow or ice.
- The additional weight of the snow or ice can overload the crane or cause the boom to buckle.
IN: ice weight 56 pounds per cubic foot; fresh fallen snow is 8 pound per cubic foot; wet packed snow is 40 pounds per cubic foot. (Bob’s Rigging & Crane Handbook, 6th edition. Pellow Engineering Services, Inc. 2005.)
Image: Shutterstock 182495450

## Slide 33: Power Lines
You must assume that all power lines are energized unless the utility company confirms that the power line has been de-energized and visibly grounded at the worksite.

## Slide 34: Clearance from a Power Line
Determine Operating Area – How Far the Crane Can Reach
If a Power Line in the Area it MUST be addressed.

## Slide 35: Power Line Safety/Assembly and Disassembly (under 350 kv) 1926.1407
Assembly/disassembly below power lines prohibited
Ensure that no part of the equipment, load line or load (including rigging and lifting accessories), gets closer than 20 feet to the power line.
De-energize and ground the ground the line.

## Slide 36: Operations Around Power Lines (up to 350 kV) - 1926.1408
The employer must make a hazard assessment and must define a work zone by demarcating boundaries.
  Option 1 – De-energize and ground the ground the line.
  Option 2 - Ensure that no part of the equipment, load line or load, gets closer than 20 feet to the power line.
  Option 3 – If line voltage is known – cannot get closer than minimum distances in Table A.

## Slide 38: Table A Minimum Clearance Distances
up to 50kv 10 feet
over 50 to 200kv 15 feet
over 200 to 350kv 20 feet
over 350 to 500kv 25 feet
over 500 to 750kv 35 feet
over 750 to 1,000kv 45 feet

## Slide 39: Option 2 & 3 – Signs and/or barriers

## Slide 40: Operations Around Power Lines (over 350 kV) - 1926.1409
The requirements of 1926.1407 and 1926.1408 apply to power lines over 350 kV,
Wherever the distance “20 feet” is specified, the distance “50 feet” shall be substituted.

## Slide 41: Operations closer than the minimum - 1926.1410
Equipment operations in which any part of the equipment is closer than the minimum approach distance under Table A to an energized power line is prohibited, except when the following requirements are met:
  It is infeasible to do the work without breaching the minimum approach distance.
  After consultation with the utility, it is infeasible to de-energize and ground the line or relocate the line.

## Slide 42
Must Show:
Staying Outside Zone
is Infeasible
Infeasible to
Deenergize and
Ground
Intentionally Working Closer Than Table A Zone
All of the following are required:
Power Line Owner – Sets Minimum Approach Distance
Planning Meeting – Procedures
Dedicated Spotter
Elevated Warning Line or Barricade
Insulating Link/Device
Nonconductive Rigging
Range Limiter (if Equipped)
Nonconductive Tag Line (if used)
Barricades - 10 feet from Equipment
Limit Access to Essential Employees
Ground Crane
Deactivate Automatic Re-energizer

## Slide 43: Power Line Safety While Traveling On Site - 1926.1411
Covers traveling the crane on the construction site with no load.
The clearances specified in Table T.
If any part of the equipment while traveling will get closer than 20 feet to the power line, a dedicated spotter who is in continuous contact with the operator is used.

## Slide 44: Table T – Minimum Clearance Distances While Traveling
With No Load And Boom/Mast Lowered
up to 0.75kv 4 feet
.75 to 50kv 6 feet
50 to 345kb 10 feet
345 to 750 16 feet
750 to 1,000 20 feet

## Slide 45: If Contact Occurs
Stay on the machine if possible.
Warn all others to stay away.
Notify power company immediately.
Attempt to move away but assure line is not “connected.”

## Slide 46: The Ground May Be Hot!
Electricity dissipates with the resistance of the ground.
As potential drops, fields develop around the electrified machine.

## Slide 47: Bail Out Procedures
If you must get out, jump with your feet together.
Do not touch the machine.
Shuffle out of the area.

## Slide 48: Working Around Transmitters
  A crane is like an antenna
    Can store electrical charge
  Common remedies
    Synthetic web slings
    Insulating riggers and other workers
    Rubber gloves
Notes: When a crane is close enough to a radio, TV, or microwave transmitter the crane can act like an antenna and store up an electrical charge. The amount of charge is not large enough to injure or kill. It can cause people to jump, slip, or fall. A common remedy is to use a synthetic web sling, also commonly known as a bull tail, to insulate riggers and other workers. It is advisable for operators to wear rubber gloves when getting on and off the machine.

## Slide 49: FAA Requirements
200 foot notification Form no. 7460 - 1
Working close to airport
Notes: Image: TCS photo 3116
FAA stands for federal aviation administration.
The FAA must be notified every time a crane is over 200 ft tall. They must be notified using form no. 7460-1 30 days in advance.
When close to airports the height requirement becomes less, contact the closest FAA office for more information.

## Slide 50: Inspections 1926.1412
Equipment that has had a repair or adjustment that relates to safe operation shall be inspected by a qualified person after such a repair or adjustment has been completed, prior to initial use.
Shift, Monthly and Annual Inspections are required.

## Slide 51: Shift Inspection 1926.1402(d)
A competent person shall begin a visual inspection prior to each shift, which shall be completed before or during that shift.
If any deficiency is identified, that constitutes a safety hazard, the equipment must be taken out of service until it has been corrected.

## Slide 52: Stop Operations
Operations shall not begin unless the safety devices are in proper working order.
If a device stops working properly during operations, the operator shall safely stop operations.
Operations shall not resume until the device is again working properly. Alternative measures are not permitted to be used.

## Slide 53: Monthly Inspections 1926.1412(e)
Each month the equipment is in service it shall be inspected by a competent person.
The inspection must be documented and maintained by the employer for a minimum of three months.

## Slide 54: Annual/comprehensive inspection - 1926.1412(f)
At least every 12 months the equipment shall be inspected by a qualified person
The following must be documented and retained for a minimum of 12 months.

## Slide 55: Wire Rope – Inspection & Selection - 1926.1413
Selection of replacement wire rope shall be in accordance with the requirements recommendations of the wire rope manufacturer, the equipment manufacturer, or a qualified person

## Slide 56: Operational Aids 1926.1416
Listed operational aids such as anti-two blocks are required on all equipment, unless otherwise specified.
Operations shall not begin unless the listed operational aids are in proper working order, except where the employer meets the specified temporary alternative measures.

## Slide 57: Operational Aids 1926.1416
If a listed operational aid stops working properly during operations, the operator shall safely stop operations until the temporary alternative measures are implemented or the device is again working properly.
A primary operational aid is the Anti-Two Block Device

## Slide 58: Anti-Two Blocks
Anti-Two Blocks must be tested

## Slide 59: Operations 1926.1417
Must comply with all manufacturer procedures applicable to operation including use with attachments.
Where the manufacturer procedures are unavailable, the employer shall develop and ensure compliance with all procedures necessary for the safe operation of the equipment and attachments.

## Slide 60: Load Weight 1926.1417(o)(3)
The operator shall verify that the load is within the rated capacity of the equipment by at least one of the following methods:
  The weight of the load shall be determined from a reliable source, by a reliable calculation method, or by other equally reliable means, or
  The operator can begin hoisting the load to determine, using an electronic load weighing device. If it exceeds 75 percent of the maximum rated capacity at the longest radius that will be used during the lift operation, the operator must STOP until load weight is determined.

## Slide 61: Overload?

## Slide 62: Critical Picks (Not Defined)
Common Issues:
  The load exceeds 85% of the capacity.
  Complications as a result of load configuration, clearance, danger to personnel power transmission equipment, or critical service process equipment.
  The weight of the load is 25 tons or greater and exceeds 50’ in length, height, and width.
  Lifts involve more than one crane to handle the load.

## Slide 63: Critical Picks Require Good Planning

## Slide 64: And Good Decision Making??!!??

## Slide 65: Tag Lines
Tag lines are not directly required by OSHA standards.
Tag lines should be attached to all loads, unless it is more hazardous to use one.
Free hanging tag lines must not be of such length or position that they could snag on the structure.

## Slide 66: Working Under Suspended Loads – 1926.1425(b)
While the operator is not moving a suspended load, no employee must be within the fall zone, except:
  Engaged in hooking, unhooking or guiding a load, or
  Engaged in the initial attachment of the load to a component or structure, or
  Operating a concrete hopper or concrete bucket.

## Slide 67: Unattended Suspended Loads 1417(e)(2)
The provisions do not apply to working gear (such as slings, spreader bars, ladders, and welding machines) where the weight of the working gear is negligible relative to the lifting capacity of the equipment as positioned, and the working gear is suspended over an area other than an entrance or exit.

## Slide 68: Is This Necessary? NO!!!
Notes: Does the contractor need to secure (or call it unsecure) compressed gases overhead like shown in the photo? No, the mishandling of the gases could have a catastrophic outcome.

## Slide 69: Authority To Stop Operation 1926.1418
Whenever there is a concern as to safety, the operator shall have the authority to stop and refuse to handle loads until a qualified person has determined that safety has been assured.

## Slide 70: Work Area Control/Swing Radius 1926.1424
Swing radius must be barricaded.
Instruct employees in how to recognize struck-by and pinch/crush hazard areas posed by the rotating superstructure.

## Slide 71: Swing Radius Barricades

## Slide 72: Signaling
Written or Oral Test
Practical Exam
Knowledge Areas
  Basic crane operations
  Standard hand signals
  Standard voice signals
  OSHA standards
Notes: Signal persons must be tested, either by a written or oral test, and demonstrate their qualifications through a practical exam.
Signal persons shall be tested and demonstrate their practical knowledge in the following areas:
Basic crane operations and limitations
Standard hand signals
Standard voice signals
OSHA standards
Photo – Brasfield & Gorie employee (ROF)

## Slide 73: Signaling 1926.1419
A signal person must be provided in each of the following situations:
  The point of operation, meaning the load travel or the area near or at load placement, is not in full view of the operator.
  When the equipment is traveling, the view in the direction of travel is obstructed.
  Due to site specific safety concerns, either the operator or the person handling the load determines that it is necessary.

## Slide 74: Signals – Radio, Telephone 1926.1420
The devices shall be tested on site before beginning operations to ensure that the transmission is clear and reliable.
Signal transmission must be through a dedicated channel.
Exception: Multiple cranes/derricks and one or more signal persons may share a dedicated channel for the purpose of coordinating operations.

## Slide 75: Voice Signals 1926.1421
The operator, signal person and lift director (if there is one), must communicate the voice signals that will be used.
Each voice signal must contain the following three elements, given in the following order:
  function (such as hoist, boom, etc.),
  direction; distance and/or speed; function,
  stop command.
The operator, signal person and lift director (if there is one), must be able to effectively communicate in the language used

## Slide 76: Signal person qualifications 1926.1428
The employer shall ensure that each signal person meets the Qualification Requirements by using either:
Third party qualified evaluator. (Portable)
Employer’s qualified evaluator. (Not Portable)

## Slide 77: Signaler Qualification Requirements 1926.1428(c)
Each signal person must:
(1) Know and understand the type of signals used.
(2) Be competent in the application of the type of signals used.
(3) Have a basic understanding of equipment operation and limitations, including the crane dynamics involved in swinging and stopping loads and boom deflection from hoisting loads.
(4) Know and understand the relevant requirements of § 1926.1419 through § 1926.1422 and § 1926.1428.
(5) Demonstrate that he/she meets the requirements in paragraphs (c)(1) through (4) of this section through an oral or written test, and through a practical test.

## Slide 78: Signal Person Documentation
The employer must make documentation of signal person’s qualification available at the site.
The documentation must specify each type of signaling (e.g. hand signals, radio signals, etc.) for which the signal person is qualified.

## Slide 79: Crane Operator Certifications 1926.1427
Crane Operators will be required to be certified in November of 2014. (2017)
The employer must ensure that the operator is either qualified or certified to operate the equipment in accordance with one of the options of this section, or is operating the equipment during a training period.

## Slide 80: Pre-Qualification/Certification Training Period
An employee who is not qualified or certified is permitted to operate equipment if:
  The employee is provided with sufficient training to enable the trainee to operate the equipment safely under limitations established.
  The tasks performed by the trainee/apprentice while operating the equipment shall be within the trainee’s ability.
  While operating the equipment, the trainee shall be continuously supervised.

## Slide 81: Hoisting Personnel 1926.1431
The use of equipment to hoist employees is prohibited except where the erection, use, and dismantling of conventional means of reaching the worksite, is not possible because of the project’s structural design or worksite conditions.
This paragraph does not apply to work covered by subpart R

## Slide 82: Multiple-Crane/Derrick Lifts -Supplemental Requirements 1926.1432
Before beginning a crane/derrick operation in which more than one crane/derrick will be supporting the load, the operation must be planned.

## Slide 83: Multi-lift Plans 1926.1432
Lift Plans must be developed by a qualified person.
Where the qualified person determines that engineering expertise is needed for the planning, the employer must ensure that it is provided.

## Slide 84: Floating Cranes and Land Cranes on Barges - 1926.1437
Supplemental requirements for floating cranes on barges.
Does not apply when using jacked barges when the jacks are deployed to the river or lake bed and the barge is fully supported by the jacks.

## Slide 85: Loading on to a Barge
Crane load on barge

## Slide 86: Barge Work
Swing Radius Protection
  Warning lines or barricades
  Clearly mark hazard areas
Crane on barge secured
  Physical Attachment
  Corralling
  Rails
  Centerline Cable
Notes:   Swing radius protection (1437(c)(2)) states that the employer must either erect and maintain warning lines or barricades or clearly mark the hazard areas by a combination of warning signs and high visibility markings on the equipment. In addition the employer must train each employee to understand what these markings signify.
  Option 1- Physical attachment- This option includes using crossed cable systems, bolting, welding, or using chains to secure the crane to the barge.
  Option 2 – Corralling – This option involves installing a barricade system that prevents the crane from shifting in any direction.
  Option 3 - Rails – This option is for cranes that are prevented from shifting due to being mounted on a rail system.
  Option 4 – Centerline cable system – This option involves preventing the crane from shifting by using a wire rope system that is attached to the barge and to the crane’s undercarriage. The wire rope system allows the crane to move longitudinally for repositioning but secures the crane against movement during operation.
  Photo - Lunda

## Slide 87: Training Requirements 1926.1430
Employers must evaluate employee’s understanding of their training.
OSHA requires training in:
  Power line safety,
  Recognizing hazards such as swing radius and pinch points.
  Competent persons and qualified persons must be trained in their respective roles.
  Signaling.

## Slide 88: Site Conditions
Provide proper working area
Assure adequate ground stability
Maintain clearance with overhead power lines
Provide overhead protection for other workers

## Slide 89: Supervision Responsibilities
Have the right crane to do the job.
Ensure crane is in safe operating condition.
Assure operator is adequately trained.
Assure riggers are competent.

## Slide 90: Supervision Responsibilities
Know the weights of the loads.
Do not pressure an operator into an unsafe lift.
Assure good communication between all involved.