## Slide 1
Introduction
Oct. 2019 – Sep. 2020
Crane Management in Construction
AGC-OSHA Susan Harwood Training Grant

## Slide 2
This material was produced under grant number SH-05112-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Photos shown in this presentation may depict situations that are not in compliance with applicable OSHA requirements.
It is not the intent of the content developers to provide compliance-based training in this presentation, the intent is more to address hazard awareness in the construction industry, and to recognize the overlapping hazards present in many construction workplaces.
It should NOT be assumed that the suggestions, comments, or recommendations contained herein constitute a thorough review of the applicable standards, nor should discussion of “issues” or “concerns” be construed as a prioritization of hazards or possible controls. Where opinions (“best practices”) have been expressed, it is important to remember that safety issues in general and construction jobsites specifically will require a great deal of site- or hazard-specificity – a “one size fits all” approach is not recommended, nor will it likely be very effective.
Disclaimer/Usage Notes
Introduction

## Slide 3
No representation is made as to the thoroughness of the presentation, nor to the exact methods of remediation to be taken. It is understood that site conditions vary constantly, and that the developers of this content cannot be held responsible for safety problems they did not address or could not anticipate, nor those which have been discussed herein or during physical presentation. It is the responsibility of the employer, its subcontractors, and its employees to comply with all pertinent rules and regulations in the jurisdiction in which they work. Copies of all OSHA regulations are available from your local OSHA office, and many pertinent regulations and supporting documents have been provided with this presentation in electronic or printed format.
It is assumed that individuals using this presentation or content to augment their training programs will be “qualified” to do so, and that said presenters will be otherwise prepared to answer questions, solve problems, and discuss issues with their audiences.
Areas of particular concern (or especially suited to discussion) have additional information provided in the “notes” section of slides throughout the program…as a presenter, you should be prepared to discuss all of the potential issues/concerns, or problems inherent in those photos particularly.
Disclaimer/Usage Notes
Introduction

## Slide 4
0.8 IACET CEUs | The Associated General Contractors of America (AGC) has been accredited as an Accredited Provider by the International Association for Continuing Education and Training (IACET). In obtaining this accreditation, AGC has demonstrated that it complies with the ANSI/IACET Standard which is recognized internationally as a standard of good practice. As a result of their Accredited Provider status, AGC is authorized to offer IACET CEUs for its programs that qualify under the ANSI/IACET Standard.
In order to qualify for IACET CEUs, participants must:
  Attend the conference for at least 90% of the time.
  Complete the instructor evaluation and overall course evaluation.
  Complete an assessment with a score of 75% or greater.
To obtain a certificate, you must complete the instructor and overall course evaluations as well as earn a passing grade from completing the assessment. More detailed instructions will be provided to participants during the training course.
How to Earn CEUs
Introduction

## Slide 5
The training will review OSHA crane standards, industry best practices, and resources for additional crane safety assistance. The training will provide information to employers and employees who need to know the following:
Hazards related to cranes;
Types, components, and crane functionality;
Crane inspections;
Personnel competency; and
Crane management.
Overall Learning Objectives
Introduction

## Slide 6
AGC event speakers may have proprietary interests, including but not limited to, exposure to the industry, increased consultation services, book sales and/or receipt of financial compensation/speaking fees.
Speaker Disclosure
Introduction

## Slide 7
You have the right to:
A safe and healthful workplace
Know about hazardous chemicals
Information about injuries and illnesses in your workplace
Complain or request hazard correction from employer
Safety & Health Training
Hazard exposure and medical records
File a complaint with OSHA
Participate in an OSHA inspection
Be free from retaliation for exercising safety and health rights
Your Rights Under OSHA
Introduction

## Slide 8
Provide a workplace free from recognized hazards and comply with OSHA standards
Provide safety & health training required by OSHA standards
Keep records of injuries and illnesses
Provide medical exams when required by OSHA standards and provide workers access to their exposure and medical records
Not discriminate against workers who exercise their rights under the Act (Section 11(c))
Post OSHA citations and abatement verification notices
Provide and pay for PPE
Employer Responsibilities
Introduction

## Slide 9
Workers may bring up safety and health concerns in the workplace to their employers without fear of discharge or discrimination, as long as the complaint is made in good faith.
Workers may file a complaint with OSHA if they believe a violation of a safety or health standard, or an imminent danger situation, exists in the workplace.
OSHA regulations protect workers who complain to their employer about unsafe or unhealthful conditions in the workplace.
Workers may request that their name not be revealed to the employer.
Complain or Request Corrections
Introduction

## Slide 10
If a worker files a complaint, they have the right to find out OSHA’s action on the complaint and request a review if an inspection is not made.
More information on workers rights and filing complaints can be found on the OSHA website at www.osha.gov/as/opa/worker/complain.html
NOTE: Often the best and fastest way to get a hazard corrected is to notify your supervisor or employer.
Complain or Request Corrections
Introduction

## Slide 11
Protection from workplace place retaliation means an employer cannot take “adverse actions” against workers, such as:
Firing or laying off
Blacklisting
Demoting
Denying overtime or promotion
Disciplining
Denial of benefits
Protection from Workplace Retaliation
Introduction
Failure to hire or rehire
Intimidation/harassment
Making threats
Reassignment affecting prospects
Reducing pay or hours

## Slide 12
Workers may report a whistleblower claim within 30 days of the incident.
Online
Fax
Mail
Telephone
In-person
How to File a Safety and Health Complaint
Introduction

## Slide 13
Boom or crane contact with energized power lines (nearly 45% of the cases)
Under the hook lifting device.
Overturned cranes.
Dropped loads.
Boom collapse.
Crushing by the counter-weight.
Outrigger use, falls and rigging failures.
Major Causes of Crane Accidents
Introduction

## Slide 14
Causes of Crane-Related Deaths in Construction, 1992-2006
Introduction
157 deaths
132 deaths
89 deaths
78 deaths
56 deaths
47 deaths
30 deaths
43 deaths
Total deaths: 632
Notes: Q: What does a crane collapse mean?
Q: How many deaths were due to crane collapse?

## Slide 15
Causes of Crane Fatalities
Introduction
Electrocution | 39% | Struck by counterweight | 3%
Crane assembly/disassembly | 12% | Two-blocking | 2%
Boom buckling | 8% | Hoist limitation | 1%
Crane upset/overturn | 7% | Killer hooks | 1%
Rigging failure | 7% | Access/egress | <1%
Overloading | 4% | Control confusion | <1%
Struck by moving load | 4% | Unknown/insufficient info. | <1%
Manlifts | 4% | Other | 5%
Source: A. Suruda,et al, Crane-Related Deaths in the U.S. Construction Industry, 1984-94

## Slide 16
Fatalities Working With Cranes
Introduction

## Slide 17
OSHA Issued 175 Citations of Subpart CC – Cranes and Derricks in Fiscal Year 2019
    131 Violations were considered Serious
    2 Violations were considered Willful
    19 Violations were the result of Accidents
    US Dept. of Labor – OSHA Stats
OSHA Citation Statistics
Introduction
Notes: Standard Total Vio(s) Ser Vio(s) Will Vio(s) Rep Vio(s) Unc. Vio(s) Othr Vio(s) Cmpt Acci. Imm. Dngr Refer. Cntsd % Cntsd Avg Abt Days Avg Corr. Days
1926.1400(f) 1 1 0 0 0 0 0 0 0 1 1 100% 14.
1926.1402(b) 5 4 0 0 0 1 0 0 0 1 0 0% 8.3 17.3
1926.1403(a) 4 4 0 0 0 0 0 1 0 1 2 50% 12.7
1926.1404(b) 1 1 0 0 0 0 0 0 0 0 1 100% 14.
1926.1404(c) 1 1 0 0 0 0 0 1 0 0 1 100% 6.
1926.1404(d)(1) 1 1 0 0 0 0 0 0 0 1 1 100% 14.
1926.1404(f)(1) 2 2 0 0 0 0 0 1 0 0 1 50% 12.
1926.1404(h)(1) 1 1 0 0 0 0 0 0 0 1 0 0% 18.
1926.1404(h)(2) 1 1 0 0 0 0 0 0 0 1 0 0% 4. 30.
1926.1404(h)(7) 1 1 0 0 0 0 0 1 0 0 1 100% 6.
1926.1404(q)(2) 2 0 0 0 0 2 0 0 0 0 0 0% 8. 8.5
1926.1404(r)(1) 1 1 0 0 0 0 0 0 0 0 0 0% 6.
1926.1408(a)(1) 2 1 0 0 0 1 0 1 0 1 0 0% 26.
1926.1408(a)(2) 4 4 0 0 0 0 0 1 0 1 0 0% 24.7 31.5
1926.1408(a)(2)(iii)(B) 4 4 0 0 0 0 0 1 0 1 2 50% 24.7 59.
1926.1408(b)(1) 1 1 0 0 0 0 0 0 0 1 0 0% 29.
1926.1408(b)(3) 2 2 0 0 0 0 0 0 0 1 2 100% 33. 68.
1926.1408(g)(1)(i) 1 1 0 0 0 0 0 0 0 0 0 0% 29. 25.
1926.1410(d)(1) 1 1 0 0 0 0 0 0 0 0 0 0% 29.
1926.1411(b)(1) 1 1 0 0 0 0 0 0 0 1 0 0% 18.
1926.1411(b)(2) 1 1 0 0 0 0 0 0 0 1 1 100%
1926.1411(b)(5)(i) 1 1 0 0 0 0 0 0 0 1 1 100%
1926.1412(c)(1) 1 1 0 0 0 0 0 0 0 1 0 0% 18.
1926.1412(c)(3) 1 1 0 0 0 0 0 1 0 0 0 0% 20.
1926.1412(d)(1) 9 8 0 0 0 1 0 0 0 0 0 0% 10.5 22.
1926.1412(d)(1)(x) 2 2 0 0 0 0 0 0 0 0 0 0% 18.
1926.1412(d)(1)(ii) 1 1 0 0 0 0 0 0 0 0 1 100% 33.
1926.1412(d)(1)(ix) 1 0 0 0 0 1 0 0 0 0 1 100%
1926.1412(d)(1)(xii) 1 1 0 0 0 0 0 0 0 0 0 0% 8.
1926.1412(d)(1)(xiv) 1 1 0 0 0 0 0 0 0 1 0 0% 4. 15.
1926.1412(d)(3) 1 1 0 0 0 0 0 0 0 0 0 0% 19.
1926.1412(e)(1) 4 3 0 0 0 1 0 1 0 0 0 0% 17.8 7.
1926.1412(e)(3) 2 1 0 0 0 1 0 0 0 0 0 0% 11.5 3.
1926.1412(e)(3)(i) 4 1 0 0 0 3 0 0 0 0 0 0% 23. 29.
1926.1412(e)(3)(i)(A) 1 0 0 0 0 1 0 0 0 0 0 0% 26. 16.
1926.1412(e)(3)(i)(B) 1 1 0 0 0 0 0 1 0 0 0 0% 16. 16.
1926.1412(f)(1) 6 3 0 0 0 3 1 0 0 0 0 0% 73.7 51.3
1926.1412(f)(2) 3 2 0 0 0 1 0 0 0 0 0 0% 19.5 22.
1926.1412(f)(2)(xiv) 1 1 0 0 0 0 0 0 0 0 0 0%
1926.1412(f)(6) 1 1 0 0 0 0 0 0 0 0 0 0% 16. 16.
1926.1412(f)(7) 4 2 0 0 0 2 0 0 0 0 0 0% 18. 24.3
1926.1412(f)(7)(i) 1 0 0 0 0 1 0 0 0 0 0 0% 18.
1926.1412(k) 1 0 0 0 0 1 0 0 0 0 0 0% 18.
1926.1413(a)(2)(i)(A) 1 1 0 0 0 0 0 0 0 0 1 100% 8.
1926.1413(b)(4) 1 0 0 0 0 1 0 0 0 0 0 0% 10.
1926.1413(c)(2) 1 0 0 0 0 1 0 0 0 0 0 0% 18. 5.
1926.1413(c)(4) 2 0 0 0 0 2 0 1 0 0 0 0% 13. 16.
1926.1415(b) 1 1 0 0 0 0 0 0 0 0 0 0%
1926.1416(b) 1 1 0 0 0 0 0 0 0 1 0 0% 4. 15.
1926.1416(d)(3)(i) 1 1 0 0 0 0 0 0 0 0 0 0% 13.
1926.1416(d)(3)(ii)(B) 1 1 0 0 0 0 0 0 0 0 1 100% 11.
1926.1416(d)(3)(ii)(D) 1 1 0 0 0 0 0 0 0 0 0 0% 20.
1926.1416(e)(3) 1 0 0 0 0 1 0 0 0 0 0 0% 18.
1926.1416(e)(4) 1 0 0 0 0 1 0 0 0 0 0 0% 18.
1926.1416(e)(5)(i) 2 1 0 0 0 1 0 1 0 1 0 0% 8. 18.
1926.1417(a) 4 4 0 0 0 0 0 1 0 1 1 25% 30.3 37.
1926.1417(c)(1) 4 2 0 0 0 2 0 0 0 0 0 0% 18.3 34.5
1926.1417(o)(1) 2 2 0 0 0 0 0 0 0 1 1 50% 18.5 17.
1926.1417(o)(2) 1 1 0 0 0 0 0 0 0 1 1 100% 4.
1926.1417(o)(3) 1 1 0 0 0 0 0 0 0 1 1 100% 4.
1926.1417(q) 1 1 0 0 0 0 0 1 0 0 0 0%
1926.1417(w) 2 2 0 0 0 0 0 0 0 0 0 0% 27.5
1926.1419(f) 2 1 0 0 0 1 0 0 0 1 1 50% 33.
1926.1422 1 0 0 0 0 1 0 0 0 0 0 0% 18.
1926.1424(a)(2)(ii) 2 1 0 0 0 1 0 0 0 0 0 0% 9. 4.
1926.1425(b)(1) 1 1 0 0 0 0 0 0 0 0 0 0%
1926.1425(c)(1) 4 2 0 0 0 2 1 0 0 1 1 25% 31. 12.
1926.1425(c)(2) 2 2 0 0 0 0 0 0 0 0 0 0% 14.
1926.1425(c)(3) 2 2 0 0 0 0 0 0 0 0 0 0% 25.
1926.1425(e)(1) 1 1 0 0 0 0 0 0 0 0 0 0% 11. 17.
1926.1425(e)(2) 1 1 0 0 0 0 1 0 0 0 0 0%
1926.1427(a) 3 2 0 0 0 1 0 0 0 0 0 0% 12.3 12.
1926.1427(a)(1) 4 4 0 0 0 0 0 0 0 1 1 25% 25. 46.3
1926.1427(a)(2) 2 1 0 0 0 1 0 1 0 0 0 0% 27.
1926.1427(b)(2) 1 1 0 0 0 0 0 0 0 0 1 100% 18.
1926.1427(b)(4) 1 1 0 0 0 0 0 0 0 0 1 100% 17.
1926.1427(c)(1)(i) 1 0 0 0 0 1 0 0 0 0 0 0%
1926.1427(f)(4) 1 1 0 0 0 0 0 0 0 0 0 0% 18.
1926.1427(k)(2)(i) 1 0 1 0 0 0 0 0 0 1 1 100% 8.
1926.1427(k)(2)(ii) 1 0 1 0 0 0 0 0 0 1 1 100% 18.
1926.1428(a) 7 5 0 0 0 2 0 0 0 0 1 14.29% 26. 20.8
1926.1428(a)(3) 1 0 0 0 0 1 0 0 0 0 0 0% 18.
1926.1428(b) 1 1 0 0 0 0 0 0 0 1 0 0% 13.
1926.1428(c)(5) 1 0 0 0 0 1 0 0 0 0 0 0% 33. 31.
1926.1430(b) 2 2 0 0 0 0 0 0 0 1 0 0% 31. 14.5
1926.1430(d) 1 1 0 0 0 0 0 0 0 0 0 0% 18.
1926.1431(a) 2 2 0 0 0 0 0 1 0 0 0 0% 24. 18.
1926.1431(e)(10) 1 1 0 0 0 0 1 0 0 0 1 100% 4. 41.
1926.1431(f)(3)(ii) 1 1 0 0 0 0 1 0 0 0 1 100% 4. 41.
1926.1431(f)(4) 2 2 0 0 0 0 0 0 0 0 0 0% 18. 14.
1926.1431(k)(2)(ii) 1 1 0 0 0 0 0 0 0 0 0 0% 19.
1926.1431(k)(10)(i) 1 1 0 0 0 0 0 1 0 0 0 0% 19.
1926.1431(m)(2) 3 2 0 0 0 1 0 0 0 0 0 0% 24. 18.
1926.1437(c)(2)(i) 2 2 0 0 0 0 0 1 0 0 0 0% 13. 16.
1926.1437(g)(1) 1 1 0 0 0 0 0 1 0 0 0 0% 13. 16.
1926.1437(h)(1) 1 1 0 0 0 0 0 0 0 0 0 0% 6.
1926.1437(n)(5) 1 1 0 0 0 0 0 0 0 0 0 0%
175 131 2 0 0 42 5 19 0 29 32

## Slide 18
OSHA Citation Statistics (2019)
Introduction
OSHA Standard | Description | Violations
1926.1412(f) | Annual Inspections, including Full Inspection and Documentations by Qualified Persons | 13
1926.1412(d) | Shift Inspections by Competent Persons | 9
1926.1408(a)(2) | Power Lines must have demarking boundaries and adequate clearance consistent with Table A is required. | 8
1926.1412(e) | Monthly Inspections and Documentation by a Competent Person | 8
1926.1417(a)&(c) | Load charts and Manufacturer’s procedures must be in the cab of the crane and complied with | 8
1926.1427(a) | Operators must be trained, certified and evaluated or be an "Operator-in-Training" | 7
1926.1428(a) | Employees signaling cranes must be Qualified | 7
1926.1402(b) | Users must provide adequate ground support | 5
1926.1403(a) | Assembly/Disassembly – Users must follow manufacturer’s procedures | 4
1926.1425(c)(1) | Materials must be rigged to prevent unintentional displacement | 4
1926.1431(m)(2) | Hoisting Personnel – Pre-lift meeting with operator, signaler, hoisted emp., and responsible person required. | 3
Notes: Most Cited Federal OSHA Citations FY2019
Subpart CC - Cranes
Standard Description Total Violations
1926.1412(d)(1) Inspections - Shift Inspections by Competent Persons 9
1926.1428(a) Signaling – Employees signaling cranes must be Qualified 7
1926.1412(f)(1 )Inspections - Annual Inspections by Qualified Persons 6
1926.1402(b) Ground Conditions – Users must provide adequate support 5
1926.1403(a) Assembly/Disassembly – Users must follow manufacturer’s procedures 4
1926.1408(a)(2) Power Lines – Users must establish demarking boundaries for adequate clearance 4
1926.1408(a)(2)(iii)(B) Power Lines – Must maintain clearance consistent with Table A Clearance Requirements 4
1926.1412(e)(1) Inspections - Monthly Inspections by a Competent Person 4
1926.1412(e)(3)(I) Inspections - Documentation of Monthly Inspections 4
1926.1412(f)(7) Inspections - Documentation of Annual/Comprehensive Inspection. 4
1926.1417(a) Operations – Employers must comply with Manufacturer’s Procedures 4
1926.1417(c)(1) Operations – Load charts and Manufacturer’s procedures must be in the cab of the crane 4
1926.1425(c)(1) Rigging – Materials must be rigged to prevent unintentional displacement 4
1926.1427(a)(1) Operator Training – Employee’s not certified and evaluated must be designated as an “Operator-in-Training” 4
1926.1412(f)(2) Inspection – Annual inspection – Disassembly is required, as necessary to do full inspection 3
1926.1427(a) Operator Training – Employer must assure each operator is trained, certified and evaluated 3
1926.1431(m)(2) Hoisting Personnel – Pre-lift meeting with operator, signaler, hoisted emp., and responsible person required. 3

## Slide 19
Applies to power-operated equipment used in construction that can hoist, lower and horizontally move a suspended load over 2,000lbs.
Such equipment includes, but is not limited to:
    articulating cranes (such as knuckle-boom cranes);
    crawler cranes;
    floating cranes;
    cranes on barges;
    locomotive cranes;
    mobile cranes.
1926.1400 Scope
Introduction

## Slide 20
The “controlling entity” is defined as the entity who has overall responsibility for safety of the jobsite in relation to the crane and derricks in construction proposal.
Controlling entity is defined as the prime contractor, general contractor, construction manager or any other legal entity which has the overall responsibility for the construction of the project—its planning, quality and completion.
1926.1401 Controlling Entity
Introduction

## Slide 21
Provide proper working area
Assure adequate ground stability
Maintain clearance with overhead power lines
Provide overhead protection for other workers
Site Conditions
Introduction

## Slide 22
Have the right crane to do the job.
Ensure crane is in safe operating condition.
Assure operator is adequately trained and qualified.
Assures signalers are qualified.
Assure riggers are qualified.
Supervision Responsibilities
Introduction

## Slide 23
Understand the working radius of cranes
Know the weights of the loads.
Do not pressure an operator into an unsafe lift.
Assure good communication between all involved.
Supervision Responsibilities
Introduction

## Slide 24
Questions?
Introduction