## Slide 1
Hazards Related to Cranes
Oct. 2019 – Sep. 2020
Crane Management in Construction
AGC-OSHA Susan Harwood Training Grant

## Slide 2
Learn about:
Weather conditions that affect crane operations
Ground conditions and hazards
Crane assembly
Swing radius protection
Power line hazards
Objectives
Hazards Related to Cranes

## Slide 3
Hazards Related to Cranes
Crane Boom Failures
Crane Overload
Tip-Over
Tower Crane Collapse

## Slide 4
Weather and Environment
Ground Conditions
Power Lines
Conditions Affecting Operations
Hazards Related to Cranes
Notes: These are the topics that will be covered in more detail later in this module.
Can anyone think of other conditions that can affect operations?
Logistics (i.e., multiple mobilizations). Requires backwards planning (~2 weeks out) to bring in a crane @ certain time/place. Preplanning is essential)
Time pressure
: What is the greatest hazard, in your opinion?

## Slide 5
Do not operate the crane when the boom is covered with snow or ice.
The weight of snow and ice can be substantial.
Weather and Environment – Ice and/or Snow-Covered Boom
Hazards Related to Cranes
Notes: Do not operate the crane when the boom is covered with snow or ice.
- The additional weight of the snow or ice can overload the crane or cause the boom to buckle.
ice weight 56 pounds per cubic foot; fresh fallen snow is 8 pound per cubic foot; wet packed snow is 40 pounds per cubic foot.
(Bob’s Rigging & Crane Handbook, 6th edition. Pellow Engineering Services, Inc. 2005.)
Image: Jim Goss

## Slide 6
Rain
    Wet clutches & brakes
    House doors, windows & leaks
    Condensation
Lightning
    Raised boom acts like lightning rod
    Retract and lower boom
Weather and Environment – Water and Wet Conditions
Hazards Related to Cranes
Image courtesy of eLCOSH.org. Used with permission.
Notes: Clutches and brakes may not hold the load if they get wet from rain or melting snow.
If rain starts during the work shift and a door is open that would allow rain to get on clutches or brakes the load could fall.
- This situation could also be caused by leaks in the machinery enclosure.
- The operator must ensure that this will not happen.
- A similar situation can happen to a snow covered crane;
“As the snow melts water can enter the enclosures or cab???”.
Condensation is a fact of life, water comes out of the air and collects on a cool surface.
- That makes it necessary to dry out clutches and brakes at the beginning of a shift.
- Also over a period of time this condensation can build up inside of enclosed spaces such as boom chords.
- This can create corrosion and even crack the members if enough water accumulates then freezes.
Raised boom acts like lightning rod
Retract and lower the boom with impending storms.
Image: eLCOSH

## Slide 7
Manufacturer Specs
    Some cranes require a reduction in capacity at 20 mph
    Others consider 0 mph in the load chart
Ways to Measure
    Anemometer (Wind Speed Gauge) on the crane boom
    Flag on the end of the boom
    Weather channels, internet, etc.
Wind Speed
Hazards Related to Cranes
Image courtesy of eLCOSH.org. Used with permission.
Notes: Wind is a very important factor in crane operations.
- Some cranes require a reduction in capacity at 20 mph, while others consider 0 mph in the load chart.
- The operator must know what the machine’s wind limitations are and take appropriate action based on the instructions for
that particular machine.
Most manufacturers do NOT account for wind on lifted load or boom.
For instance: Grove’s TLL chart contains a cautionary set of Operation Notes.
Grove’s TLL Chart’s Operation Note #5 states: “ Rated loads do not account for wind on the lifted load or boom. It is recommended when wind velocity is above 20 mph, rated loads and boom lengths shall be appropriately reduced.”
As stated in the first sentence of this note, the manufacturer does not account for wind.
The second part of this note states that it is up to the operator to appropriately reduce lifting capacities.
Discuss ways that wind speed can be measured:
Anemometer on the crane boom is the best, provided the anemometer is properly calibrated.
Watch weather channels, internet, 1-800- weather, etc.
When using data from these sources, you have to know where their data comes from!
Most students will say the information comes from the airport.
This is not always true!
Even if it does come from the airport…,
how far is the contractor’s job from the airport?
Where on the airport does the data come from?
  Most students will say the tower.
  This is not totally accurate, since the actual reading normally comes from a NOA weather station at the end of a runway.
  These are not usually very tall (around 50 feet).
Flag on the end of the boom
This does indicate wind direction which is important.
Wind taken from the side can caused side-loading of the crane boom.
Wind taken from the back of the boom, can cause the radius to increase which could result in an unstable condition if operating too close to the crane’s rated capacity.
REMEMBER:
Wind speed and direction can change based upon terrain.
In city environments, the “tunnel” effect is common.

## Slide 8
Over 50% of crane accidents are the result of
Support failure
Improper use of outriggers
Crane Accidents
Hazards Related to Cranes
Notes: Most incidents called “crane accidents” are really “rigging failures.” Those incidents where rigging failure is not the issue are largely from support failure or improper use of outriggers.

## Slide 9
The “controlling entity” will
    Provide a firm, drained and graded area sufficient to support the crane (in conjunction with blocking, mats, etc.)
    Inform the user and the operator of the location of hazards beneath the equipment set-up area (such as voids, tanks, utilities) if those hazards are identified in documents that are in the possession of the controlling entity or the hazards are otherwise known to that controlling entity.
1926.1402 Ground Conditions
Hazards Related to Cranes

## Slide 10
Poor Ground Conditions & Crane Overloads Result in Crane Tip-Overs
Hazards Related to Cranes

## Slide 11
Hazards Related to Cranes
Ground Failure Under Tracks
Failure Over Voids
Failure on Bridge Deck

## Slide 12
Backfilled areas may have lower bearing capacities.
Do not set up on backfilled areas unless backfill is properly compacted and larger mats or floats are used
Uncompacted Fills
Hazards Related to Cranes
Ground Failure Uncompacted Soils

## Slide 13
Hazards Related to Cranes
Ground Settlement Failure Under Tracks
Notes: IN: Corps of Engineers job at Parris Island, SC. No mats used.
Image: Chip Pocock

## Slide 14
Ground Support
Hazards Related to Cranes
Crane Topple Waikato
Ground Failure Crane Tip-over Accident Video

## Slide 15
Assuming 50,000 lb Outrigger Load
Ground Pressure Under Outriggers
Hazards Related to Cranes
3 feet
3 ft. diameter pad is 7 sq. ft.
Pressure is 7150 lb./sq. ft.
5 feet
5 ft. square float is 25 sq. ft.
Pressure is 2000 lb./sq. ft.

## Slide 16
Outrigger pads are designed for good ground conditions.
Poor ground conditions reduce the amount of load a crane can safely place on the outrigger pad.
Outrigger Pads and Floats
Hazards Related to Cranes

## Slide 17
Machine Set Up
Lift Boom Off Ground No Outriggers
Lay Boom On Ground No Outriggers
Change Boom No Outriggers
Add/Remove Counter Weight No Outriggers
Improper Use Of Outriggers
Hazards Related to Cranes

## Slide 18
Responsibility of User
Use additional support cribbing or "floats."
Floats must be level to assure the outrigger pad will not slide off causing the crane to tip.
Improper Outrigger Setup
Hazards Related to Cranes
NO!!!!

## Slide 19
Poor Outrigger Support
Hazards Related to Cranes
Soft ground, no cribbing

## Slide 20
Good Outrigger Support
Hazards Related to Cranes
Full Ground Cover and Distribution of Outrigger Weight on Outrigger Floats

## Slide 21
Crawler Crane Ground Support
Hazards Related to Cranes
Notes: Highest ground pressure exerted by tracks is when boom is over a corner
Lowest is when boom is directly over the side
In the middle is when the boom is directly over an end
Image: TEEX

## Slide 22
Ground Support Mats
Hazards Related to Cranes
Full Ground Cover and Distribution of Outrigger
Weight on Outrigger Floats

## Slide 23
Proper Leveling
    Target level has low accuracy
    Accurate methods to level
      Carpenter’s level
      Ball as plumb bob
Crane Set-Up
Hazards Related to Cranes
Not
level
Notes: Image: Rob Dahl & Ken Lindberg, Travelers employees
The small target levels provided by manufacturers are usually not accurate enough to level the crane to meet the requirements of the load chart.
There are two accurate methods available to level the crane.
  Use a carpenters level on a substantial component on the upper works of the crane such as the turn table bearing. The longer the level the more accurate. Gluing a equal thickness washer to each end of the level can also improve accuracy.
  Boom up to the highest boom angle possible. Look straight at the boom and notice if the ball hangs parallel to the boom. This does not work well in windy conditions.

## Slide 24
Cranes should be within 1 degree of level.
Past this point, the crane can lose 20% or more of its rated capacity.
Tipping and boom failures are possible.
Leveling
Hazards Related to Cranes
Side load to boom

## Slide 25
Assembly/disassembly Director (A/D)
  Assembly/disassembly must be supervised by a person who meets the criteria for both a competent person and a qualified person, or by a competent person who is assisted by one or more qualified persons.
1926.1404 Assembly/Disassembly
Hazards Related to Cranes

## Slide 26
When pins (or similar devices) are being removed, employees must not be under the boom, jib, or other components, except …
When the A/D director implements procedures that minimize the risk of unintended dangerous movement and minimize the duration and extent of exposure under the boom.
1926.1404(f) Working Under the Boom, Jib or Other
Components
Hazards Related to Cranes
Image courtesy eCLOSH. Used with permission.
Image courtesy eCLOSH. Used with permission.
Notes: This provision is conditional
“when site constraints require one or more employees to be under the boom, jib, or other components…”
IN: Top picture is incorrect AD bc worker inside boom. “Inside is suicide; outside is safe side.”
Images: (Bottom) OSHA
Top: eLCOSH

## Slide 27
Before commencing assembly/disassembly operations, the A/D director must ensure that the crew members understand all of the following:
    Their tasks.
    The hazards associated with their tasks.
    The hazardous positions/locations that they need to avoid.
1926.1404(d)(1) Crew Instructions
Hazards Related to Cranes
Notes: Make sure all of these are covered in entirety.

## Slide 28
Employer shall:
    Instruct employees in how to recognize struck-by and pinch/crush hazard areas posed by the rotating superstructure.
    Erect and maintain control lines, warning lines, railings or similar barriers to mark the boundaries of the hazard areas.
1926.1424 Work area control/Swing radius
Hazards Related to Cranes
Swing Radius Needs to Barricaded – Unsafe Condition
Worker should NEVER be in this position – Unsafe Act

## Slide 29
Exception to Positive Swing Radius: where it is not feasible to erect barriers, the hazard areas shall be clearly marked by a combination of warning signs and high visibility markings that identify the hazard areas.
Swing radius (Con’t)
Hazards Related to Cranes

## Slide 30
Swing Radius Barricades
Hazards Related to Cranes
Drop Hoop on Crane Body
Barricades Around Crane Carriage
Barricades Between Outriggers
Barricades Around Crane
Barricades Around Crane

## Slide 31
You must assume that all power lines are energized unless the utility company confirms that the power line has been de-energized and visibly grounded at the worksite.
Power Lines
Hazards Related to Cranes

## Slide 32
Clearance from Power Lines
Hazards Related to Cranes
Table A Clearance Distance
Image courtesy of TEEX. Used with permission.
Notes: IN: How do you set up? Boom + load + 20’
Graphic: TEEX

## Slide 33
Hazards Related to Cranes
OSHA V-Tool Power Line Contact Video

## Slide 34
Assembly/disassembly below power lines prohibited
Ensure that no part of the equipment, load line or load (including rigging and lifting accessories), gets closer than 20 feet to the power line.
De-energize and ground the ground the line.
1926.1407 Power Line Safety/Assembly and Disassembly (under 350 kV)
Hazards Related to Cranes

## Slide 35
The employer must make a hazard assessment and must define a work zone by demarcating boundaries.
    Option 1 – De-energize and ground the ground the line.
    Option 2 – Ensure that no part of the equipment, load line or load, gets closer than 20 feet to the power line.
    Option 3 – If line voltage is known – cannot get closer than minimum distances in Table A.
1926.1408 Operations Around Power Lines
(up to 350 kV)
Hazards Related to Cranes

## Slide 36
1926.1408 Clearance Options
Hazards Related to Cranes
Image courtesy of TEEX. Used with permission.
Notes: Graphic: TEEX

## Slide 37
Table A. Minimum Clearance Distances
Hazards Related to Cranes
Notes: Review the definition of registered professional engineer, RPE.

## Slide 38
Option 2 & 3 – Signs and/or Barriers
Hazards Related to Cranes

## Slide 39
Equipment operations in which any part of the equipment is closer than the minimum approach distance under Table A to an energized power line is prohibited, except when the following requirements are met:
    It is infeasible to do the work without breaching the minimum approach distance.
    After consultation with the utility, it is infeasible to de-energize and ground the line or relocate the line.
1926.1410 Operations Closer than the Minimum
Hazards Related to Cranes

## Slide 40
Intentionally Working Closer than Table A Zone
Hazards Related to Cranes
All of the following are required:
Power Line Owner – Sets Minimum Approach Distance
Planning Meeting – Procedures
Dedicated Spotter
Elevated Warning Line or Barricade
Insulating Link/Device
Nonconductive Rigging
Range Limiter (if Equipped)
Nonconductive Tag Line (if used)
Barricades - 10 feet from Equipment
Limit Access to Essential Employees
Ground Crane
Deactivate Automatic Re-energizer
Must Show:
Staying Outside Zone is Infeasible
Infeasible to De-energize and Ground

## Slide 41
With No Load And Boom/Mast Lowered
up to 0.75 kV 4 feet
0.75 to 50kV 6 feet
50 to 345kV 10 feet
345 to 750 kV 16 feet
750 to 1,000 kV 20 feet
Minimum Clearance Distances While Traveling - Table T
Hazards Related to Cranes

## Slide 42
A crane is like an antenna
    Can store electrical charge
Common remedies
    Synthetic web slings
    Insulating riggers and other workers
    Rubber gloves
Working Around Transmitters
Hazards Related to Cranes
Notes: When a crane is close enough to a radio, TV, or microwave transmitter the crane can act like an antenna and store up an electrical charge. The amount of charge is not large enough to injure or kill. It can cause people to jump, slip, or fall. A common remedy is to use a synthetic web sling, also commonly known as a bull tail, to insulate riggers and other workers. It is advisable for operators to wear rubber gloves when getting on and off the machine.

## Slide 43
200 foot notification FAA Form no. 7460 – 1
Working close to airport
Working close to Helipads
FAA Requirements
Hazards Related to Cranes
Notes: Image: TCS photo 3116
FAA stands for federal aviation administration.
The FAA must be notified every time a crane is over 200 ft tall. They must be notified using form no. 7460-1 30 days in advance.
When close to airports the height requirement becomes less, contact the closest FAA office for more information.

## Slide 44
Questions?
Hazards Related to Cranes