## Slide 1
Types, Components, & Crane Functionality
Oct. 2019 – Sep. 2020
Crane Management in Construction
AGC-OSHA Susan Harwood Training Grant

## Slide 2
Learn about:
Various types of cranes
Boom types and configurations
Crane operational aides
Principles of crane leverage
Objectives
Types, Components and Crane Functionality

## Slide 3
Rough Terrain
Types, Components and Crane Functionality
Rough-Terrain Crane –Stationary
Cab does not swing with boom
Rough-Terrain Crane –Swing Cab
Cab swings with boom
Notes: Rough Terrain is a poor name choice
Most likely to tip over on your job;
- High center of gravity
- Second to boom trucks in low operator experience
- Neck breaker has poor load visibility
Most likely to fail while lifting “on rubber”
Proactive, eliminate “on rubber” lifts
Image Sources: TEEX

## Slide 4
Lattice Boom Truck Crane
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Truck Crane with Lattice Truss Boom supported on Outriggers
Notes: - Popular where the crane changes jobsites frequently
- Older models lacked front OR and could not work 360 deg
- With long boom difficult to move on rough and sloping ground
- Usually has an “on rubber” chart
Not all of these machines have “pick and carry” chart
Image: Jim Goss, used with permission

## Slide 5
Crawler Cranes
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Crawler Crane with Lattice Truss Boom supported on Tracks
Notes: Not all crawlers are like this 999 - this is a huge machine and it takes up a lot of space on the job.
- Even though it has a lot of capacity, when you put in boom and reach out away from the crane the capacity goes down a lot.
High capacity is with min. boom at min. radius
Smaller models with jibs can be a big problem
Image: TEEX

## Slide 6
Boom Truck
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Boom Truck Crane with Hydraulic Boom supported on Outriggers
Notes: Where do we put the most inexperienced operators?
- These cranes are the least forgiving
- Most likely accidents will be with power lines
Lots of subs have these type of machines
Image: TEEX

## Slide 7
Barge Crane
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Crane with Lattice Truss Boom mounted on Barge
Notes: Barge cranes are covered by other rules
Image: TEEX

## Slide 8
Tower Crane
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy Bob Emmerich. Used with permission.
Stationary Tower Swing Crane with Horizontal Truss Boom
Notes: Image: Bob Emmerich

## Slide 9
Deck Crane
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
Mobile Deck Type Crane with Hydraulic Boom and Stationary Cab
Notes: This is also known as a “Shuttle Deck” or “Carry Deck”
Image: TEEX

## Slide 10
Multi-Purpose Machine
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
Image courtesy of SP Holding Group, UK. Used with permission.
Can Function as a Forklift or can also have a winch and hook to function like a crane. The machine also has the ability to swing like a crane.
Notes: 29 CFR 1926 Subpart CC - Cranes and Derricks in Construction Mr. Paul Bolon, Mr. Garvin Branch and Mr. Bruce Justh. Directorate of Construction
Chairman Stafford then directed attention to the second regulatory update issue which was minor revisions to the crane and derrick standard. Mr. Paul Bolon, Mr. Garvin Branch and Mr. Bruce Justh, Directorate of Construction came forward to facilitate the discussion. Mr. Bolon informed the attendees that it was not uncommon for OSHA to publish a notice, that is usually just a technical corrections, six months to two years after a final standard is published. Normally, it corrects grammar, bad references, misspellings and things like that. This time there are a few larger things to correct, so OSHA is calling this an "amendment to the final standard," rather than just being a technical correction. Mr. Bolon emphasized the point that OSHA will probably not do a Direct Final Rule, but do a normal proposal, have a comment period, and then have a Final Rule.
Question: Chairman Stafford - So that I understand clearly, what is the next step once OSHA gets the recommendation from ACCSH?
Answer: Mr. Bolon - Publish a proposal with these amendments.
Mr. Bolon and team went on to facilitate the following discussion on the proposed amendments:
1926 Subpart O - Motor Vehicles, Mechanized Equipment, and Marine Operations
  1926.600 - Equipment - We're substituting the word "equipment" for "crane. We tried to use the word "equipment" for crane throughout the regulatory text, because the standard covers a lot more equipment besides cranes.
    (a)(6)(i) - Substitute "equipment" for "crane or load".
    (a)(6)(ii) - Substitute "equipment" for "crane or load".
    (a)(6)(v) - Substitute "equipment" for "cranes".
    (a)(6)(vii) - Substitute "equipment" for "crane".
1926 Subpart CC - Cranes & Derricks in Construction
  1926.1400 - Scope - The material delivery exclusion is intended to apply when certain material is moved from a truck crane directly to the building. It does not apply when material on the truck crane is placed directly on the ground because that is not a construction activity in the first place. However, as now written, the exclusion could be read to apply to material delivered to the ground. The amendment would avoid that potential misreading.
    (c)(8) - Change paragraph to read: Powered industrial trucks (forklifts), unless equipped with a boom and hoist.
    (c)(17)(iii) - Change paragraph to read: The exclusion in paragraph (c)(17)(ii) of this section does not apply when:
    (c)(17)(iii)(D) - Change paragraph to read: The activity is not specifically excluded under §1400(c)(17)(ii).
Question: Mr. Pratt - Why don't we exclude forklifts completely from this standard?
Answer: Mr. Bolon - That's what was proposed, and that was the draft text that came from the Advisory Committee. But we had comments in rulemaking that persuaded OSHA that if forklifts were modified with booms and winches and wire ropes that they take on the characteristics of cranes.
Question: Mr. Stafford - So this language was adopted based on comments you received during the rulemaking process, and you're not changing the intent. You're just trying to clarify what it means with respect to forklifts?
Answer: Mr. Bolon - We're trying to eliminate any confusion. If you are using a hook under the forks, a sling or chain, and this is fairly common, that you're not under the standard. Only if you add a boom and a hoist.
Question: Mr. Stribling - Unless equipped with a boom and hoist, so it takes two specific additions to that forklift to be considered under the crane standard?
Answer: Mr. Bolon - That's right. The "and" is very important, just like the winch or hook caught us because it could just be a hook and suddenly you're a crane, and that wasn't our intent.

## Slide 11
What about this one?
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
Video of a Homemade Mobile Lifting Device
Obviously- This is totally unacceptable as a Crane

## Slide 12
Truss Boom Crawler Crane
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
Image courtesy TEEX. Used with permission.
Notes: Graphic: TEEX

## Slide 13
Truss Boom Truck Crane
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
Image courtesy TEEX. Used with permission.
Notes: Graphic: TEEX

## Slide 14
Hydraulic Boom Truck Crane
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
Image courtesy TEEX. Used with permission.
Notes: Graphic: TEEX

## Slide 15
Mobile Crane
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
Image courtesy TEEX. Used with permission.
Notes: Graphic: TEEX
IN: “Teach” also to cranes in your area—most frequently used and components

## Slide 16
Tower Crane
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
Notes: Graphic: TEEX
IN: “Teach” also to cranes in your area—most frequently used and components

## Slide 17
Booms & Jibs
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
Image courtesy TEEX. Used with permission.
Notes: Graphic: TEEX
IN: “Teach” also to cranes in your area—most frequently used and components

## Slide 18
Listed operational aids such as anti-two blocks are required on all equipment, unless otherwise specified.
Operations shall not begin unless the listed operational aids are in proper working order, except where the employer meets the specified temporary alternative measures.
If a listed operational aid stops working properly during operations, the operator shall safely stop operations until the temporary alternative measures are implemented or the device is again working properly.
1926.1416 Operational aids
Types, Components and Crane Functionality
Notes: 1926.1416 Operational aids.
(a) The devices listed in this section (“listed operational aids”) are required on all equipment covered by this subpart, unless otherwise specified.
(1) The requirements in paragraphs (e)(1), (e)(2), and (e)(3) of this section do not apply to articulating cranes.
(2) The requirements in paragraphs (d)(3), (e)(1), and (e)(4) of this section apply only to those digger derricks manufactured after November 8, 2011.
(b) Operations must not begin unless the listed operational aids are in proper working order, except where an operational aid is being repaired the employer uses the specified temporary alternative measures. The time periods permitted for repairing defective operational aids are specified in paragraphs (d) and (e) of this section. More protective alternative measures specified by the crane/derrick manufacturer, if any, must be followed.
(c) If a listed operational aid stops working properly during operations, the operator must safely stop operations until the temporary alternative measures are implemented or the device is again working properly. If a replacement part is no longer available, the use of a substitute device that performs the same type of function is permitted and is not considered a modification under § 1926.1434.

## Slide 19
Boom hoist limiting device.
Luffing jib limiting device
Anti two-blocking device.
Alternative measures OK if not working.
Must be repaired in 7 calendar days.
1926.1416 (d) Category I Operational Aides
Types, Components and Crane Functionality
Notes: (d) Category I operational aids and alternative measures. Operational aids listed in this paragraph that are not working properly must be repaired no later than 7 calendar days after the deficiency occurs. Exception: If the employer documents that it has ordered the necessary parts within 7 calendar days of the occurrence of the deficiency, the repair must be completed within 7 calendar days of receipt of the parts. See§ 1926.1417(j) for additional requirements.
(1) Boom hoist limiting device.
(i) For equipment manufactured after December 16, 1969, a boom hoist limiting device is required. Temporary alternative measures (use at least one). One or more of the following methods must be used:
(A) Use a boom angle indicator.
(B) Clearly mark the boom hoist cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to keep the boom within the minimum allowable radius. In addition, install mirrors or remote video cameras and displays if necessary for the operator to see the mark.
(C) Clearly mark the boom hoist cable (so that it can easily be seen by a spotter) at a point that will give the spotter sufficient time to signal the operator and have the operator stop the hoist to keep the boom within the minimum allowable radius.
(ii) If the equipment was manufactured on or before December 16, 1969, and is not equipped with a boom hoist limiting device, at least one of the measures in paragraphs (d)(1)(i)(A) through (C) of this section must be used.
(2) Luffing jib limiting device. Equipment with a luffing jib must have a luffing jib limiting device. Temporary alternative measures are the same as in paragraph (d)(1)(i) of this section, except to limit the movement of the luffing jib rather than the boom hoist.
(3) Anti two-blocking device.
(i) Telescopic boom cranes manufactured after February 28, 1992, must be equipped with a device which automatically prevents damage from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device(s) must prevent such damage at all points where two-blocking could occur.
Temporary alternative measures: Clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, and use a spotter when extending the boom.
(ii) Lattice boom cranes.
(A) Lattice boom cranes manufactured after Feb 28, 1992, must be equipped with a device that either automatically prevents damage and load failure from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component), or warns the operator in time for the operator to prevent two-blocking. The device must prevent such damage/failure or provide adequate warning for all points where two-blocking could occur.
(B) Lattice boom cranes and derricks manufactured after November 8, 2011 must be equipped with a device which automatically prevents damage and load failure from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device(s) must prevent such damage/failure at all points where two-blocking could occur.
(C) Exception. The requirements in paragraphs (d)(3)(ii)(A) and (B) of this section do not apply to such lattice boom equipment when used for dragline, clamshell (grapple), magnet, drop ball, container handling, concrete bucket, marine operations that do not involve hoisting personnel, and pile driving work.
(D) Temporary alternative measures. Clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, or use a spotter.
(iii) Articulating cranes manufactured after December 31, 1999, that are equipped with a load hoist must be equipped with a device that automatically prevents damage from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device must prevent such damage at all points where two-blocking could occur. Temporary alternative measures: When two-blocking could only occur with movement of the load hoist, clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, or use a spotter. When two-blocking could occur without movement of the load hoist, clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, and use a spotter when extending the boom.
(d) Category I operational aids and alternative measures. Operational aids listed in this paragraph that are not working properly must be repaired no later than 7 calendar days after the deficiency occurs. Exception: If the employer documents that it has ordered the necessary parts within 7 calendar days of the occurrence of the deficiency, the repair must be completed within 7 calendar days of receipt of the parts. See§ 1926.1417(j) for additional requirements.
(1) Boom hoist limiting device.
(i) For equipment manufactured after December 16, 1969, a boom hoist limiting device is required. Temporary alternative measures (use at least one). One or more of the following methods must be used:
(A) Use a boom angle indicator.
(B) Clearly mark the boom hoist cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to keep the boom within the minimum allowable radius. In addition, install mirrors or remote video cameras and displays if necessary for the operator to see the mark.
(C) Clearly mark the boom hoist cable (so that it can easily be seen by a spotter) at a point that will give the spotter sufficient time to signal the operator and have the operator stop the hoist to keep the boom within the minimum allowable radius.
(ii) If the equipment was manufactured on or before December 16, 1969, and is not equipped with a boom hoist limiting device, at least one of the measures in paragraphs (d)(1)(i)(A) through (C) of this section must be used.
(2) Luffing jib limiting device. Equipment with a luffing jib must have a luffing jib limiting device. Temporary alternative measures are the same as in paragraph (d)(1)(i) of this section, except to limit the movement of the luffing jib rather than the boom hoist.
(3) Anti two-blocking device.
(i) Telescopic boom cranes manufactured after February 28, 1992, must be equipped with a device which automatically prevents damage from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device(s) must prevent such damage at all points where two-blocking could occur.
Temporary alternative measures: Clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, and use a spotter when extending the boom.
(ii) Lattice boom cranes.
(A) Lattice boom cranes manufactured after Feb 28, 1992, must be equipped with a device that either automatically prevents damage and load failure from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component), or warns the operator in time for the operator to prevent two-blocking. The device must prevent such damage/failure or provide adequate warning for all points where two-blocking could occur.
(B) Lattice boom cranes and derricks manufactured after November 8, 2011 must be equipped with a device which automatically prevents damage and load failure from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device(s) must prevent such damage/failure at all points where two-blocking could occur.
(C) Exception. The requirements in paragraphs (d)(3)(ii)(A) and (B) of this section do not apply to such lattice boom equipment when used for dragline, clamshell (grapple), magnet, drop ball, container handling, concrete bucket, marine operations that do not involve hoisting personnel, and pile driving work.
(D) Temporary alternative measures. Clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, or use a spotter.
(iii) Articulating cranes manufactured after December 31, 1999, that are equipped with a load hoist must be equipped with a device that automatically prevents damage from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device must prevent such damage at all points where two-blocking could occur. Temporary alternative measures: When two-blocking could only occur with movement of the load hoist, clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, or use a spotter. When two-blocking could occur without movement of the load hoist, clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, and use a spotter when extending the boom.

## Slide 20
Examples of Temporary Alternative Measures for non-operating Anti-Two Block Device:
    Clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking,
    and use a spotter when extending the boom.
Include Alternate Methods
Types, Components and Crane Functionality

## Slide 21
Boom angle or radius indicator
Jib angle indicator if the equipment has a luffing jib
Boom length indicator if the equipment has a telescopic boom
Load weighing and similar devices.
Outrigger/stabilizer position sensor/monitor
Alternative Measures OK if not working.
Must be repaired in 30 calendar days.
Exception: unless employer has documented it ordered parts then repaired within 7 calendar days of receipt.
1926.1416 (e) Category II Operational Aides
Types, Components and Crane Functionality
Notes: (e) Category II operational aids and alternative measures. Operational aids listed in this paragraph that are not working properly must be repaired no later than 30 calendar days after the deficiency occurs. Exception: If the employer documents that it has ordered the necessary parts within 7 calendar days of the occurrence of the deficiency, and the part is not received in time to complete the repair in 30 calendar days, the repair must be completed within 7 calendar days of receipt of the parts. See§ 1926.1417(j) for additional requirements.
(1) Boom angle or radius indicator. The equipment must have a boom angle or radius indicator readable from the operator's station. Temporary alternative measures: Radii or boom angle must be determined by measuring the radii or boom angle with a measuring device.
(2) Jib angle indicator if the equipment has a luffing jib. Temporary alternative measures: Radii or jib angle must be determined by ascertaining the main boom angle and then measuring the radii or jib angle with a measuring device.
(3) Boom length indicator if the equipment has a telescopic boom, except where the rated capacity is independent of the boom length. Temporary alternative measures. One or more of the following methods must be used:
(i) Mark the boom with measured marks to calculate boom length,
(ii) Calculate boom length from boom angle and radius measurements,
(iii) Measure the boom with a measuring device.
(4) Load weighing and similar devices.
(i) Equipment (other than derricks and articulating cranes) manufactured after March 29, 2003 with a rated capacity over 6,000 pounds must have at least one of the following: load weighing device, load moment (or rated capacity) indicator, or load moment (or rated capacity) limiter. Temporary alternative measures: The weight of the load must be determined from a source recognized by the industry (such as the load's manufacturer) or by a calculation method recognized by the industry (such as calculating a steel beam from measured dimensions and a known per foot weight). This information must be provided to the operator prior to the lift.
(ii) Articulating cranes manufactured after November 8, 2011 must have at least one of the following: automatic overload prevention device, load weighing device, load moment (or rated capacity) indicator, or load moment (rated capacity) limiter. Temporary alternative measures: The weight of the load must be determined from a source recognized by the industry (such as the load's manufacturer) or by a calculation method recognized by the industry (such as calculating a steel beam from measured dimensions and a known per foot weight). This information must be provided to the operator prior to the lift.
(5) The following devices are required on equipment manufactured after November 8, 2011:
(i) Outrigger/stabilizer position (horizontal beam extension) sensor/monitor if the equipment has outriggers or stabilizers. Temporary alternative measures: The operator must verify that the position of the outriggers or stabilizers is correct (in accordance with manufacturer procedures) before beginning operations requiring outrigger or stabilizer deployment.
(ii) Hoist drum rotation indicator if the equipment has a hoist drum not visible from the operator's station. Temporary alternative measures: Mark the drum to indicate the rotation of the drum. In addition, install mirrors or remote video cameras and displays if necessary for the operator to see the mark.

## Slide 22
Boom Angle Indicator Temporary Alternative Measures:
    Radii or boom angle must be determined by measuring the radii or boom angle with a measuring device.
Jib Angle Indicator Temporary Alternative Measures:
    Radii or jib angle must be determined by ascertaining the main boom angle and then measuring the radii or jib angle with a measuring device.
Temporary Alternative Measures
Types, Components and Crane Functionality

## Slide 23
Must comply with all manufacturer procedures applicable to operation including use with attachments.
Where the manufacturer procedures are unavailable, the employer shall develop and ensure compliance with all procedures necessary for the safe operation of the equipment and attachments.
1926.1417 (a) & (b) Operations
Types, Components and Crane Functionality
Notes: 1926.1417 Operation.
(a) The employer must comply with all manufacturer procedures applicable to the operational functions of equipment, including its use with attachments.
(b) Unavailable operation procedures.
(1) Where the manufacturer procedures are unavailable, the employer must develop and ensure compliance with all procedures necessary for the safe operation of the equipment and attachments.
(2) Procedures for the operational controls must be developed by a qualified person.
(3) Procedures related to the capacity of the equipment must be developed and signed by a registered professional engineer familiar with the equipment.
(c) Accessibility of procedures.
(1) The procedures applicable to the operation of the equipment, including rated capacities (load charts), recommended operating speeds, special hazard warnings, instructions, and operator's manual, must be readily available in the cab at all times for use by the operator.
(2) Where rated capacities are available in the cab only in electronic form: In the event of a failure which makes the rated capacities inaccessible, the operator must immediately cease operations or follow safe shut-down procedures until the rated capacities (in electronic or other form) are available.
(d) The operator must not engage in any practice or activity that diverts his/her attention while actually engaged in operating the equipment, such as the use of cellular phones (other than when used for signal communications).
(e) Leaving the equipment unattended.
(1) The operator must not leave the controls while the load is suspended, except where all of the following are met:
(i) The operator remains adjacent to the equipment and is not engaged in any other duties.
(ii) The load is to be held suspended for a period of time exceeding normal lifting operations.
(iii) The competent person determines that it is safe to do so and implements measures necessary to restrain the boom hoist and telescoping, load, swing, and outrigger or stabilizer functions.
(iv) Barricades or caution lines, and notices, are erected to prevent all employees from entering the fall zone. No employees, including those listed in §§ 1926.1425(b)(1) through (3), § 1926.1425(d) or § 1926.1425(e), are permitted in the fall zone.
(2) The provisions in § 1926.1417(e)(1) do not apply to working gear (such as slings, spreader bars, ladders, and welding machines) where the weight of the working gear is negligible relative to the lifting capacity of the equipment as positioned, and the working gear is suspended over an area other than an entrance or exit.
(f) Tag-out.
(1) Tagging out of service equipment/functions. Where the employer has taken the equipment out of service, a tag must be placed in the cab stating that the equipment is out of service and is not to be used. Where the employer has taken a function(s) out of service, a tag must be placed in a conspicuous position stating that the function is out of service and is not to be used.
(2) Response to “do not operate”/tag-out signs.
(i) If there is a warning (tag-out or maintenance/do not operate) sign on the equipment or starting control, the operator must not activate the switch or start the equipment until the sign has been removed by a person authorized to remove it, or until the operator has verified that:
(A) No one is servicing, working on, or otherwise in a dangerous position on the machine.
(B) The equipment has been repaired and is working properly.
(ii) If there is a warning (tag-out or maintenance/do not operate) sign on any other switch or control, the operator must not activate that switch or control until the sign has been removed by a person authorized to remove it, or until the operator has verified that the requirements in paragraphs (f)(2)(i)(A) and (B) of this section have been met.
(g) Before starting the engine, the operator must verify that all controls are in the proper starting position and that all personnel are in the clear.
(h) Storm warning. When a local storm warning has been issued, the competent person must determine whether it is necessary to implement manufacturer recommendations for securing the equipment.
(i) [Reserved.]
(j) If equipment adjustments or repairs are necessary:
(1) The operator must, in writing, promptly inform the person designated by the employer to receive such information and, where there are successive shifts, to the next operator; and
(2) The employer must notify all affected employees, at the beginning of each shift, of the necessary adjustments or repairs and all alternative measures.
(k) Safety devices and operational aids must not be used as a substitute for the exercise of professional judgment by the operator.
(l) [Reserved.]
(m) If the competent person determines that there is a slack rope condition requiring re-spooling of the rope, it must be verified (before starting to lift) that the rope is seated on the drum and in the sheaves as the slack is removed.
(n) The competent person must adjust the equipment and/or operations to address the effect of wind, ice, and snow on equipment stability and rated capacity.
(o) Compliance with rated capacity.
(1) The equipment must not be operated in excess of its rated capacity.
(2) The operator must not be required to operate the equipment in a manner that would violate paragraph (o)(1) of this section.
(3) Load weight. The operator must verify that the load is within the rated capacity of the equipment by at least one of the following methods:
(i) The weight of the load must be determined from a source recognized by the industry (such as the load's manufacturer), or by a calculation method recognized by the industry (such as calculating a steel beam from measured dimensions and a known per foot weight), or by other equally reliable means. In addition, when requested by the operator, this information must be provided to the operator prior to the lift; or
(ii) The operator must begin hoisting the load to determine, using a load weighing device, load moment indicator, rated capacity indicator, or rated capacity limiter, if it exceeds 75 percent of the maximum rated capacity at the longest radius that will be used during the lift operation. If it does, the operator must not proceed with the lift until he/she verifies the weight of the load in accordance with paragraph (o)(3)(i) of this section.
(p) The boom or other parts of the equipment must not contact any obstruction.
(q) The equipment must not be used to drag or pull loads sideways.
(r) On wheel-mounted equipment, no loads must be lifted over the front area, except as permitted by the manufacturer.
(s) The operator must test the brakes each time a load that is 90% or more of the maximum line pull is handled by lifting the load a few inches and applying the brakes. In duty cycle and repetitive lifts where each lift is 90% or more of the maximum line pull, this requirement applies to the first lift but not to successive lifts.
(t) Neither the load nor the boom must be lowered below the point where less than two full wraps of rope remain on their respective drums.
(u) Traveling with a load.
(1) Traveling with a load is prohibited if the practice is prohibited by the manufacturer.
(2) Where traveling with a load, the employer must ensure that:
(i) A competent person supervises the operation, determines if it is necessary to reduce rated capacity, and makes determinations regarding load position, boom location, ground support, travel route, overhead obstructions, and speed of movement necessary to ensure safety.
(ii) The determinations of the competent person required in paragraph (u)(2)(i) of this section are implemented.
(iii) For equipment with tires, tire pressure specified by the manufacturer is maintained.
(v) Rotational speed of the equipment must be such that the load does not swing out beyond the radius at which it can be controlled.
(w) A tag or restraint line must be used if necessary to prevent rotation of the load that would be hazardous.
(x) The brakes must be adjusted in accordance with manufacturer procedures to prevent unintended movement.
(y) The operator must obey a stop (or emergency stop) signal, irrespective of who gives it.
(z) Swinging locomotive cranes. A locomotive crane must not be swung into a position where railway cars on an adjacent track could strike it, until it is determined that cars are not being moved on the adjacent track and that proper flag protection has been established.
(aa) Counterweight/ballast.
(1) The following applies to equipment other than tower cranes:
(i) Equipment must not be operated without the counterweight or ballast in place as specified by the manufacturer.
(ii) The maximum counterweight or ballast specified by the manufacturer for the equipment must not be exceeded.
(2) Counterweight/ballast requirements for tower cranes are specified in § 1926.1435(b)(8).

## Slide 24
Principle of Leverage
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
Image courtesy TEEX. Used with permission.
Crane = Teeter-Totter = Lever
Notes: Every object has a center of gravity. The Teetor Totter Effect describes the need to be able to balance a load
Center of Gravity (CG) = the point around which weight is evenly distributed
A crane’s center of gravity = sum of all the individual parts
Typical location is some where near counterweight
A crane is just a big expensive lever.
3 parts of a lever fulcrum and 2 arms
The crane’s center of gravity moves with every crane movement.
Image: TEEX

## Slide 25
Principles of Operation
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
Image courtesy TEEX. Used with permission.
Three Parts of a Lever
Notes: A simple lever has 3 parts;
- a resistance arm,
- a production arm, and
- a fulcrum
If you make changes to one, it will change them all
Graphic: TEEX

## Slide 26
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
Image courtesy TEEX. Used with permission.
Balanced
=
Heavy Load X Short Distance
Light Load X Long Distance
Tipping Axis
Unbalanced
Notes: Leverage = Wt X Distance
Wt = Crane Wt & Load Wt.
Distance = feet from fulcrum, not center of rotation
Crane tips when load leverage is bigger than crane leverage
Image: TEEX

## Slide 27
Crane Base Configuration
Types, Components and Crane Functionality
Image courtesy Jim Goss. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission
Image courtesy TEEX. Used with permission.
On Crawlers
On Outriggers
On Tires
Image courtesy Jim Goss. Used with permission.
Image courtesy Jim Goss. Used with permission.
Image courtesy Bob Emmrich. Used with permission.
Notes: Configuration of base determines fulcrum or tipping axis
Images: Bob Emmerich and Jim Goss

## Slide 28
Base and Capacity
Truck Cranes
    Biggest change from one quadrant to another
    Highest capacity over the rear
Crawlers
    Least change from one quadrant to another
Principles of Operation
Types, Components and Crane Functionality
Images courtesy AGC. Used with permission.
Notes: Because the center of gravity moves when a crane swings, capacity may change a lot when the boom is in different quadrants.
- The type of base the crane is on determines how much change there is from one quadrant to another.
Truck cranes usually have the biggest change from one quadrant to another, with over the rear having the highest capacity.
Crawlers usually have the least difference from quadrant to quadrant and RT hydraulics are usually in the middle.
Image – AGC

## Slide 29
Types of slings covered are those made from alloy steel chain, wire rope, metal mesh, natural or synthetic fiber rope, and synthetic web.
Rigging Equipment Slings
Types, Components and Crane Functionality
Chain
Wire rope
Metal mesh
Synthetic
Notes: 1926.251(a)(5)
Reference - Technical links page for sling safety www.osha.gov/doc/outreachtraining/htmlfiles/slings.html
This section applies to slings used in conjunction with other material handling equipment for the movement of material by hoisting, in employments covered by this part.
The types of slings covered are those made from alloy steel chain, wire rope, metal mesh, natural or synthetic fiber rope (conventional three strand construction), and synthetic web (nylon, polyester, and polypropylene).
Three types of slings are discussed in detail in this presentation: alloy steel chain, wire rope and synthetic web.

## Slide 30
Slings must have tags that indicate capacities.
Only qualified entities can “retag” slings
Sling Tags
Types, Components and Crane Functionality
Notes: All nylon and chain slings must have legible tags.
Riggers must understand wire rope sling capacities.
All riggers must know how to inspect slings and properly rigged loads.
Don’t overload the slings.

## Slide 31
Questions?
Types, Components, and Crane Functionality