## Slide 1
Crane Inspections
Oct. 2019 – Sep. 2020
Crane Management in Construction
AGC-OSHA Susan Harwood Training Grant

## Slide 2
Learn about:
Describe OSHA [post-assembly, shift, monthly, annual] crane inspection process requirements.
Examine all [post-assembly, shift, monthly, annual] inspection documentation.
Describe wire rope inspection process.
Objectives
Crane Inspections

## Slide 3
Before a Crane is Put in Services:
    Equipment that has been modified by a qualified person
    Equipment that has had a repair or adjustment shall be inspected by a qualified person.
    Equipment must be inspected after it is assembled by a qualified person.
1926.1412 Crane Inspections
Crane Inspections
Notes: 1926.1412 Inspections.
(a) Modified equipment.
(1) Equipment that has had modifications or additions which affect the safe operation of the equipment (such as modifications or additions involving a safety device or operational aid, critical part of a control system, power plant, braking system, load-sustaining structural components, load hook, or in-use operating mechanism) or capacity must be inspected by a qualified person after such modifications/additions have been completed, prior to initial use. The inspection must meet all of the following requirements:
(i) The inspection must assure that the modifications or additions have been done in accordance with the approval obtained pursuant to § 1926.1434 (Equipment modifications).
(ii) The inspection must include functional testing of the equipment.
(2) Equipment must not be used until an inspection under this paragraph demonstrates that the requirements of paragraph (a)(1)(i) of this section have been met.
(b) Repaired/adjusted equipment.
(1) Equipment that has had a repair or adjustment that relates to safe operation (such as: A repair or adjustment to a safety device or operator aid, or to a critical part of a control system, power plant, braking system, load-sustaining structural components, load hook, or in-use operating mechanism), must be inspected by a qualified person after such a repair or adjustment has been completed, prior to initial use. The inspection must meet all of the following requirements:
(i) The qualified person must determine if the repair/adjustment meets manufacturer equipment criteria (where applicable and available).
(ii) Where manufacturer equipment criteria are unavailable or inapplicable, the qualified person must:
(A) Determine if a registered professional engineer (RPE) is needed to develop criteria for the repair/adjustment. If an RPE is not needed, the employer must ensure that the criteria are developed by the qualified person. If an RPE is needed, the employer must ensure that they are developed by an RPE.
(B) Determine if the repair/adjustment meets the criteria developed in accordance with paragraph (b)(1)(ii)(A) of this section.
(iii) The inspection must include functional testing of the repaired/adjusted parts and other components that may be affected by the repair/adjustment.
(4) Equipment must not be used until an inspection under this paragraph demonstrates that the repair/adjustment meets the requirements of paragraph (b)(1)(i) of this section (or, where applicable, paragraph (b)(1)(ii) of this section).
(c) Post-assembly.
(1) Upon completion of assembly, the equipment must be inspected by a qualified person to assure that it is configured in accordance with manufacturer equipment criteria.
(2) Where manufacturer equipment criteria are unavailable, a qualified person must:
(i) Determine if a registered professional engineer (RPE) familiar with the type of equipment involved is needed to develop criteria for the equipment configuration. If an RPE is not needed, the employer must ensure that the criteria are developed by the qualified person. If an RPE is needed, the employer must ensure that they are developed by an RPE.
(ii) Determine if the equipment meets the criteria developed in accordance with paragraph (c)(2)(i) of this section.
(3) Equipment must not be used until an inspection under this paragraph demonstrates that the equipment is configured in accordance with the applicable criteria.
(d) Each shift.
(1) A competent person must begin a visual inspection prior to each shift the equipment will be used, which must be completed before or during that shift. The inspection must consist of observation for apparent deficiencies. Taking apart equipment components and booming down is not required as part of this inspection unless the results of the visual inspection or trial operation indicate that further investigation necessitating taking apart equipment components or booming down is needed. Determinations made in conducting the inspection must be reassessed in light of observations made during operation. At a minimum the inspection must include all of the following:
(i) Control mechanisms for maladjustments interfering with proper operation.
(ii) Control and drive mechanisms for apparent excessive wear of components and contamination by lubricants, water or other foreign matter.
(iii) Air, hydraulic, and other pressurized lines for deterioration or leakage, particularly those which flex in normal operation.
(iv) Hydraulic system for proper fluid level.
(v) Hooks and latches for deformation, cracks, excessive wear, or damage such as from chemicals or heat.
(vi) Wire rope reeving for compliance with the manufacturer's specifications.
(vii) Wire rope, in accordance with § 1926.1413(a).
(viii) Electrical apparatus for malfunctioning, signs of apparent excessive deterioration, dirt or moisture accumulation.
(ix) Tires (when in use) for proper inflation and condition.
(x) Ground conditions around the equipment for proper support, including ground settling under and around outriggers/stabilizers and supporting foundations, ground water accumulation, or similar conditions. This paragraph does not apply to the inspection of ground conditions for railroad tracks and their underlying support when the railroad tracks are part of the general railroad system of transportation that is regulated pursuant to the Federal Railroad Administration under 49 CFR part 213.
(xi) The equipment for level position within the tolerances specified by the equipment manufacturer's recommendations, both before each shift and after each move and setup.
(xii) Operator cab windows for significant cracks, breaks, or other deficiencies that would hamper the operator's view.
(xiii) Rails, rail stops, rail clamps and supporting surfaces when the equipment has rail traveling. This paragraph does not apply to the inspection of rails, rail stops, rail clamps and supporting surfaces when the railroad tracks are part of the general railroad system of transportation that is regulated pursuant to the Federal Railroad Administration under 49 CFR part 213.
(xiv) Safety devices and operational aids for proper operation.
(2) If any deficiency in paragraphs (d)(1)(i) through (xiii) of this section (or in additional inspection items required to be checked for specific types of equipment in accordance with other sections of this standard) is identified, an immediate determination must be made by the competent person as to whether the deficiency constitutes a safety hazard. If the deficiency is determined to constitute a safety hazard, the equipment must be taken out of service until it has been corrected. See§ 1926.1417.
(3) If any deficiency in paragraph (d)(1)(xiv) of this section (safety devices/operational aids) is identified, the action specified in § 1926.1415 and § 1926.1416 must be taken prior to using the equipment.
(e) Monthly.
(1) Each month the equipment is in service it must be inspected in accordance with paragraph (d) of this section (each shift).
(2) Equipment must not be used until an inspection under this paragraph demonstrates that no corrective action under paragraphs (d)(2) and (3) of this section is required.

## Slide 4
    Shift
      By Competent Person
      Started before start of shift
    Monthly
      By Competent Person
      Documented and retained 3 months
    Annual/Comprehensive Inspections
      By Qualified Person
      Documented and Retained
1926.1412 Crane Inspections
Crane Inspections
Notes: (d) Each shift.
(1) A competent person must begin a visual inspection prior to each shift the equipment will be used, which must be completed before or during that shift. The inspection must consist of observation for apparent deficiencies. Taking apart equipment components and booming down is not required as part of this inspection unless the results of the visual inspection or trial operation indicate that further investigation necessitating taking apart equipment components or booming down is needed. Determinations made in conducting the inspection must be reassessed in light of observations made during operation. At a minimum the inspection must include all of the following:
(i) Control mechanisms for maladjustments interfering with proper operation.
(ii) Control and drive mechanisms for apparent excessive wear of components and contamination by lubricants, water or other foreign matter.
(iii) Air, hydraulic, and other pressurized lines for deterioration or leakage, particularly those which flex in normal operation.
(iv) Hydraulic system for proper fluid level.
(v) Hooks and latches for deformation, cracks, excessive wear, or damage such as from chemicals or heat.
(vi) Wire rope reeving for compliance with the manufacturer's specifications.
(vii) Wire rope, in accordance with § 1926.1413(a).
(viii) Electrical apparatus for malfunctioning, signs of apparent excessive deterioration, dirt or moisture accumulation.
(ix) Tires (when in use) for proper inflation and condition.
(x) Ground conditions around the equipment for proper support, including ground settling under and around outriggers/stabilizers and supporting foundations, ground water accumulation, or similar conditions. This paragraph does not apply to the inspection of ground conditions for railroad tracks and their underlying support when the railroad tracks are part of the general railroad system of transportation that is regulated pursuant to the Federal Railroad Administration under 49 CFR part 213.
(xi) The equipment for level position within the tolerances specified by the equipment manufacturer's recommendations, both before each shift and after each move and setup.
(xii) Operator cab windows for significant cracks, breaks, or other deficiencies that would hamper the operator's view.
(xiii) Rails, rail stops, rail clamps and supporting surfaces when the equipment has rail traveling. This paragraph does not apply to the inspection of rails, rail stops, rail clamps and supporting surfaces when the railroad tracks are part of the general railroad system of transportation that is regulated pursuant to the Federal Railroad Administration under 49 CFR part 213.
(xiv) Safety devices and operational aids for proper operation.
(2) If any deficiency in paragraphs (d)(1)(i) through (xiii) of this section (or in additional inspection items required to be checked for specific types of equipment in accordance with other sections of this standard) is identified, an immediate determination must be made by the competent person as to whether the deficiency constitutes a safety hazard. If the deficiency is determined to constitute a safety hazard, the equipment must be taken out of service until it has been corrected. See§ 1926.1417.
(3) If any deficiency in paragraph (d)(1)(xiv) of this section (safety devices/operational aids) is identified, the action specified in § 1926.1415 and § 1926.1416 must be taken prior to using the equipment.
(e) Monthly.
(1) Each month the equipment is in service it must be inspected in accordance with paragraph (d) of this section (each shift).
(2) Equipment must not be used until an inspection under this paragraph demonstrates that no corrective action under paragraphs (d)(2) and (3) of this section is required.
(3) Documentation.
(i) The following information must be documented and maintained by the employer that conducts the inspection:
(A) The items checked and the results of the inspection.
(B) The name and signature of the person who conducted the inspection and the date.
(ii) This document must be retained for a minimum of three months.
(f) Annual/comprehensive.
(1) At least every 12 months the equipment must be inspected by a qualified person in accordance with paragraph (d) of this section (each shift) except that the corrective action set forth in paragraphs (f)(4), (f)(5), and (f)(6) of this section must apply in place of the corrective action required by paragraphs (d)(2) and (d)(3) of this section.
(2) In addition, at least every 12 months, the equipment must be inspected by a qualified person. Disassembly is required, as necessary, to complete the inspection. The equipment must be inspected for all of the following:
(i) Equipment structure (including the boom and, if equipped, the jib):
(A) Structural members: Deformed, cracked, or significantly corroded.
(B) Bolts, rivets and other fasteners: loose, failed or significantly corroded.
(C) Welds for cracks.
(ii) Sheaves and drums for cracks or significant wear.
(iii) Parts such as pins, bearings, shafts, gears, rollers and locking devices for distortion, cracks or significant wear.
(iv) Brake and clutch system parts, linings, pawls and ratchets for excessive wear.
(v) Safety devices and operational aids for proper operation (including significant inaccuracies).
(vi) Gasoline, diesel, electric, or other power plants for safety-related problems (such as leaking exhaust and emergency shut-down feature) and conditions, and proper operation.
(vii) Chains and chain drive sprockets for excessive wear of sprockets and excessive chain stretch.
(viii) Travel steering, brakes, and locking devices, for proper operation.
(ix) Tires for damage or excessive wear.
(x) Hydraulic, pneumatic and other pressurized hoses, fittings and tubing, as follows:
(A) Flexible hose or its junction with the fittings for indications of leaks.
(B) Threaded or clamped joints for leaks.
(C) Outer covering of the hose for blistering, abnormal deformation or other signs of failure/impending failure.
(D) Outer surface of a hose, rigid tube, or fitting for indications of excessive abrasion or scrubbing.
(xi) Hydraulic and pneumatic pumps and motors, as follows:
(A) Performance indicators: Unusual noises or vibration, low operating speed, excessive heating of the fluid, low pressure.
(B) Loose bolts or fasteners.
(C) Shaft seals and joints between pump sections for leaks.
(xii) Hydraulic and pneumatic valves, as follows:
(A) Spools: Sticking, improper return to neutral, and leaks.
(B) Leaks.
(C) Valve housing cracks.
(D) Relief valves: Failure to reach correct pressure (if there is a manufacturer procedure for checking pressure, it must be followed).
(xiii) Hydraulic and pneumatic cylinders, as follows:
(A) Drifting caused by fluid leaking across the piston.
(B) Rod seals and welded joints for leaks.
(C) Cylinder rods for scores, nicks, or dents.
(D) Case (barrel) for significant dents.
(E) Rod eyes and connecting joints: Loose or deformed.
(xiv) Outrigger or stabilizer pads/floats for excessive wear or cracks.
(xv) Slider pads for excessive wear or cracks.
(xvi) Electrical components and wiring for cracked or split insulation and loose or corroded terminations.
(xvii) Warning labels and decals originally supplied with the equipment by the manufacturer or otherwise required under this standard: Missing or unreadable.
(xviii) Originally equipped operator seat (or equivalent): Missing.
(xix) Operator seat: Unserviceable.
(xx) Originally equipped steps, ladders, handrails, guards: Missing.
(xxi) Steps, ladders, handrails, guards: In unusable/unsafe condition.
(3) This inspection must include functional testing to determine that the equipment as configured in the inspection is functioning properly.
(4) If any deficiency is identified, an immediate determination must be made by the qualified person as to whether the deficiency constitutes a safety hazard or, though not yet a safety hazard, needs to be monitored in the monthly inspections.
(5) If the qualified person determines that a deficiency is a safety hazard, the equipment must be taken out of service until it has been corrected, except when temporary alternative measures are implemented as specified in § 1926.1416(d) or § 1926.1435(e). See§ 1926.1417.
(6) If the qualified person determines that, though not presently a safety hazard, the deficiency needs to be monitored, the employer must ensure that the deficiency is checked in the monthly inspections.
(7) Documentation of annual/comprehensive inspection. The following information must be documented, maintained, and retained for a minimum of 12 months, by the employer that conducts the inspection:
(i) The items checked and the results of the inspection.
(ii) The name and signature of the person who conducted the inspection and the date.
(g) Severe service. Where the severity of use/conditions is such that there is a reasonable probability of damage or excessive wear (such as loading that may have exceeded rated capacity, shock loading that may have exceeded rated capacity, prolonged exposure to a corrosive atmosphere), the employer must stop using the equipment and a qualified person must:
(1) Inspect the equipment for structural damage to determine if the equipment can continue to be used safely.
(2) In light of the use/conditions determine whether any items/conditions listed in paragraph (f) of this section need to be inspected; if so, the qualified person must inspect those items/conditions.
(3) If a deficiency is found, the employer must follow the requirements in paragraphs (f)(4) through (6) of this section.
(h) Equipment not in regular use. Equipment that has been idle for 3 months or more must be inspected by a qualified person in accordance with the requirements of paragraph (e) (Monthly) of this section before initial use.
(i) [Reserved.]
(j) Any part of a manufacturer's procedures regarding inspections that relate to safe operation (such as to a safety device or operational aid, critical part of a control system, power plant, braking system, load-sustaining structural components, load hook, or in-use operating mechanism) that is more comprehensive or has a more frequent schedule of inspection than the requirements of this section must be followed.
(k) All documents produced under this section must be available, during the applicable document retention period, to all persons who conduct inspections under this section.

## Slide 5
Before each tower crane component is erected, it must be inspected by a qualified person for damage or excessive wear.
The qualified person must pay particular attention to components that will be difficult to inspect thoroughly during shift inspections.
If the qualified person determines that a component is damaged or worn to the extent that it would create a safety hazard if used on the crane, that component must not be erected on the crane unless it is repaired and, upon re-inspection by the qualified person, found to no longer create a safety hazard..
1926.1435(f)(2) Tower Crane Pre-Erection Inspection
Crane Inspections
Notes: (f) Inspections.
(1) Section 1926.1412 (Inspections) applies to tower cranes, except that the term “assembly” is replaced by “erection.” Section 1926.1413 (Wire rope—inspection) applies to tower cranes.
(2) Pre-erection inspection. Before each crane component is erected, it must be inspected by a qualified person for damage or excessive wear.
(i) The qualified person must pay particular attention to components that will be difficult to inspect thoroughly during shift inspections.
(ii) If the qualified person determines that a component is damaged or worn to the extent that it would create a safety hazard if used on the crane, that component must not be erected on the crane unless it is repaired and, upon reinspection by the qualified person, found to no longer create a safety hazard.
(iii) If the qualified person determines that, though not presently a safety hazard, the component needs to be monitored, the employer must ensure that the component is checked in the monthly inspections. Any such determination must be documented, and the documentation must be available to any individual who conducts a monthly inspection.
(3) Post-erection inspection. In addition to the requirements in § 1926.1412(c), the following requirements must be met:
(i) A load test using certified weights, or scaled weights using a certified scale with a current certificate of calibration, must be conducted after each erection.
(ii) The load test must be conducted in accordance with the manufacturer's instructions when available. Where these instructions are unavailable, the test must be conducted in accordance with written load test procedures developed by a registered professional engineer familiar with the type of equipment involved.
(4) Monthly. The following additional items must be included:
(i) Tower (mast) bolts and other structural bolts (for loose or dislodged condition) from the base of the tower crane up or, if the crane is tied to or braced by the structure, those above the upper-most brace support.
(ii) The upper-most tie-in, braces, floor supports and floor wedges where the tower crane is supported by the structure, for loose or dislodged components.
(5) Annual. In addition to the items that must be inspected under § 1926.1412(f), all turntable and tower bolts must be inspected for proper condition and torque.

## Slide 6
A load test using certified weights, or scaled weights using a certified scale with a current certificate of calibration, must be conducted after each erection.
The load test must be conducted in accordance with the manufacturer’s instructions when available.
1926.1435(f)(3) Post-Erection Inspection
Crane Inspections

## Slide 7
Operations shall not begin unless the safety devices are in proper working order.
If a device stops working properly during operations, the operator shall safely stop operations.
Operations shall not resume until the device is again working properly. Alternative measures are not permitted to be used.
Stop Operations
Crane Inspections
Notes: 1926.1415 Safety devices.
(a) Safety devices. The following safety devices are required on all equipment covered by this subpart, unless otherwise specified:
(1) Crane level indicator.
(i) The equipment must have a crane level indicator that is either built into the equipment or is available on the equipment.
(ii) If a built-in crane level indicator is not working properly, it must be tagged-out or removed. If a removable crane level indicator is not working properly, it must be removed.
(iii) This requirement does not apply to portal cranes, derricks, floating cranes/derricks and land cranes/derricks on barges, pontoons, vessels or other means of flotation.
(2) Boom stops, except for derricks and hydraulic booms.
(3) Jib stops (if a jib is attached), except for derricks.
(4) Equipment with foot pedal brakes must have locks.
(5) Hydraulic outrigger jacks and hydraulic stabilizer jacks must have an integral holding device/check valve.
(6) Equipment on rails must have rail clamps and rail stops, except for portal cranes.
(7) Horn
(i) The equipment must have a horn that is either built into the equipment or is on the equipment and immediately available to the operator.
(ii) If a built-in horn is not working properly, it must be tagged-out or removed. If a removable horn is not working properly, it must be removed.
(b) Proper operation required. Operations must not begin unless all of the devices listed in this section are in proper working order. If a device stops working properly during operations, the operator must safely stop operations. If any of the devices listed in this section are not in proper working order, the equipment must be taken out of service and operations must not resume until the device is again working properly. See§ 1926.1417 (Operation). Alternative measures are not permitted to be used.

## Slide 8
A competent person shall begin a visual inspection prior to each shift, which shall be completed before or during that shift.
If any deficiency is identified, that constitutes a safety hazard, the equipment must be taken out of service until it has been corrected.
1926.1402(d) Shift Inspection
Crane Inspections

## Slide 9
1926.1415 (a) Safety devices. The following safety devices are required on all equipment covered by this subpart, unless otherwise specified:
Crane level indicator.
Boom stops, except for derricks and hydraulic booms.
Jib stops (if a jib is attached), except for derricks.
Equipment with foot pedal brakes must have locks.
Hydraulic outrigger jacks and hydraulic stabilizer jacks must have an integral holding device/check valve.
Equipment on rails must have rail clamps and rail stops, except for portal cranes.
Horn
Safety Devices That MUST Function
Crane Inspections
Notes: 1926.1415 Safety devices.
(a) Safety devices. The following safety devices are required on all equipment covered by this subpart, unless otherwise specified:
(1) Crane level indicator.
(i) The equipment must have a crane level indicator that is either built into the equipment or is available on the equipment.
(ii) If a built-in crane level indicator is not working properly, it must be tagged-out or removed. If a removable crane level indicator is not working properly, it must be removed.
(iii) This requirement does not apply to portal cranes, derricks, floating cranes/derricks and land cranes/derricks on barges, pontoons, vessels or other means of flotation.
(2) Boom stops, except for derricks and hydraulic booms.
(3) Jib stops (if a jib is attached), except for derricks.
(4) Equipment with foot pedal brakes must have locks.
(5) Hydraulic outrigger jacks and hydraulic stabilizer jacks must have an integral holding device/check valve.
(6) Equipment on rails must have rail clamps and rail stops, except for portal cranes.
(7) Horn
(i) The equipment must have a horn that is either built into the equipment or is on the equipment and immediately available to the operator.
(ii) If a built-in horn is not working properly, it must be tagged-out or removed. If a removable horn is not working properly, it must be removed.
(b) Proper operation required. Operations must not begin unless all of the devices listed in this section are in proper working order. If a device stops working properly during operations, the operator must safely stop operations. If any of the devices listed in this section are not in proper working order, the equipment must be taken out of service and operations must not resume until the device is again working properly. See§ 1926.1417 (Operation). Alternative measures are not permitted to be used.

## Slide 10
The operator must be able to perform a visual inspection looking for deficiencies including:
If any deficiency is identified, that constitutes a safety hazard, the equipment must be taken out of service until it has been corrected.
1926.1402(d) Shift Inspection
Crane Inspections
  Control mechanisms.
  Control and drive.
  Air, hydraulic, and other pressurized lines.
  Hydraulic system for proper fluid level.
  Hooks and latches.
  Wire rope reeving.
  Wire rope.
  Electrical apparatus.
  Tires for proper inflation and condition.
  Ground conditions.
  The equipment for level position.
  Operator cab glass
  Safety devices
  Operational aids for proper operation.

## Slide 11
Each month the equipment is in service it shall be inspected by a competent person.
The inspection must be documented and maintained by the employer for a minimum of three months.
1926.1412(e) Monthly Inspections
Crane Inspections

## Slide 12
At least every 12 months the equipment shall be inspected by a qualified person
The following must be documented and retained for a minimum of 12 months.
1926.1412(f) Annual/Comprehensive Inspection
Crane Inspections

## Slide 13
All inspection documentation required by this standard must be available to all inspectors performing required inspections (including wire rope inspections).
All inspection documentation should be in cab of crane, available to operator.
Inspection Documentation
Crane Inspections
Notes: All inspection documentation should be in cab of crane available to operator (it is not an OSHA requirement)
All inspection documentation must be retained for a minimum of three months for monthly inspections and twelve months for annual inspections.

## Slide 14
Date of Inspection
Signature of Person Conducting Inspection
Serial Number or Other Identifier
Crane Inspection Records
Crane Inspections

## Slide 15
Selection of replacement wire rope shall be in accordance with the requirements recommendations of the wire rope manufacturer, the equipment manufacturer, or a qualified person
1926.1413 Wire Rope – Inspection & Selection
Crane Inspections

## Slide 16
Daily (Shift) – No Documentation
    Untwisting (opening) of wire rope or booming down is not required as part of this inspection.
Monthly – Documented
Annual – Documented
Category I, II, or III Deficiencies
1926.1414 Wire Rope Inspection
Crane Inspections

## Slide 17
Significant distortion of the wire rope structure such as kinking, crushing, unstranding, birdcaging, signs of core failure or steel core protrusion between the outer strands.
Significant corrosion.
Electric arc damage (non-power line)or heat damage.
Improperly applied end connections.
Significantly corroded, cracked, bent, or worn end connections, etc.
Wire Rope Deficiency Category I
Crane Inspections

## Slide 18
Visible broken wires, as follows:
    In running wire ropes: Six randomly distributed broken wires in one rope lay or three broken wires in one strand in one rope lay, where a rope lay is the length along the rope in which one strand makes a complete revolution around the rope.
In rotation resistant ropes: Two randomly distributed broken wires in six rope diameters or four randomly distributed broken wires in 30 rope diameters.
In pendants or standing wire ropes: More than two broken wires in one rope lay located in rope beyond end connections and/or more than one broken wire in a rope lay located at an end connection.
A diameter reduction of more than 5% from nominal diameter.
Wire Rope Deficiencies Category II
Crane Inspections

## Slide 19
In rotation resistant wire rope, core protrusion or other distortion indicating core failure.
Prior electrical contact with a power line.
A broken strand.
Wire Rope Deficiencies Category III
Crane Inspections

## Slide 20
Replacement of the wire rope, or
The wire rope is severed at the bad spot, or
Exceptions
    Category I - An immediate determination is made by the qualified person that it does NOT constitute a safety hazard.
    Category II - Comply with the wire rope manufacturer's criterion for removal from service or criterion approved by manufacturer
    Category III – No Exception
1926.1413(a)(4) Use of Damaged Wire Rope Prohibited
Crane Inspections

## Slide 21
These safety devices are required on equipment
Crane level indicator.
Boom stops, except for derricks and hydraulic booms.
Jib stops (if a jib is attached), except for derricks.
Equipment with foot pedal brakes shall have locks, except for portal cranes and floating cranes.
Hydraulic outrigger jacks shall have an integral holding device/check valve.
Equipment on rails shall have rail clamps and rail stops.
Horn
1926.1415 Safety Devices
Crane Inspections

## Slide 22
Listed operational aids such as anti-two blocks are required on all equipment, unless otherwise specified.
Operations shall not begin unless the listed operational aids are in proper working order, except where the employer meets the specified temporary alternative measures.
If a listed operational aid stops working properly during operations, the operator shall safely stop operations until the temporary alternative measures are implemented or the device is again working properly.
1926.1416 Operational Aids
Crane Inspections

## Slide 23
Boom hoist limiting device.
Luffing jib limiting device.
Anti two-blocking device.
Alternative measures
Must be repaired in 7 calendar days.
1926.1426(d) Category I Operational Aides
Crane Inspections
Notes: 1926.1416 Operational aids.
(a) The devices listed in this section (“listed operational aids”) are required on all equipment covered by this subpart, unless otherwise specified.
(1) The requirements in paragraphs (e)(1), (e)(2), and (e)(3) of this section do not apply to articulating cranes.
(2) The requirements in paragraphs (d)(3), (e)(1), and (e)(4) of this section apply only to those digger derricks manufactured after November 8, 2011.
(b) Operations must not begin unless the listed operational aids are in proper working order, except where an operational aid is being repaired the employer uses the specified temporary alternative measures. The time periods permitted for repairing defective operational aids are specified in paragraphs (d) and (e) of this section. More protective alternative measures specified by the crane/derrick manufacturer, if any, must be followed.
(c) If a listed operational aid stops working properly during operations, the operator must safely stop operations until the temporary alternative measures are implemented or the device is again working properly. If a replacement part is no longer available, the use of a substitute device that performs the same type of function is permitted and is not considered a modification under § 1926.1434.
(d) Category I operational aids and alternative measures. Operational aids listed in this paragraph that are not working properly must be repaired no later than 7 calendar days after the deficiency occurs. Exception: If the employer documents that it has ordered the necessary parts within 7 calendar days of the occurrence of the deficiency, the repair must be completed within 7 calendar days of receipt of the parts. See§ 1926.1417(j) for additional requirements.
(1) Boom hoist limiting device.
(i) For equipment manufactured after December 16, 1969, a boom hoist limiting device is required. Temporary alternative measures (use at least one). One or more of the following methods must be used:
(A) Use a boom angle indicator.
(B) Clearly mark the boom hoist cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to keep the boom within the minimum allowable radius. In addition, install mirrors or remote video cameras and displays if necessary for the operator to see the mark.
(C) Clearly mark the boom hoist cable (so that it can easily be seen by a spotter) at a point that will give the spotter sufficient time to signal the operator and have the operator stop the hoist to keep the boom within the minimum allowable radius.
(ii) If the equipment was manufactured on or before December 16, 1969, and is not equipped with a boom hoist limiting device, at least one of the measures in paragraphs (d)(1)(i)(A) through (C) of this section must be used.
(2) Luffing jib limiting device. Equipment with a luffing jib must have a luffing jib limiting device. Temporary alternative measures are the same as in paragraph (d)(1)(i) of this section, except to limit the movement of the luffing jib rather than the boom hoist.
(3) Anti two-blocking device.
(i) Telescopic boom cranes manufactured after February 28, 1992, must be equipped with a device which automatically prevents damage from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device(s) must prevent such damage at all points where two-blocking could occur.
Temporary alternative measures: Clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, and use a spotter when extending the boom.
(ii) Lattice boom cranes.
(A) Lattice boom cranes manufactured after Feb 28, 1992, must be equipped with a device that either automatically prevents damage and load failure from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component), or warns the operator in time for the operator to prevent two-blocking. The device must prevent such damage/failure or provide adequate warning for all points where two-blocking could occur.
(B) Lattice boom cranes and derricks manufactured after November 8, 2011 must be equipped with a device which automatically prevents damage and load failure from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device(s) must prevent such damage/failure at all points where two-blocking could occur.
(C) Exception. The requirements in paragraphs (d)(3)(ii)(A) and (B) of this section do not apply to such lattice boom equipment when used for dragline, clamshell (grapple), magnet, drop ball, container handling, concrete bucket, marine operations that do not involve hoisting personnel, and pile driving work.
(D) Temporary alternative measures. Clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, or use a spotter.
(iii) Articulating cranes manufactured after December 31, 1999, that are equipped with a load hoist must be equipped with a device that automatically prevents damage from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device must prevent such damage at all points where two-blocking could occur. Temporary alternative measures: When two-blocking could only occur with movement of the load hoist, clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, or use a spotter. When two-blocking could occur without movement of the load hoist, clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, and use a spotter when extending the boom.

## Slide 24
Anti-Two Block Devices
Crane Inspections
Usually a weight hanging from the top of a boom that the running rope (load line) runs through. If the ball or block hits and raises the weight it cuts out the boom hoist so that the ball or block does not contact the upper shieves.
Notes: 1926.1416 Operational aids.
(a) The devices listed in this section (“listed operational aids”) are required on all equipment covered by this subpart, unless otherwise specified.
(1) The requirements in paragraphs (e)(1), (e)(2), and (e)(3) of this section do not apply to articulating cranes.
(2) The requirements in paragraphs (d)(3), (e)(1), and (e)(4) of this section apply only to those digger derricks manufactured after November 8, 2011.
(b) Operations must not begin unless the listed operational aids are in proper working order, except where an operational aid is being repaired the employer uses the specified temporary alternative measures. The time periods permitted for repairing defective operational aids are specified in paragraphs (d) and (e) of this section. More protective alternative measures specified by the crane/derrick manufacturer, if any, must be followed.
(c) If a listed operational aid stops working properly during operations, the operator must safely stop operations until the temporary alternative measures are implemented or the device is again working properly. If a replacement part is no longer available, the use of a substitute device that performs the same type of function is permitted and is not considered a modification under § 1926.1434.
(d) Category I operational aids and alternative measures. Operational aids listed in this paragraph that are not working properly must be repaired no later than 7 calendar days after the deficiency occurs. Exception: If the employer documents that it has ordered the necessary parts within 7 calendar days of the occurrence of the deficiency, the repair must be completed within 7 calendar days of receipt of the parts. See§ 1926.1417(j) for additional requirements.
(1) Boom hoist limiting device.
(i) For equipment manufactured after December 16, 1969, a boom hoist limiting device is required. Temporary alternative measures (use at least one). One or more of the following methods must be used:
(A) Use a boom angle indicator.
(B) Clearly mark the boom hoist cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to keep the boom within the minimum allowable radius. In addition, install mirrors or remote video cameras and displays if necessary for the operator to see the mark.
(C) Clearly mark the boom hoist cable (so that it can easily be seen by a spotter) at a point that will give the spotter sufficient time to signal the operator and have the operator stop the hoist to keep the boom within the minimum allowable radius.
(ii) If the equipment was manufactured on or before December 16, 1969, and is not equipped with a boom hoist limiting device, at least one of the measures in paragraphs (d)(1)(i)(A) through (C) of this section must be used.
(2) Luffing jib limiting device. Equipment with a luffing jib must have a luffing jib limiting device. Temporary alternative measures are the same as in paragraph (d)(1)(i) of this section, except to limit the movement of the luffing jib rather than the boom hoist.
(3) Anti two-blocking device.
(i) Telescopic boom cranes manufactured after February 28, 1992, must be equipped with a device which automatically prevents damage from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device(s) must prevent such damage at all points where two-blocking could occur.
Temporary alternative measures: Clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, and use a spotter when extending the boom.
(ii) Lattice boom cranes.
(A) Lattice boom cranes manufactured after Feb 28, 1992, must be equipped with a device that either automatically prevents damage and load failure from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component), or warns the operator in time for the operator to prevent two-blocking. The device must prevent such damage/failure or provide adequate warning for all points where two-blocking could occur.
(B) Lattice boom cranes and derricks manufactured after November 8, 2011 must be equipped with a device which automatically prevents damage and load failure from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device(s) must prevent such damage/failure at all points where two-blocking could occur.
(C) Exception. The requirements in paragraphs (d)(3)(ii)(A) and (B) of this section do not apply to such lattice boom equipment when used for dragline, clamshell (grapple), magnet, drop ball, container handling, concrete bucket, marine operations that do not involve hoisting personnel, and pile driving work.
(D) Temporary alternative measures. Clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, or use a spotter.
(iii) Articulating cranes manufactured after December 31, 1999, that are equipped with a load hoist must be equipped with a device that automatically prevents damage from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device must prevent such damage at all points where two-blocking could occur. Temporary alternative measures: When two-blocking could only occur with movement of the load hoist, clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, or use a spotter. When two-blocking could occur without movement of the load hoist, clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, and use a spotter when extending the boom.

## Slide 25
Boom angle or radius indicator
Jib angle indicator if the equipment has a luffing jib
Boom length indicator if the equipment has a telescopic boom
Load weighing and similar devices.
Outrigger/stabilizer position sensor/monitor - Cranes Manufactured After 11/8/2011
Alternative Measures
Must be repaired in 30 calendar days.
Exception: unless employer has documented it ordered parts then repaired within 7 calendar days of receipt.
1926.1426(e) Category II Operational Aides
Crane Inspections
Notes: 1926.1416 Operational aids.
(a) The devices listed in this section (“listed operational aids”) are required on all equipment covered by this subpart, unless otherwise specified.
(1) The requirements in paragraphs (e)(1), (e)(2), and (e)(3) of this section do not apply to articulating cranes.
(2) The requirements in paragraphs (d)(3), (e)(1), and (e)(4) of this section apply only to those digger derricks manufactured after November 8, 2011.
(b) Operations must not begin unless the listed operational aids are in proper working order, except where an operational aid is being repaired the employer uses the specified temporary alternative measures. The time periods permitted for repairing defective operational aids are specified in paragraphs (d) and (e) of this section. More protective alternative measures specified by the crane/derrick manufacturer, if any, must be followed.
(c) If a listed operational aid stops working properly during operations, the operator must safely stop operations until the temporary alternative measures are implemented or the device is again working properly. If a replacement part is no longer available, the use of a substitute device that performs the same type of function is permitted and is not considered a modification under § 1926.1434.
(d) Category I operational aids and alternative measures. Operational aids listed in this paragraph that are not working properly must be repaired no later than 7 calendar days after the deficiency occurs. Exception: If the employer documents that it has ordered the necessary parts within 7 calendar days of the occurrence of the deficiency, the repair must be completed within 7 calendar days of receipt of the parts. See§ 1926.1417(j) for additional requirements.
(1) Boom hoist limiting device.
(i) For equipment manufactured after December 16, 1969, a boom hoist limiting device is required. Temporary alternative measures (use at least one). One or more of the following methods must be used:
(A) Use a boom angle indicator.
(B) Clearly mark the boom hoist cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to keep the boom within the minimum allowable radius. In addition, install mirrors or remote video cameras and displays if necessary for the operator to see the mark.
(C) Clearly mark the boom hoist cable (so that it can easily be seen by a spotter) at a point that will give the spotter sufficient time to signal the operator and have the operator stop the hoist to keep the boom within the minimum allowable radius.
(ii) If the equipment was manufactured on or before December 16, 1969, and is not equipped with a boom hoist limiting device, at least one of the measures in paragraphs (d)(1)(i)(A) through (C) of this section must be used.
(2) Luffing jib limiting device. Equipment with a luffing jib must have a luffing jib limiting device. Temporary alternative measures are the same as in paragraph (d)(1)(i) of this section, except to limit the movement of the luffing jib rather than the boom hoist.
(3) Anti two-blocking device.
(i) Telescopic boom cranes manufactured after February 28, 1992, must be equipped with a device which automatically prevents damage from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device(s) must prevent such damage at all points where two-blocking could occur.
Temporary alternative measures: Clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, and use a spotter when extending the boom.
(ii) Lattice boom cranes.
(A) Lattice boom cranes manufactured after Feb 28, 1992, must be equipped with a device that either automatically prevents damage and load failure from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component), or warns the operator in time for the operator to prevent two-blocking. The device must prevent such damage/failure or provide adequate warning for all points where two-blocking could occur.
(B) Lattice boom cranes and derricks manufactured after November 8, 2011 must be equipped with a device which automatically prevents damage and load failure from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device(s) must prevent such damage/failure at all points where two-blocking could occur.
(C) Exception. The requirements in paragraphs (d)(3)(ii)(A) and (B) of this section do not apply to such lattice boom equipment when used for dragline, clamshell (grapple), magnet, drop ball, container handling, concrete bucket, marine operations that do not involve hoisting personnel, and pile driving work.
(D) Temporary alternative measures. Clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, or use a spotter.
(iii) Articulating cranes manufactured after December 31, 1999, that are equipped with a load hoist must be equipped with a device that automatically prevents damage from contact between the load block, overhaul ball, or similar component, and the boom tip (or fixed upper block or similar component). The device must prevent such damage at all points where two-blocking could occur. Temporary alternative measures: When two-blocking could only occur with movement of the load hoist, clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, or use a spotter. When two-blocking could occur without movement of the load hoist, clearly mark the cable (so that it can easily be seen by the operator) at a point that will give the operator sufficient time to stop the hoist to prevent two-blocking, and use a spotter when extending the boom.

## Slide 26
Questions?
Crane Inspections