## Slide 1
Personnel Competency
Oct. 2019 – Sep. 2020
Crane Management in Construction
AGC-OSHA Susan Harwood Training Grant

## Slide 2
Describe required employee training.
Describe crane operator qualifications/ certification requirements.
Describe signal person qualification requirements.
Describe rigger personnel qualification requirements.
Objectives
Personnel Competency

## Slide 3
All employees must be trained to work around crane operations.
Employers must evaluate employee’s understanding of their training.
OSHA requires training in/for:
    Overhead powerlines
    Signal persons
    Operators
    Competent persons and qualified persons
    Crush/pinch points
    Tag-out
1926.1430 Training Requirements
Personnel Competency
Notes:   Recognize other hazards such as swing radius, friction equipment, unintended equipment movement.
  Competent persons and qualified persons must be trained in their respective roles
  Refresher training as warranted
  Whenever required under this subpart, employer must provide training at no cost to employee.

## Slide 4
Managers and supervisors who plan and oversee crane operations must be knowledgeable in areas such as:
    Proper crane selection
    General site conditions such as ground conditions, power line issues, boom swing radius’s etc.
    Multi-crane operations
    Multi-employer crane operations
1926.1430 Training Requirements
Personnel Competency

## Slide 5
Crane Operators are required to be licensed or certified by an accredited agency.
The employer must ensure that the operator is also qualified to operate the equipment or is operating the equipment during a training period as an “Operator-in-Training”.
1926.1427(a) Operator Certification & Qualification
Personnel Competency
Notes: Paragraph (a) refers to the employer’s duty to assess the operator to ensure that an operator has the skills, knowledge, and ability to recognize and avert risks to operate equipment safely. The standard also includes requirements for the individual who performs the evaluation and requirements for documenting the evaluation.
Paragraph (a)(1) permits an employee to operate equipment as an “operator-in-training” prior to being certified and evaluated, provided that he or she is supervised and operates the equipment in accordance with the training requirements in paragraph (b). This is the only means by which an individual may operate equipment prior to being trained, certified, and evaluated as competent to do so.

## Slide 6
Assembly/Disassembly must be supervised by an A/D Director
That is person who meets the criteria for both a competent person and a qualified person, or by a competent person who is assisted by one or more qualified persons.
1926.1404 Assembly/Disassembly Director
Personnel Competency

## Slide 7
Inspector Qualifications
Personnel Competency

## Slide 8
The operator must:
Understand the crane’s functions and limitations and operating characteristics.
Be familiar with the operating manual & load chart.
Inspect and maintain the crane regularly.
Inform the Owner of any problems, needed maintenance or necessary repairs to the machine.
Operator Responsibilities
Personnel Competency

## Slide 9
Being aware of any site conditions, ground, the presence of power lines, etc.
Check that the site is adequately prepared for the crane.
Review the planned operation with the supervision.
Find out the load and rigging weight and determine where the load is to be placed.
Operator Responsibilities (Con’t)
Personnel Competency

## Slide 10
Maintain communication with signal persons.
Shut down and secure the machine properly when it is unattended.
Ensure that the accessible areas within the swing radius of the rear of the rotating superstructure of the crane are sufficiently barricaded.
Operator Responsibilities (Con’t)
Personnel Competency

## Slide 11
Certifications are by TYPE or TYPE & CAPACITY
Certifications must be based on a determination through:
    Through a written test that the individual knows the information necessary for safe operation of the specific type of equipment the individual will operate.
    A practical test operating specific types of equipment.
1926.1427(c) Crane Operator Certification/ Licensing
Personnel Competency
Notes: The current certification/licensing requirement, which is the centerpiece of the previous operator requirements, remains largely unchanged under the revised standard, with the exception that different certifications for different capacities of cranes would no longer be required. The reference to “certified/licensed” is intended to encompass each of the certification options in the standard (third-party certification or an audited employer certification program) as well as state or local operator licensing requirements.
Paragraph (c)(3) requires employers to provide at no cost to employees the certification or licensing required by § 1926.1427.
Note, however, that this provision does not mandate an employer to maintain its employment of an employee/operator who cannot pass certification testing or who is not a good operator candidate. Furthermore, an employee who does not possess a certification may still be allowed by the employer to operate a crane, but only as an operator-in-training and through the employer’s compliance with all requirements of the standard.
Paragraph (c)(2) provides two options for certification: compliance with paragraph (d) (third-party certification) or paragraph (e) (audited employer program). Compliance with the requirements of paragraph (d) is the option that OSHA expects the vast majority of employers to use.
OSHA considers testing organizations whose programs provide certifications that specify “type and capacity” equally acceptable.

## Slide 12
Written testing must include:
The controls and operational/performance characteristics.
Use of, and the ability to calculate (manually or with a calculator), load/capacity information on a variety of configurations of the equipment.
Procedures for preventing and responding to power line contact.
Technical knowledge of the specific type of equipment the individual will operate.
Technical knowledge applicable to the suitability of the supporting ground and surface to handle expected loads, site hazards, and site access.
Ability to read and locate relevant information in the equipment manual and other materials.
Areas of Written Testing for Certification
Personnel Competency

## Slide 13
A practical test must be conducted for each type of equipment to show that the individual has the skills necessary for safe operation of the equipment, including the following:
Ability to do a shift safety inspection.
Operational and maneuvering skills.
Application of load chart information.
Application of safe shut-down and securing procedures.
Areas of Practical Testing for Certification
Personnel Competency

## Slide 14
Certification Criteria
Personnel Competency
OPTION 1:
Accredited testing organization
OPTION 2:
Audited employer qualification program
OPTION 3:
Public entity license
OPTION 4:
U.S. military
Knowledge (Written Test)
  Controls/performance characteristics
  Calculate load chart capacity
  Preventing power line contact
  Ground support
  Read and locate info in operating manual
  Appendix C subjects
  1926.1430(c)(4)
Skills (Practical Test)
  Shift Inspection criteria
  Operational skills
  Application of load chart information
  Safe shut-down and securing procedures
1926.1427(c)

## Slide 15
The crane operator testing organization providing the certification must:
    Be accredited by a nationally recognized accrediting agency (NCCA and/or ANSI)
    Administer written and practical tests that assess the operator knowledge and skills.
    Provide certification based on equipment type, or type and capacity.
    A certification is valid for 5 years.
A certification is portable among employers who are required to have operators certified under this option.
1926.1427 (d) Accredited Agency Certification
Personnel Competency
Notes: First, the most significant change is that paragraph (d)(1)(ii)(B) replaces the references to certification by “type and capacity” that appeared in previous sub-paragraph (b)(1)(ii)(B) with “type, or type and capacity,” as recommended by ACCSH . The “type, or type and capacity” language has been included in the final rule to make clear that while all certifying bodies must certify by type of crane for their certifications to meet OSHA’s requirements, testing organizations may also choose to specify for their certifications different levels of rated lifting capacity of cranes

## Slide 16
National Commission for the Certification of Crane Operators (NCCCO)
National Center for Construction Education & Research (NCCER)
Crane Institute Certification – Only through December 2, 2019
Operating Engineers Certification Program (OECP)
Electrical Industry Certifications Association (EICA)
These certifications as of December 1, 2019
Current Accredited Agencies
Personnel Competency
Notes: December 2, 2019 - OSHA Issues Temporary Enforcement Policy for Crane Operator Certifications Issued by Crane Institute Certification (CIC)
OSHA requires crane operators engaged in construction activity to be certified by an entity accredited by a nationally recognized accrediting agency. CIC no longer holds such accreditation. To avoid industry confusion and potential disruptions of construction projects, OSHA has issued an enforcement policy for crane operator certifications issued by CIC.
The policy explains that, although CIC-issued certifications are not compliant with OSHA’s operator certification requirement, OSHA does not intend to cite employers for operating equipment that violates that requirement if their operators, in good faith, obtained CIC-issued certifications prior to December 2, 2019, with the belief the certifications met the standard’s requirements. Until further notice, OSHA will not accept CIC certifications – including re-certifications – issued on or after December 2, 2019.

## Slide 17
An employer's certification program of its employee must meet all of the requirements of an accredited agency’s program and approved by an auditor.
Written and practical tests developed by a national crane testing organization or approved by the auditor.
The auditor must be to certified to evaluate such tests and is NOT an employee of the employer.
A program certification is valid for 3 years.
Records of the program must be made available to OSHA
1926.1400(e) Audited Employer Program
Personnel Competency

## Slide 18
The operator’s certification is:
NOT portable and is only valid while working for that employer.
Valid for 5 years while under the employ of the employer
Operators must be retested.
1926.1400(e) Audited Employer Program (Con’t)
Personnel Competency
Notes: The record amply demonstrates the sufficiency of the accreditation process that must be passed for a testing organization to become accredited. That process is designed to ensure that accredited testing organizations use a sufficiently reliable process for certifying operators. The record also shows that such a mechanism is an effective one for determining operator competence.
Recertification establishes a standardized,
baseline knowledge of equipment operation for operators and indicates to an employer
that a certified operator has at least a certain knowledge of how to operate a crane.
Recertification helps to ensure that an operator does not lose this baseline knowledge over time. It also helps to ensure continuing education for certified operators so they are aware of any regulatory changes that impact their work. The agency believes there are some employers that would find it difficult to make sure their operators are up to date on changes to equipment and updates to regulations that affect their operation unless they had the ability to have their operators recertified. Therefore, OSHA is retaining the requirement for recertification as proposed.

## Slide 19
Where required, the equipment operator must be licensed by that government entity for operation of equipment within that entity's jurisdiction if that government licensing program meets the following requirements:
    The assessment must include written and practical tests regarding knowledge and skills listed for certification.
    The testing meets industry-recognized criteria for written testing materials, practical examinations, test administration, grading, facilities/equipment, and personnel.
1926.1427(c)(1) Public Entity Licensing
Personnel Competency
Notes: When a state or local government issues operator licenses for equipment covered under subpart CC, and that government licensing program meets the requirements specified in the standard, then employers must ensure that equipment operators are properly licensed when working in the state or local jurisdiction, even if the operator is also certified by a nationally accredited certification organization. However, the state or local license would satisfy OSHA’s certification requirement: OSHA will not require an operator who obtains such a state or local license to also obtain a separate certification from a nationally accredited certification organization or an employer-audited program.

## Slide 20
The government authority that oversees the licensing department/office has determined that the requirements of certification under OSHA have been met.
The licensing department/office has testing procedures for re-licensing designed to ensure that the operator continues to meet the technical knowledge and skills requirements.
A license is valid for the period of time stipulated by the licensing department/office, but no longer than 5 years.
1926.1427(c)(1) Public Entity Licensing (Con’t)
Personnel Competency

## Slide 21
An operator is considered qualified if he/she has a current operator qualification issued by the U.S. military for operation of the equipment while working for the U.S. Military. (Uniform and Civilian)
Certification is NOT portable
Qualification by the U.S. Military
Personnel Competency

## Slide 22
Tests for certification may be administered verbally, with answers given verbally, where the operator:
    Passes a written demonstration of literacy relevant to the work.
    Demonstrates the ability to use the type of written manufacturer procedures applicable to the class/type of equipment for which the candidate is seeking certification.
1926.1427(h)(1) Language and Literacy
Personnel Competency
Notes: The standard allowes operators to be certified in a language other than English, provided that the operator understands that language. The last sentence of paragraph (h)(2) has been reworded to clarify that an operator is permitted to operate equipment only when he or she is furnished materials that are necessary for safe operation of the equipment and required by subpart CC, such as operations manuals and load charts, in the language of the operator’s certification.
Paragraph (h) continues to allow “tests” in languages understood by the operator. In revised paragraph (h), “tests” encompasses both the certification test and the employer’s evaluation of the operator. Either or both may be in any language understood by the operator. The language of the operator’s manual or other furnished materials required by the standard would only need to match the language of the certification

## Slide 23
Tests may be administered in any language the operator understands.
The operator's certification documentation must note the language in which the test was given.
The operator is only permitted to operate equipment that is furnished with materials, such as operations manuals and load charts, that are written in the language of the certification.
1926.1427(h)(2) Language and Literacy
Personnel Competency

## Slide 24
The employer must assure each operator is trained on the safe operation of the equipment the operator will be using.
An employee who has not been certified/licensed, trained and evaluated by the employer may only operate the equipment under supervision as an “Operator-in-Training”.
1926.1427(b) Employer/Operator Training
Personnel Competency
Notes: An employee who is an experienced operator may need far less training than a less experienced employee. Employers must determine what level of practical and formal training an operator-in-training would need under paragraph (b) to ensure that they develop the skills, knowledge and ability to recognize and avoid risks necessary for safe crane operation in a variety of conditions. Ultimately, the training methods chosen by the employer must be effective and responsive to each operator’s training needs.
Even after the operator-in-training is determined competent by employer evaluation, the employer’s training duty can continue when the operator operates new equipment or performs tasks that require new skills or knowledge. An individual may be a fully certified and evaluated operator with respect to one piece of equipment such that he or she is allowed to operate that equipment independently, but simultaneously be an operator-in-training (and thus subject to the operating restrictions in the standard) with respect to different equipment or tasks that require significantly different skills or knowledge to ensure safety.

## Slide 25
The employer must provide each operator-in-training with sufficient training, through a combination of formal and practical instruction, to ensure that the operator-in-training develops the skills, knowledge, and judgment necessary to operate the equipment safely for the assigned work.
The employer must provide instruction on the knowledge and skills needed to operate the crane in its various configurations and as described under the Evaluation section.
The employer may only assign tasks within the operator-in-training's ability.
Operator-in-Training Training
Personnel Competency

## Slide 26
An operator-in-training shall not operate the equipment in any of the following circumstances unless certified in accordance with OSHA’s operator certification requirements:
If any part of the equipment, load line or load (including rigging and lifting accessories), if operated up to the equipment's maximum working radius in the work zone (see Sec. 1926.1408(a)(1)), could get within 20 feet of a power line that is up to 350 kV, or within 50 feet of a power line that is over 350 kV.
If the equipment is used to hoist personnel.
In multiple-equipment lifts.
If the equipment is used over a shaft, cofferdam, or in a tank farm.
In multiple-lift rigging operations, except where the operator's trainer determines that the operator-in-training skills are sufficient for this high-skill work.
1926.1427(b)(3) Operator-in-Training Restrictions
Personnel Competency
Notes: OSHA continues to agree with C-DAC that these lifts are too complex and potentially dangerous to be attempted by an operator candidate who may lack the basic knowledge and skills required for general crane operation. But the prior regulatory text left no way forward for even a certified
operator to gain the experience necessary to perform those functions safely, and did not leave room for an employer to have an operator evaluated on these tasks in accordance with revised § 1926.1427(f). This language change therefore respe

## Slide 27
While operating the equipment, the operator-in-training must be continuously monitored by an individual ("operator's trainer") who:
Is an employee or agent of the operator-in-training's employer.
Has the knowledge, training, and experience necessary to direct the operator-in-training on the equipment in use.
1926.1427(b)(4)(i)(B) Operator’s Trainer
Personnel Competency
Notes: Paragraph (b)(4)(i)(B) requires that the trainer must “have the knowledge, training, and experience necessary to direct the operator-in-training on the equipment in use.” This requirement is the same as the proposal but is different from the requirements of paragraph § 1926.1427(f)(3) of the 2010 crane standard, which required that a trainer either be a certified operator or have passed the written part of a certification test, and have familiarity with the equipment’s controls. This revision recognizes that some uncertified trainers may have the knowledge and experience to be competent to teach or monitor the equipment operations of an operator-in-training.

## Slide 28
This is a performance-based qualification.
Employers would determine the level of knowledge and experience that the trainer must possess based on the skill level of the operator-in-training and the nature of the activity performed.
The trainer's experience with the task and equipment used could be sufficient for experienced personnel to provide training even without being a certified operator.
Trainers are not required to be a certified crane operator or pass a written test.
1926.1427(b)(4)(i) Trainer Qualifications
Personnel Competency
Notes: Under the final rule, even after the basic crane knowledge and operating skills of operators have been confirmed through certification testing, employers must still determine through evaluation if operator training already provided is sufficient or if more is necessary, based on the complexity of equipment that will be used and activity that will be performed. Thus, requiring an individual to pass a written certification exam appears to be likewise insufficient as the sole criterion for confirming a trainer’s ability to monitor and train an operator-in-training.
Second, using certification as a required criterion for the trainer could exclude individuals from the role who have extensive operating experience and familiarity with the controls of the relevant equipment but do not possess a certification. Under the trainer requirements of the 2010 crane rule, an experienced but uncertified operator may have been required to be monitored by a less experienced but certified individual. In stark contrast, an uncertified person who has significant experience operating the particular equipment used during the training may have more insight into the function of its controls and the nuances of its operation than someone who is certified for that type of equipment but has never operated that particular equipment. Allowing only certified operators in these training roles is also inconsistent with the industry practice of pairing inexperienced operators with experienced trainers who monitor the safety and professional development of the inexperienced operator.
Third, passing a written certification test is not a definitive indicator of safe training practices in the industry and requiring certification of all trainers could significantly alter many previous work practices in the industry. Stakeholder feedback suggests that many different employees or agents of an employer successfully fulfill the role of a trainer but may not be certified.

## Slide 29
While monitoring the operator-in-training, the operator's trainer cannot perform any tasks that could detract from the trainer's ability to monitor the operator-in-training.
For equipment other than tower cranes: The operator's trainer and the operator-in-training must be in direct line of sight of each other and communicate verbally or by hand signals.
1926.1427(b)(4) Operator’s Trainer (Con’t)
Personnel Competency

## Slide 30
For tower cranes, the operator's trainer and the operator-in-training must be in direct communication with each other.
By radio or other direct communication device
Operator’s Trainer – Tower Crane
Personnel Competency

## Slide 31
The employer must ensure that an operator-in-training is continuously monitored by the qualified trainer when operating the equipment.
The only exceptions to Continuous Monitoring are for short breaks where all of the following are met:
    The break lasts no longer than 15 minutes and there is no more than one break per hour.
    Immediately prior to the break the operator's trainer informs the operator-in-training of the specific tasks that the operator-in-training is to perform and limitations to which he/she must adhere during the operator trainer's break.
    The specific tasks that the operator-in-training will perform during the operator trainer's break are within the operator-in-training's abilities.
1926.1427(b)(4)(i) Continuous Monitoring of Operators-in-Training
Personnel Competency

## Slide 32
The employer must provide refresher training in relevant topics for each operator when, based on the performance of the operator or an evaluation of the operator's knowledge, there is an indication that retraining is necessary.
Retraining & Re-evaluation
Personnel Competency
Notes: Paragraph (f)(7) requires the employer to re-evaluate an operator whenever the employer is required to retrain the operator under § 1926.1427(b)(5). Paragraph
1926.1427(b)(5) requires retraining if the operator’s performance or an evaluation of the operator’s knowledge indicate that retraining is necessary. OSHA intends this requirement to ensure that when an employer becomes aware that an operator is not competent in a necessary aspect of safe crane operation, the employer provides additional training to the operator and re-evaluates the operator. Re-evaluation is needed to ensure that the operator is competent in the area of the observed deficiency.
As discussed in the explanation for paragraph (b)(5), triggers for retraining under paragraph (b)(5) and re-evaluation under paragraph (f)(7) might include a wide variety of feedback, such as (but not limited to) information from an on-site supervisor or safety manager, contractor, or other person that the operator was operating equipment unsafely, OSHA citations, a crane near miss, or other incidents that indicate unsafe operation of the crane.24 The re-evaluation must target the deficiency in skills, knowledge, or ability to recognize and avert risk that triggered the retraining, but need not include a re-evaluation of other previously evaluated skills, knowledge, or ability.

## Slide 33
The employer must evaluate each operator to assure that the operator meets minimum requirements for determining operator competency to be qualified.
Qualification is valid only where the operator is employed by (and operating the equipment for) the employer that issued the qualification and is NOT portable.
Qualification is valid for the period of time stipulated by the employer.
1926.1427(f) Qualification/Evaluation
Personnel Competency

## Slide 34
The definition of “qualified” in section OSHA 29CFR 1926.32 does not apply to crane operator evaluation and qualification.
Possession of a certificate or degree cannot, by itself, cause a person to be qualified for crane operation.
An operator can be qualified by the employer if:
    The operator is fully trained in the operation of the equipment he/she will operate
    Is certified or licensed as described in Certification/Licensing
    Has been fully evaluated by the operator’s employer’s trainer on the equipment he/she will operate
Qualified Operator
Personnel Competency
Notes: OSHA proposed language for its similarity to language from ASME B30.5 and OSHA’s qualified person standard, and the flexibility it offers employers in choosing trainers for their crane operators. OSHA considered simply requiring a trainer to be a “qualified person,” but relying solely on the definition of qualified person as criteria for trainers presents a problem. In § 1926.1401, OSHA defines a qualified person as one “who, by possession of a recognized degree, certificate, or professional standing, or who by extensive knowledge, training and experience,successfully demonstrated the ability to solve/resolve problems relating to the subject matter, the work, or the project.” However, even under the previous standard OSHA did not intend for the possession of a certificate to be enough for an individual to be a trainer – the previous standard also required knowledge of the equipment’s controls. Relying on the definition of “qualified person” in the crane standard as the lone criteria for trainers would mean that anyone possessing a certificate would automatically be a “qualified person,” regardless of their knowledge of any of the controls or other aspects of the equipment to be operated.

## Slide 35
To qualify an operator an employer must ensure that each operator demonstrates the skills and knowledge necessary to operate the equipment safely as well as the ability to recognize and avert risk.
The evaluation must be conducted by a qualified evaluator.
Once the evaluation is completed successfully, the employer may allow the operator to operate other equipment that the employer can demonstrate does not require substantially different skills, knowledge, or ability to recognize and avert risk to operate.
Operator Evaluation
Personnel Competency
Notes: OSHA does not intend to require the additional evaluation of operators when it is not necessary, such as when there are minor differences between equipment models of the same type that do not necessitate substantially different skills, knowledge, or abilities to operate the crane safely.
In requiring that employers demonstrate that the different equipment does not require substantially different skills, knowledge, or ability to identify and avert risk, OSHA intends that the employer will be able to justify the basis for its determination.
An example of this justification could include an employer consulting an operator who has experience safely operating both pieces of equipment and could provide feedback about the differences in operation, or the employer could cite discussions with equipment manufacturers about the differences between models as justification for the basis of its determination. In response to the commenter, it is not likely that this change in capacity would require the employer to conduct an additional evaluation as long as the cranes are operated in similar configurations and other aspects of the crane (such as the computer operating systems, spatial arrangement of controls, control functions, safety devices, operational aides, mode of travel, and function of the equipment) are similar.
However, changes in the configuration such as the use of different attachments (e.g., wrecking ball versus a clamshell), significant changes in boom length, or the addition of counterweights are a few examples of differences that may require an additional evaluation. Similarly, design differences like the location and function of the controls (e.g., the boom hoist control is located where the line hoist control was located on the other equipment) may also require the operator to become familiarized with these changes

## Slide 36
Work Competency must be to be evaluated for crane type and set-up including:
    Use of Safety devices
    Use of Operational aids
    Use of software and understanding load charts
    Proper Shift inspections
1926.1427(j)1 & 2 Evaluation of the Operator
Personnel Competency
Notes: Ability to recognize, from visual and auditory observation, the items listed in § 1926.1412(d) (shift inspection).
Operational and maneuvering skills.
Application of load chart information.
Application of safe shut-down and securing procedures.

## Slide 37
Operators must be able to Evaluate Ground Conditions and proper crane stability including:
    Hidden Hazards
    Stable Ground
    Outrigger set-ups
    Use of Pads and Floats
    Use of Mats on Crawlers
Leveling of the Crane
Weather Conditions such as:
    Wind
    lightning
    Ice and snow build up
Evaluation of Operator (Con’t)
Personnel Competency

## Slide 38
Operators who will perform the following functions must also be evaluated in the ability to perform the hoisting activities required for the assigned work including, if applicable:
    Communications with Qualified Signalers
    Blind lifts
    Personnel hoisting
    Multi-crane lifts
    Multi-lifting for steel erection
    Floating crane and cranes on barges
Operator Evaluation (Con’t)
Personnel Competency
Notes: the determination whether a new evaluation is needed turns on whether the safe operation of the new crane requires additional skills, knowledge, or ability to recognize and avert risk. For example, an employer may evaluate an operator and determine that he or she has demonstrated the ability to safely operate a large crane in a relatively complex configuration. If the employer determines that the operator has the skills, knowledge, and ability to identify and avert risk necessary to safely operate a smaller crane of the same type and operating system, in a simpler configuration with a shorter boom, then the operator would not need to be re-evaluated (assuming that the tasks are similar). Similarly, a new evaluation may not be necessary for an operator to operate a larger crane for the same task. Where the two cranes are configured similarly, and they have similar controls (including computer operating systems, spatial arrangement of controls, and control functions), safety devices, operational aides, mode of travel, and overall function, such that significant new skills, knowledge, and ability to identify and avert risk are not necessary to operate the cane safely, then a new evaluation would not be required.

## Slide 39
Evaluations are specific to the operators, equipment, and tasks, but are not dependent on location.
However, if assigned work at multiple locations requires an operator to have substantially different skills, knowledge, or ability to recognize and avert risk, then an employer must perform an evaluation of the operator to ensure he or she can perform the assigned work.
Crane Relocation
Personnel Competency
Notes: Evaluations are specific to the operators, equipment, and tasks, but are not dependent on location.
However, if assigned work at multiple locations requires an operator to have substantially different skills, knowledge, or ability to recognize and avert risk, then an employer must perform an evaluation of the operator to ensure he or she can perform the assigned work.

## Slide 40
The evaluation must be conducted by an individual who has the knowledge, training, and experience necessary to assess equipment operators.
The evaluator must be an employee or agent of the employer.
Employers that assign evaluations to an outside agent retain the duty to ensure that the requirements for qualification are satisfied.
An Evaluator does not need to be a certified operator.
The Trainer can also be identified as the Evaluator.
1926.1427(f)(5) Evaluator
Personnel Competency
Notes: Paragraph (f)(4) establishes minimum criteria for the person who performs the required evaluation of an operator-in-training. The evaluation must be conducted by an individual who possesses the knowledge, training, and experience necessary to assess operators. This standard affords some flexibility to employers as they seek to ensure operator safety. An evaluator could be, for example, a current or former operator who is also trained to assess equipment operators. The key, however, much like the criteria for the person performing training and evaluation of operators under the powered industrial truck operator training standard (§ 1910.178(1)(2)(iii)), is that the evaluator possess the requisite knowledge, training, and experience for assessing an operator’s knowledge, skill, and ability to recognize and avert risk. Such knowledge, training, and experience is not necessarily the same as the knowledge, training, and experience to perform the particular construction operations or processes oneself.
OSHA is not requiring that evaluators must be certified or have previous experience as an operator. While experience as an operator and certification might be
helpful, C-DAC did not recommend either for trainers and OSHA is not requiring it in the final rule because it does not think it is necessary to hold evaluators to a higher standard than C-DAC recommended for trainers. As stated in the NPRM, OSHA heard from stakeholders who have successfully involved a variety of personnel in the evaluation of operators, including riggers, maintenance personnel, signal personnel, tradesmen, managers, and foremen who have demonstrated the necessary experience to conduct this assessment. These personnel are typically not certified to operate cranes . Based on the record, OSHA does not wish to
prevent these kinds of personnel from performing effective evaluations.
If OSHA prohibited trainers from also serving as evaluators, employers would be bound to a process in which a formal evaluation would take place only after the completion of training. While that model is acceptable under the standard, OSHA also intends to allow employers to maintain more flexible models in which operators may be allowed to try new equipment, configurations,or tasks under the guidance of a trainer as the opportunities present themselves at the worksite. If the trainer also meets the requirements of an evaluator, that person would be able to determine when the trainee has demonstrated sufficient skill, knowledge, and ability for particular equipment or tasks. The trainer/evaluator could evaluate and document the trainee’s success and move on to other areas of training. This model may be particularly useful in scenarios where an operator is expected to operate many
different pieces of equipment for many different tasks, using different configurations or attachments, when there are significant differences that would require additional skills,knowledge, or ability. A trainer also serving as an evaluator would be able to evaluate the operator as the operator gains experience with those different tasks, configurations, and equipment differences; it could save significant time and effort that would otherwise be required to replicate all of those scenarios later in front of a different evaluator.
Finally, by allowing a trainer to also evaluate the operator in actual work settings
engaged in tasks that the operator will be expected to perform, the evaluations might
actually provide a more realistic gauge of the operator’s skills, knowledge, and ability
than in a more sterile evaluation setting. For all of those reasons, OSHA is not
prohibiting an operator’s trainer from also serving as that operator’s evaluator.

## Slide 41
If an employer rents a crane from a crane rental company and that company provides the operator – The employer of the operator is the crane rental company and they are responsible to evaluate and qualify the operator.
If the employer rents a crane from a crane rental company but supplies their own operator (Bare Rental) – The employer is responsible to evaluate and qualify the operator.
Rental Cranes
Personnel Competency
Notes: There are at least two methods of compliance in that scenario. First, that contractor could select a firm that offers the crane along with a qualified operator who has been certified and evaluated by that firm. In that scenario the crane firm would be operator’s employer and have the responsibility to ensure that the operator is certified and evaluated.
A “bare rental” company that rents cranes will be responsible for signing off on the operator’s document of evaluation. In that scenario, the crane rental company is not the employer of the operator and will not be on site or otherwise be controlling the operator. OSHA’s standard does not require that crane rental company to ensure that the operator of its crane is certified or evaluated. That would be the responsibility of the employer of the operator.

## Slide 42
The employer must document the evaluation.
This document must provide:
Operator's name;
Evaluator's name and signature;
Date;
Make, model, and configuration of equipment used in the evaluation.
The employer must make the document available at the worksite.
19261427(f) Operator Evaluation Documentation
Personnel Competency
Notes: Paragraph (f)(6) requires the employer to document the evaluation of each operator and to ensure that the documentation is available at the worksite. OSHA, by requiring this documentation to be available at the worksite in the NPRM, implied that the documentation must be maintained by the employer for the duration of the operator’s employment. OSHA is adding language to this final rule that states explicitly the documentation must be maintained while the operator is employed by the employer.
The documentation under 1926.1427(f)(6) must include: the operator’s name, the evaluator’s name, the date of the evaluation, and the make, model, and configuration of the equipment on which the operator was evaluated. But the documentation would not need to be in any particular format.
The documentation requirement will ensure accountability and direct the employer’s attention to the critical aspects of operating the assigned equipment that must be considered during the evaluation. The documentation of the evaluation will record key baseline information that an employer can use to help make subsequent determinations about whether the operator is competent to operate particular equipment on future projects. It will also provide a quick reference for site supervisors, lift directors, and any employee, such as a hoist crew member, whose safety is affected by crane operations.
Rather, employers would have the flexibility to capture this information using their own existing systems or create documentation that best meets the needs of their workplace. For example, employers could issue operator cards that include this information, keep records electronically in a database accessible at the worksite, develop logs for each piece of equipment, or use any other method that memorializes the mandatory information.
As previously discussed, paragraph (f) permits the employer to evaluate the operator on one crane and then make a determination that the operator is also competent to safely run other equipment that requires the same level of operating skills, crane knowledge, and ability to recognize and avert risk. This provision allows employers to document these determinations collectively. For example, if an employer with five cranes, possibly configured in slightly different ways, determines that an operator’s evaluation on Crane #2 also demonstrates the operator’s competency with respect to the other four cranes, the employer could use a single document to record the operator’s competence to operate all five cranes. In fact, the documentation for the original evaluation could simply be amended to state that it is also applicable to identified equipment that does not require substantially different skills, knowledge, or abilities.

## Slide 43
A signal person must be provided in each of the following situations:
    The point of operation, meaning the load travel or the area near or at load placement, is not in full view of the operator.
    When the equipment is traveling, the view in the direction of travel is obstructed.
    Due to site specific safety concerns, either the operator or the person handling the load determines that it is necessary.
1926.1419 Crane Signaling
Personnel Competency

## Slide 44
Each signal person must:
Know and understand the type of signals used.
Be competent in the application of the type of signals used.
Have a basic understanding of equipment operation and limitations, including the crane dynamics involved in swinging and stopping loads and boom deflection from hoisting loads.
1926.1428(c) Signaler Qualification Requirements
Personnel Competency

## Slide 45
The employer shall ensure that each signal person meets the Qualification Requirements by using either:
Third party qualified evaluator. (Portable)
Employer’s qualified evaluator. (Not Portable)
1926.1428 Signal Person Qualifications
Personnel Competency
Images courtesy TEEX. Used with permission.
Notes: Graphics: TEEX

## Slide 46
The operator, signal person and lift director (if there is one), must communicate the voice signals that will be used.
Each voice signal must contain the following three elements, given in the following order:
    function (such as hoist, boom, etc.),
    direction; distance and/or speed; function,
    stop command.
The operator, signal person and lift director (if there is one), must be able to effectively communicate in the language used
1926.1421 Voice Signal Requirements
Personnel Competency

## Slide 47
The employer must make documentation of signal person’s qualification available at the site.
The documentation must specify each type of signaling (e.g., hand signals, radio signals, etc.) for which the signal person is qualified.
Signal Person Documentation
Personnel Competency

## Slide 48
When Required
During Hoisting Activities While Assembling or Disassembling a Crane or Derrick (Subpart CC)
During Steel Erection Operations (Subpart R)
Best Practices:
    Hooking, unhooking, guiding the load or
    In the initial connection of a load to a component or structure and are within the fall zone.
ALL THE TIME!
Qualified Riggers
Personnel Competency
Notes: Not particularly specified in OSHA requirements, let’s call it “best practices”.
Remind students that fall zone means “the area (including but not limited to the area directly beneath the load) in which it is reasonably foreseeable that partially or completely suspended materials could fall in the event of an accident.”

## Slide 49
Qualified Riggers must:
Know and understand the requirements of applicable ASME standards (such as B30.9, Slings and B30.26, Rigging Hardware)
Know and understand the type of sling and hitches used including removal criteria for rigging gear
Basic understanding of the applicable slings, rigging hardware, winch, below-the-hook lifting devices and their limitations
Know and understand rigging related conditions, such as load weight estimation, center of gravity, effect of angles on rigging components and basic hand signals, as applicable.
Qualified Riggers (Con’t)
Personnel Competency

## Slide 50
Be competent in the application of the type of hitches used
Qualified Riggers (Con’t)
Personnel Competency
Image courtesy TEEX. Used with permission.
Notes: Image: TEEX

## Slide 51
Questions?
Personnel Competency