## Slide 1
Crane Management
Oct. 2019 – Sep. 2020
Crane Management in Construction
AGC-OSHA Susan Harwood Training Grant

## Slide 2
Understanding loads, charts and critical lifts.
Suspended loads, use of open hooks and stopping operations.
Understanding Fall protection
Identify supplemental requirements for hoisting personnel.
Recognize planning requirements for multi-crane lifts.
Recognize supplemental requirements for tower cranes.
Discuss requirements for floating cranes on barges.
Recognize requirements for pile drivers.
Objectives
Crane Management

## Slide 3
The procedures applicable to the operation of the equipment, including rated capacities (load charts), recommended operating speeds, special hazard warnings, instructions, and operator’s manual, shall be readily available in the cab at all times for use by the operator.
1926.1417(c) Manuals and Charts
Crane Management
This means that the load charts and manuals must be in the crane!

## Slide 4
Determine load weight
Determine work radius
Determine boom angle
Determine boom length
Determine crane capacity
Safe Load Planning
Crane Management

## Slide 5
The operator shall verify that the load is within the rated capacity of the equipment by at least one of the following methods:
    The weight of the load shall be determined from a reliable source, by a reliable calculation method, or by other equally reliable means, or
    The operator can begin hoisting the load to determine, using an electronic load weighing device. If it exceeds 75 percent of the maximum rated capacity at the longest radius that will be used during the lift operation, the operator must STOP until load weight is determined.
1926.1417(o)(3) Load weight
Crane Management

## Slide 6
Operator responsible for weight before picking load
Management responsible for providing information (weight)
Verifying Load Weight
Crane Management
Notes: A crane operator is responsible for knowing the load weight before he picks it up. It is management's responsibility to give it to him, but this does not forgive an operator for picking a load he does not know the weight of.
Sometimes the weight may be hard to determine. Work hard to determine weights accurately. There are many sources to help you determine the weight.
Photo - TCS

## Slide 7
Lifting Capacity vs. Radius
Crane Management
Lift Diagrams and Load Charts are necessary to determine how much load weight the crane can handle at a specific radius and boom angle.
Notes: LIFT RANGE - Just as important as lift capacity is lift range. For that, a range diagram is usually included in every chart which illustrates how much boom length is needed to pick up and lift a load both at a distance and at height.
EXAMPLE: You need to pick up a load at 25 feet and lift it to the top of a five-story, 65-foot building. Consulting the range diagram, 69 feet of boom is required to make the lift.

## Slide 8
The operator must be able to show the he/she can properly plan for and execute a critical lift:
The load exceeds 85% of the capacity.
Complications as a result of load configuration, clearance, danger to personnel power transmission equipment, or critical service process equipment.
The weight of the load is 25 tons or greater and exceeds 50’ in length, height, and width.
Lifts involve more than one crane to handle the load.
Critical Lifts
Crane Management

## Slide 9
Precautions For Using Tag Lines
    Provide proper training
    Never wrap around body or hand
    Never drag across site unattended
Tag Lines
Crane Management
Notes: Tag lines can be very helpful during a lift. They can be a hazard to people handling the lines. Each person handling a line should be trained on how to do the job safely and properly.
Never allow people to wrap the line around their body and have sufficient people on each line to provide the required pull.
Do not allow tag lines to drag across the jobsite or structure unattended.
Photo - TCS

## Slide 10
The operator shall not engage in any practice that diverts his/her attention while actually engaged in operating the crane, such as the use of cell phones (other than when used for signal communications) or other attention-diverting activities.
1926.1417(d) Distractions
Crane Management
Notes: Electronics (iPad, tablets, video games, TVs) are not good
What about fatigue? Coast Guard has a fatigue management program.

## Slide 11
The operator shall not leave the controls while the load is suspended, except where the following are met:
The operator remains adjacent to the equipment and is not engaged in any other duties.
The load is to be held suspended for a period of time exceeding normal lifting operations.
The competent person determines that it is safe to do so and implements measures necessary to restrain the boom hoist and telescoping, load, swing, and outrigger functions.
Barricades or caution lines, and notices, are erected to prevent all employees from entering the fall zone.
1926.1417(e)(1) Leaving the Equipment Unattended
Crane Management

## Slide 12
The provisions do not apply to working gear (such as slings, spreader bars, ladders, and welding machines) where the weight of the working gear is negligible relative to the lifting capacity of the equipment as positioned, and the working gear is suspended over an area other than an entrance or exit.
1417(e)(2) Suspending Loads
Crane Management

## Slide 13
Hoisting routes should not be over other employees to the extent consistent with public safety.
No employee shall be under a stationary suspended load except when:
    Engaged in hooking, unhooking or guiding a load, or
    Engaged in the initial attachment of the load to a component or structure, or
    Operating a concrete hopper or concrete bucket.
1926.1425 Keeping clear of the load
Crane Management

## Slide 14
Whenever there is a concern as to safety, the operator shall have the authority to stop and refuse to handle loads until a qualified person has determined that safety has been assured.
1926.1418 Authority to Stop Operation
Crane Management
Image courtesy AGC. Used with permission.
Notes: If operations not stopped, operator license can be suspended/revoked.
Image: AGC

## Slide 15
Hooks with self-closing latches or their equivalent shall be used.
Exceptions:
    Open hooks are allowed to set steel purlins and bar joists in accordance with subpart R
    “J” hooks are permitted to be used for setting wooden trusses.
    THESE ARE THE ONLY EXCEPTIONS
Use of Open Hooks
Crane Management

## Slide 16
Fall protection must be provided on a walking/working surface with an unprotected side or edge 6 feet above a lower level.
When moving point to point workers assembling crane parts must comply as follows:
    At 6 feet on non-lattice booms (whether horizontal or not horizontal).
    At 6 feet on lattice booms that are not horizontal.
    At 15 feet on horizontal lattice booms.
1926.1423(e) Fall Protection (Non Assembly/Disassembly)
Crane Management
Notes: 1926.1423 Fall protection.
(a) Application.
(1) Paragraphs (b), (c)(3), (e) and (f) of this section apply to all equipment covered by this subpart except tower cranes.
(2) Paragraphs (c)(1), (c)(2), (d), (g), (j) and (k) of this section apply to all equipment covered by this subpart.
(3) Paragraphs (c)(4) and (h) of this section apply only to tower cranes.
(b) Boom walkways.
(1) Equipment manufactured after November 8, 2011 with lattice booms must be equipped with walkways on the boom(s) if the vertical profile of the boom (from cord centerline to cord centerline) is 6 or more feet.
(2) Boom walkway criteria.
(i) The walkways must be at least 12 inches wide.
(ii) Guardrails, railings and other permanent fall protection attachments along walkways are:
(A) Not required.
(B) Prohibited on booms supported by pendant ropes or bars if the guardrails/railings/attachments could be snagged by the ropes or bars.
(C) Prohibited if of the removable type (designed to be installed and removed each time the boom is assembled/disassembled).
(D) Where not prohibited, guardrails or railings may be of any height up to, but not more than, 45 inches.
(c) Steps, handholds, ladders, grabrails, guardrails and railings.
(1) Section 1926.502(b) does not apply to equipment covered by this subpart.
(2) The employer must maintain in good condition originally-equipped steps, handholds, ladders and guardrails/railings/grabrails.
(3) Equipment manufactured after November 8, 2011 must be equipped so as to provide safe access and egress between the ground and the operator work station(s), including the forward and rear positions, by the provision of devices such as steps, handholds, ladders, and guardrails/railings/grabrails. These devices must meet the following criteria:
(i) Steps, handholds, ladders and guardrails/railings/grabrails must meet the criteria of SAE J185 (May 2003) (incorporated by reference, see§ 1926.6) or ISO 11660-2:1994(E) (incorporated by reference, see§ 1926.6) except where infeasible.
(ii) Walking/stepping surfaces, except for crawler treads, must have slip-resistant features/properties (such as diamond plate metal, strategically placed grip tape, expanded metal, or slip-resistant paint).
(4) Tower cranes manufactured after November 8, 2011 must be equipped so as to provide safe access and egress between the ground and the cab, machinery platforms, and tower (mast), by the provision of devices such as steps, handholds, ladders, and guardrails/railings/grabrails. These devices must meet the following criteria:
(i) Steps, handholds, ladders, and guardrails/railings/grabrails must meet the criteria of ISO 11660-1:2008(E) (incorporated by reference, see§ 1926.6) and ISO 11660-3:2008(E) (incorporated by reference, see§ 1926.6) or SAE J185 (May 2003) (incorporated by reference, see§ 1926.6) except where infeasible.
(ii) Walking/stepping surfaces must have slip-resistant features/properties (such as diamond plate metal, strategically placed grip tape, expanded metal, or slip-resistant paint).
(d) Personal fall arrest and fall restraint systems. Personal fall arrest system components must be used in personal fall arrest and fall restraint systems and must conform to the criteria in § 1926.502(d) except that § 1926.502(d)(15) does not apply to components used in personal fall arrest and fall restraint systems. Either body belts or body harnesses must be used in personal fall arrest and fall restraint systems.
(e) For non-assembly/disassembly work, the employer must provide and ensure the use of fall protection equipment for employees who are on a walking/working surface with an unprotected side or edge more than 6 feet above a lower level as follows:
(1) When moving point-to-point:
(i) On non-lattice booms (whether horizontal or not horizontal).
(ii) On lattice booms that are not horizontal.
(iii) On horizontal lattice booms where the fall distance is 15 feet or more.
(2) While at a work station on any part of the equipment (including the boom, of any type), except when the employee is at or near draw-works (when the equipment is running), in the cab, or on the deck.
(f) For assembly/disassembly work, the employer must provide and ensure the use of fall protection equipment for employees who are on a walking/working surface with an unprotected side or edge more than 15 feet above a lower level, except when the employee is at or near draw-works (when the equipment is running), in the cab, or on the deck.
(g) Anchorage criteria.
(1) Sections 1926.502(d)(15) and 1926.502(e)(2) apply to equipment covered by this subpart only to the extent delineated in paragraph (g)(2) of this section.
(2) Anchorages for personal fall arrest and positioning device systems.
(i) Personal fall arrest systems must be anchored to any apparently substantial part of the equipment unless a competent person, from a visual inspection, without an engineering analysis, would conclude that the criteria in § 1926.502(d)(15) would not be met.
(ii) Positioning device systems must be anchored to any apparently substantial part of the equipment unless a competent person, from a visual inspection, without an engineering analysis, would conclude that the criteria in § 1926.502(e)(2) would not be met.
(iii) Attachable anchor devices (portable anchor devices that are attached to the equipment) must meet the anchorage criteria in § 1926.502(d)(15) for personal fall arrest systems and § 1926.502(e)(2) for positioning device systems.
(3) Anchorages for fall restraint systems. Fall restraint systems must be anchored to any part of the equipment that is capable of withstanding twice the maximum load that an employee may impose on it during reasonably anticipated conditions of use.
(h) Tower cranes.
(1) For work other than erecting, climbing, and dismantling, the employer must provide and ensure the use of fall protection equipment for employees who are on a walking/working surface with an unprotected side or edge more than 6 feet above a lower level, except when the employee is at or near draw-works (when the equipment is running), in the cab, or on the deck.
(2) For erecting, climbing, and dismantling work, the employer must provide and ensure the use of fall protection equipment for employees who are on a walking/working surface with an unprotected side or edge more than 15 feet above a lower level.
(i) [Reserved.]
(j) Anchoring to the load line. A personal fall arrest system is permitted to be anchored to the crane/derrick's hook (or other part of the load line) where all of the following requirements are met:
(1) A qualified person has determined that the set-up and rated capacity of the crane/derrick (including the hook, load line and rigging) meets or exceeds the requirements in § 1926.502(d)(15).
(2) The equipment operator must be at the work site and informed that the equipment is being used for this purpose.
(3) No load is suspended from the load line when the personal fall arrest system is anchored to the crane/derrick's hook (or other part of the load line).
(k) Training. The employer must train each employee who may be exposed to fall hazards while on, or hoisted by, equipment covered by this subpart on all of the following:
(1) the requirements in this subpart that address fall protection.
(2) the applicable requirements in §§ 1926.500 and 1926.502.

## Slide 17
Fall protection required on a walking/working surface with an unprotected side or edge more than 15 feet above a lower level, except when the employee is at or near draw-works (when the equipment is running), in the cab, or on the deck.
1926.1423(f) Fall Protection (Assembly / disassembly work)
Crane Management

## Slide 18
The use of equipment to hoist employees is prohibited except where the employer demonstrates that the erection, use, and dismantling of conventional means of reaching the worksite, is not possible because of the project’s structural design or worksite conditions.
This paragraph does not apply to work covered by subpart R (Steel Erection).
1926.1431 Hoisting Personnel
Crane Management
Image courtesy TEEX. Used with permission
Notes:   Image: TEEX

## Slide 19
Hoisting Personnel
Crane Management
Decision to Hoist Personnel
Use of Personnel Platform
Equipment Set-Up
Equipment Criteria
Personnel Platform Criteria
Personnel Platform Loading
Attachment and Rigging
Trial Lift and Inspection
Proof Testing
Work Practices
Environmental Conditions
Fall Protection
Special Situations
Notes: REMEMBER!
Personnel hoisting is permitted only when there is no feasible way for personnel to access the work!
‘Trial Lifts’ are different than ‘Proof Testing’
– Facilitate a short discussion on the differences between the two

## Slide 20
Before beginning a crane/derrick operation in which more than one crane/derrick will be supporting the load, the operation must be planned.
1926.1432 Multiple-Crane/Derrick Lifts
Crane Management
Image courtesy TEEX. Used with permission
Notes: Requirements for Plan:
Developed by qualified person
Ensure requirements of this subpart are met
Where QP determined that engineering expertise is needed, employer must provide
Plan Implementation
Directed by person who meets criteria for competent and qualified person or by competent person assisted by qualified person
Lift director must review plan with all workers involved
Image: TEEX

## Slide 21
Lift Plan
    The plan must be developed by a qualified person.
    The plan must be designed to ensure that the requirements of this subpart are met.
    Lift director required
    Where the qualified person determines that engineering expertise is needed for the planning, the employer must ensure that it is provided.
MULTI-CRANE LIFTS
Crane Management
Notes: Before beginning a crane/derrick operation in which more than one crane/derrick will be supporting the load, the operation must be planned
REMEMBER: You cannot stress the importance of documentation enough!

## Slide 22
Plan Implementation
    The multiple-crane/derrick lift must be directed by a person who meets the criteria for both a competent person and a qualified person, or by a competent person who is assisted by one or more qualified persons (lift director).
    The lift director must review the plan in a meeting with all workers who will be involved with the operation.
MULTI-CRANE LIFTS
Crane Management
Notes: Before beginning a crane/derrick operation in which more than one crane/derrick will be supporting the load, the operation must be planned
REMEMBER: If multiple cranes are using multiple signal persons – the communications protocols can be confusing. Make sure that this is addressed so that each crane operator is taking signals from their designated signal person.

## Slide 23
This section contains supplemental requirements for tower cranes; all sections of this subpart apply to tower cranes unless specified otherwise.
1926.1435 Tower Cranes
Crane Management
Image courtesy Bob Emmrich. Used with permission.
Notes: Image: Bob Emmerich

## Slide 24
Foundations and structural supports
    Design and Inspection
    Designed by manufacturer or
Plumb tolerance
    Specification followed
    Verified by qualified person
Foundation Requirements for Tower Cranes
Crane Management
Image courtesy of Jim Goss. Used with permission.
Notes: Image: Jim Goss

## Slide 25
Pre- and Post-erection inspection
    By qualified person
    Post-erection load test
Required inspections
    Pre – Erection
    Post – Erection
    Monthly
    Annual
Requirements for Tower Cranes
Crane Management
Image courtesy of OSHA. Used with permission.
Notes: Image: OSHA
Review the requirements of the prescribed inspections for Tower Cranes and identify those as part of the general 1926.1400 standard, and those specific to Tower Cranes.

## Slide 26
There are supplemental requirements for floating cranes/derricks and land cranes/derricks on barges.
Coast Guard and Corps of Engineers requirements may apply
1926.1437 Floating cranes/derricks and
land cranes/derricks on barges
Crane Management

## Slide 27
A qualified person (floating cranes/derricks) is a qualified person whose expertise is with the respect to vessel/floatation devices.
Floating Cranes on Barges
Crane Management
Notes: Image: Jim Goss
Inspections required by § 1926.1437(h) ensure the safety of the means of attachment and flotation for floating cranes/derricks or land cranes/derricks on barges or other means of flotation.
Inspection requirements of § 1926.1437(h) are supplemental to those of § 1926.1412, which ensure the safety of the crane/derrick and the hoisting activity performed.

## Slide 28
List and trim requirements
Restraint requirements
  4 Options
    Physical attachment
    Corralling
    Crane on rails
    Centerline cable system
Land Cranes on Barges
Crane Management
Notes: Image: OSHA

## Slide 29
Section 1926.1416(d)(3) (anti two-block device) does not apply.
Section 1926.1416(e)(4) (Load weight/capacity devices) applies only to dedicated pile drivers manufactured more than one year after the effective date of this standard.
Operator qualification and certification applies, and shall be for operation of either dedicated pile drivers or equipment that is the most similar to.
1926.1439 Dedicated Pile Drivers
Crane Management

## Slide 30
The provisions of subpart CC apply to dedicated pile drivers, except as specified in this section.
Anti two-blocking device does not apply.
Design, construction and testing requirements apply to dedicated pile drivers
Dedicated Pile Drivers
Crane Management
Notes: Explain the definition of a “Dedicated Pile Driver”, as all participants may not be familiar with all types of cranes, or multi-purpose machine configurations.

## Slide 31
Questions?
Crane Management